Satellite Mission Index (alphabetically ordered)

ACRIMSAT (Active Cavity Radiometer Irradiance Monitor) NASA	15

ADM-Aeolus (Atmospheric Dynamics Mission (Earth Explorer Core Mission)) ESA	15

ALOS (Advanced Land Observing Satellite) JAXA	15

Aqua (Aqua (formerly EOS PM-1)) NASA	15

Aura (Aura (formerly EOS Chemistry)) NASA	16

Baumanets  ROSKOSMOS	16

BelKA  ROSKOSMOS	16

BIRD (Bi-spectral Infrared Detection) DLR	16

BISSAT ((Bistatic SAR mission)) ASI	17

CALIPSO (Cloud-Aerosol Lidar and Infrared Pathfinder Satellite Observations) NASA	17

CARTOSAT-1 (Indian Remote Sensing Satellite - P5) ISRO	17

CARTOSAT-2  ISRO	17

CBERS-2 (China Brazil Earth Resources Satellite - 2) CAST	18

CBERS-2B (China Brazil Earth Resources Satellite - 2B) CAST	18

CBERS-3 (China Brazil Earth Resources Satellite - 3) CAST	18

CBERS-4 (China Brazil Earth Resources Satellite - 4) CAST	18

CHAMP (Challenging Mini-Satellite Payload for Geophysical Research and Application) DLR	19

CloudSat (CloudSat) NASA	19

COSMO - SkyMed (COnstellation of small Satellites for Mediterranean basin Observation) ASI	19

CRYOSAT (CryoSat (Earth Explorer Opportunity Mission)) ESA	19

DEMETER (Detection of Electro-Magnetic Emissions Transmitted from Earthquake Regions) CNES	20

Diademe 1&2  CNES	20

DMSP F-13 (Defense Meteorological Satellite Program F-13) NOAA	20

DMSP F-15 (Defense Meteorological Satellite Program F-15) NOAA	20

DMSP F-16 (Defense Meteorological Satellite Program F-16) NOAA	21

DMSP F-17 (Defense Meteorological Satellite Program F-17) NOAA	21

DMSP F-18 (Defense Meteorological Satellite Program F-18) NOAA	21

DMSP F-19 (Defense Meteorological Satellite Program F-19) NOAA	21

DMSP F-20 (Defense Meteorological Satellite Program F-20) NOAA	22

DSCOVR (DSCOVR (formerly Triana)) NASA	22

Elektro-L (Geostationary Operational Meteorological Satellite - 2) ROSHYDROMET	22

Envisat (Environmental Satellite) ESA	22

ERBS (Earth Radiation Budget Satellite) NASA	23

ERS-2 (European Remote Sensing satellite - 2) ESA	23

ESA Future Missions (ESA Future Missions) ESA	23

FedSat (Federation Satellite) CSIRO	23

FY-2C (FY-2C Geostationary Meteorological Satellite) NRSCC	24

FY-2D (FY-2D Geostationary Meteorological Satellite) NRSCC	24

FY-2E (FY-2E Geostationary Meteorological Satellite) NRSCC	24

FY-3A (FY-3A Polar-orbiting Meteorological Satellite) NRSCC	24

FY-3B (FY-3B Polar-orbiting Meteorological Satellite) NRSCC	25

FY-3C (FY-3C Polar-orbiting Meteorological Satellite) NRSCC	25

FY-3D (FY-3D Polar-orbiting Meteorological Satellite) NRSCC	25

FY-3E (FY-3E Polar-orbiting Meteorological Satellite) NRSCC	25

FY-3F (FY-3F Polar-orbiting Meteorological Satellite) NRSCC	26

FY-3G (FY-3G Polar-orbiting Meteorological Satellite) NRSCC	26

GCOM-C (Global Climate Observation Mission-C) JAXA	26

GCOM-W (Global Climate Observation Mission-W) JAXA	26

Glory (Glory) NASA	27

GMS-5 (Geostationary Meteorogical Satellite - 5) JAXA	27

GOCE (Gravity Field and Steady-State Ocean Circulation Explorer (Earth Explorer Core Mission)) ESA	27

GOES-9 (Geostationary Operational Environmental Satellite - 9) NOAA	27

GOES-10 (Geostationary Operational Environmental Satellite - 10) NOAA	28

GOES-11 (Geostationary Operational Environmental Satellite - 11) NOAA	28

GOES-12 (Geostationary Operational Environmental Satellite - 12) NOAA	28

GOES-N (Geostationary Operational Environmental Satellite - N) NOAA	28

GOES-O (Geostationary Operational Environmental Satellite - O) NOAA	29

GOES-P (Geostationary Operational Environmental Satellite - P) NOAA	29

GOES-R (Geostationary Operational Environmental Satellite - R) NOAA	29

GOSAT (Greenhouse gases Observing Satellite) JAXA	29

GPM Constellation (Global Precipitation Measurement Mission Constellation spacecraft) NASA	30

GPM Core (Global Precipitation Measurement Mission Core spacecraft) NASA	30

GRACE (Gravity Recovery and Climate Experiment) NASA	30

HJ-1A (Disaster and Environment Monitoring and Forecast Small Satellite A) CAST	30

HJ-1B (Disaster and Environment Monitoring and Forecast Small Satellite B) CAST	31

HJ-1C (Disaster and Environment Monitoring and Forecast Small Satellite B) CAST	31

HY-1B (Ocean color satellite B) CAST	31

HYDROS (Hydrosphere State) NASA	31

Hyperspectral Mission (Hyperspectral Earth Observer) ASI	32

ICESat (Ice, Cloud, and Land Elevation Satellite) NASA	32

IGPM  ASI	32

INSAT-2E (Indian National Satellite - 2E) ISRO	32

INSAT-3A (Indian National Satellite - 3A) ISRO	33

INSAT-3D (Indian National Satellite - 3D) ISRO	33

IRS-P4 (OCEANSAT-1) ISRO	33

Jason (Ocean surface topography) NASA	33

Jason-2 (also known as OSTM) (Ocean Surface Topography Mission) NASA	34

KALAPANA (Meteorological satellite) ISRO	34

Kanopus-Vulkan  ROSKOSMOS	34

KOMPSAT-1 (Korea Multi-Purpose Satellite 1) KARI	34

KOMPSAT-2 (Korea Multi-Purpose Satellite 2) KARI	35

LAGEOS-1 (Laser Geodynamics Satellite - 1) NASA	35

LAGEOS-2 (Laser Geodynamics Satellite - 2) NASA	35

LAGEOS-3 (Laser Geodynamics Satellite - 3) NASA	35

Landsat-5  USGS	36

Landsat-7  USGS	36

MEGHA-TROPIQUES  CNES	36

METEOR-3M N1  ROSHYDROMET	36

METEOR-3M N2  ROSHYDROMET	37

Meteor-M No1  ROSHYDROMET	37

Meteor-M No2  ROSHYDROMET	37

METEOSAT-5 (Meteosat-5) EUMETSAT	37

METEOSAT-6 (Meteosat-6) EUMETSAT	38

METEOSAT-7 (Meteosat-7) EUMETSAT	38

METEOSAT-8 (Meteosat Second Generation-1) EUMETSAT	38

METEOSAT-9 (Meteosat Second Generation-2) EUMETSAT	38

METEOSAT-10 (Meteosat Second Generation-3) EUMETSAT	39

METEOSAT-11 (Meteosat Second Generation-4) EUMETSAT	39

METOP-1 (Meteorological Operational Polar Satellite - 1) EUMETSAT	39

METOP-2 (Meteorological Operational Polar Satellite - 2) EUMETSAT	39

METOP-3 (Meteorological Operational Polar Satellite - 3) EUMETSAT	40

Monitor-E  ROSKOSMOS	40

MTSAT-1R (Multi-functional Transport Satellite) JMA	40

MTSAT-2 (Multi-functional Transport Satellite) JMA	40

NMP EO-1 (New Millenium Program Earth Observing-1) NASA	41

NMP EO-3 GIFTS (New Millenium Program EO-3 - Geosynchronous Imaging Fourier Transform Spectrometer - (GIFTS)) NASA	41

NOAA-12 (National Oceanic and Atmospheric Administration - 12) NOAA	41

NOAA-14 (National Oceanic and Atmospheric Administration - 14) NOAA	41

NOAA-15 (National Oceanic and Atmospheric Administration - 15) NOAA	42

NOAA-16 (National Oceanic and Atmospheric Administration - 16) NOAA	42

NOAA-17 (National Oceanic and Atmospheric Administration - M) NOAA	42

NOAA-N (National Oceanic and Atmospheric Administration - N) NOAA	42

NOAA-N' (National Oceanic and Atmospheric Administration - N') NOAA	43

NPOESS-1 (National Polar-orbiting Operational Environmental Satellite System - 1) NOAA	43

NPOESS-2 (National Polar-orbiting Operational Environmental Satellite System - 2) NOAA	43

NPOESS-3 (National Polar-orbiting Operational Environmental Satellite System - 3) NOAA	43

NPOESS-4 (National Polar-orbiting Operational Environmental Satellite System - 4) NOAA	44

NPOESS-5 (National Polar-orbiting Operational Environmental Satellite System - 4) NOAA	44

NPOESS-6 (National Polar-orbiting Operational Environmental Satellite System - 4) NOAA	44

NPP (NPOESS (National Polar-orbiting Operational Environmental Satellite System) Preparatory Project) NOAA	44

OCEANSAT-2 (Ocean satellite-2) ISRO	45

OCO (Orbiting Carbon Observatory) NASA	45

Odin  SNSB	45

PARASOL (Polarization and Anisotropy of Reflectances for Atmospheric Science coupled with Observations from a LIDAR) CNES	45

PICARD  CNES	46

Pleiades 1  CNES	46

Pleiades 2  CNES	46

QuikSCAT (Quick Scatterometer) NASA	46

RADARSAT-1 (Radar satellite-1) CSA	47

RADARSAT-2 (Radar satellite-2) CSA	47

RapidEye (RapidEye) DLR	47

RESOURCESAT-1 (Resource satellite-1) ISRO	47

RESOURCESAT-2 (Resource satellite-2) ISRO	48

Resurs DK  ROSKOSMOS	48

RISAT-1 (Radar Imaging Satellite) ISRO	48

SAC-C  CONAE	48

SAC-D/Aquarius  CONAE	49

SAC-E/SABIA  CONAE	49

SAC-F  CONAE	49

SAOCOM 1A  CONAE	49

SAOCOM 1B  CONAE	50

SAOCOM-2B (1)  CONAE	50

SAOCOM-2B (2)  CONAE	50

SCD-1 (Data Collecting Satellite 1) INPE	50

SCD-2 (Data Collecting Satellite 2) INPE	51

SCISAT-1 (SCISAT-I/ACE) CSA	51

SICH-1M  NSAU	51

SICH-2  NSAU	51

SMOS (Soil Moisture and Ocean Salinity (Earth Explorer Opportunity Mission)) ESA	52

SORCE (Solar Radiation and Climate Experiment) NASA	52

SPOT-2 (Satellite Pour l'Observation de la Terre - 2) CNES	52

SPOT-4 (Satellite Pour l'Observation de la Terre - 4) CNES	52

SPOT-5 (Satellite Pour l'Observation de la Terre - 5) CNES	53

SSR-1 (Remote Sensing Satellite 1) INPE	53

SSR-2 (Remote Sensing Satellite 2) INPE	53

STARLETTE  CNES	53

STELLA  CNES	54

Swarm (Earth's Magnetic Field and Environment Exploreres; Constellation of three satellites) ESA	54

Terra (Terra (formerly EOS AM-1)) NASA	54

TerraSAR-L (TerraSAR L band) BNSC	54

TerraSAR-X (TerraSAR-X) DLR	55

TES (Technology Experimental Satellite) ISRO	55

THEOS (Thailand Earth Observation System) GISTDA	55

TIMED (Thermosphere Ionosphere Mesosphere Energetics and Dynamics mission) NASA	55

Topex-Poseidon (Topographic Experiment/Poseidon) NASA	56

TopSat (Optical Imaging Satellite) BNSC	56

UARS (Upper Atmosphere Research Satellite) NASA	56

UK-DMC (UK Disaster Monitoring Constellation) BNSC	56

Vulkan-Kompas-2  ROSKOSMOS	57

Satellite Instrument Index (Alphabetical)

AATSR Advanced Along-Track Scanning Radiometer BNSC	58

ABI Advanced Baseline Imager NOAA	58

ACC Accelerometer ESA	58

ACE-FTS Atmospheric Chemistry Experiment (ACE) mission CSA	58

ACRIM II Active Cavity Radiometer Irradiance Monitor NASA	58

ACRIM III Active Cavity Radiometer Irradiance Monitor NASA	59

A-DCS ARGOS-Data Collection System NOAA	59

AIRS Atmospheric Infra-red Sounder NASA	59

ALADIN Atmospheric Laser Doppler Instrument ESA	59

ALI Advanced Land Imager NASA	59

ALT Altimeter NOAA	59

AMI/SAR/Image Active Microwave Instrumentation. Image Mode ESA	60

AMI/SAR/wave Active Microwave Instrumentation. Wave mode ESA	60

AMI/scatterometer Active Microwave Instrumentation. Wind mode ESA	60

AMSR follow-on Advanced Microwave Scanning Radiometer follow-on JAXA	60

AMSR-E Advanced Microwave Scanning Radiometer-EOS JAXA (NASA)	60

AMSU-A Advanced Microwave Sounding Unit-A NOAA (BNSC)	61

AMSU-B Advanced Microwave Sounding Unit-B NOAA (BNSC)	61

APS Aerosol Polarimetry Sensor NOAA	61

Aquarius  NASA (CONAE)	61

ARGOS  CNES (NASA)	61

Arina  ROSKOSMOS	62

ASAR Advanced Synthetic-Aperture Radar ESA	62

ASAR (image mode) Advanced Synthetic Aperture Radar (Image mode) ESA	62

ASAR (wave mode) Advanced Synthetic Aperture Radar (Wave mode) ESA	62

ASCAT Advanced Scatterometer EUMETSAT (ESA)	62

ASM Absolute Scalar Magnetometer ESA (CNES)	62

ASTER Advanced Spaceborne Thermal Emission and Reflection Radiometer METI (Japan) (NASA)	63

ATLID ATmospheric LIDar ESA	63

ATMS Advanced Technology Microwave Sounder NOAA (NASA)	63

ATSR/M  CNES	63

ATSR-2 Along Track Scanning Radiometer - 2 BNSC (CSIRO)	63

AVHRR/2 Advanced Very High Resolution Radiometer/2 NOAA	63

AVHRR/3 Advanced Very High Resolution Radiometer/3 NOAA	64

AVNIR-2 Advanced Visible and Near Infra-red Radiometer type 2 JAXA	64

AWiFS Advanced Wide Field Sensor ISRO	64

BISSAT Bissat Passive Radar ASI	64

CALIOP Cloud-Aerosol Lidar with Orthogonal Polarization NASA	64

CCD (CBERS) High Resolution CCD Camera CAST (INPE)	64

CCD (HJ, HY) CCD camera CAST	64

CCD camera  ISRO	65

CERES Cloud and the Earth's Radiant Energy System NASA	65

CHAMP GPS Sounder GPS TurboRogue Space Receiver (TRSR) NASA (DLR)	65

CHAMP gravity package (Accelerometer+GPS) STAR Accelerometer CNES (DLR)	65

CHAMP magnetometry package (1 Scalar + 2 Vector Magnetometer) Overhauser Magnetometer and Fluxgate Magnetometer DLR	65

CIA Advanced Hyperspectral camera ASI	66

CLAES Cryogenic Limb Array Etalon Spectrometer instrument NASA	66

Cloud Sensor Cloud and aerosol sensor JAXA	66

CMIS Conical-scanning Microwave Imager/Sounder NOAA	66

COCTS Ocean colour scanner CAST	66

Communications payload (Ka and UHF band)  CSIRO	66

CPR Cloud Profiling Radar ESA	67

CPR (Cloudsat) Cloud Profiling Radar NASA	67

CrIS Cross-track Infrared Sounder NOAA (NASA)	67

CZI Coast region imager CAST	67

DCP (SCD) Data Collecting Platform Transponder INPE	67

DCS (CAST) Data Collecting System Transponder (CAST) CAST	67

DCS (JAXA) Data Collection System (JAXA) JAXA	67

DCS (NOAA) Data Collection System (NOAA) NOAA	68

DCS (ROSHYDROMET) Data Collection System ROSHYDROMET (ROSKOSMOS)	68

DMC Imager Disaster Management Constellation Imager BNSC	68

DORIS Doppler Orbitography and Radio-positioning Integrated by Satellite CNES	68

DORIS-NG Doppler Orbitography and Radio-positioning Integrated by Satellite-NG CNES	68

DPR Dual-frequency Precipitation Radar JAXA (NASA)	68

DRF  ROSKOSMOS	68

ECHO-V  ROSKOSMOS	69

EFI Electric Field Instrument ESA (CSA)	69

EGG 3-Axis Electrostatic Gravity Gradiometer ESA	69

EHIS Energetic Heavy Ion Sensor NOAA	69

ENVISAT Comms Communications package on ENVISAT ESA	69

EOC Electro-Optical Camera KARI	69

EPIC Earth PolyChromatic Imaging Camera NASA	69

ERBE Earth Radiation Budget Experiment (non-scanner) NASA	69

ERBS Earth Radiation Budget Sensor NOAA	69

ERS Comms Communication package for ERS ESA	70

ETM+ Enhanced Thematic Mapper Plus USGS	70

EUVS Extreme Ultraviolet Sensor NOAA	70

Fluxgate magnetometer  CRCSS	70

GALS-M Galactic space rays detector ROSHYDROMET	70

Geomicrowave sounder  NOAA	70

Geoton-L1  ROSKOSMOS	70

GERB Geostationary Earth Radiation Budget EUMETSAT (ASI)	71

GGAK-E Heliogeophysical hardware complex ROSKOSMOS	71

GGAK-M Heliogeophysical hardware complex ROSKOSMOS	71

GHG Sensor Greenhouse gases observing sensor JAXA	71

GID-12T  ROSKOSMOS	71

GIFTS Geosynchronous Imaging Fourier Transform Spectrometer NASA	71

GLAS Geoscience Laser Altimeter System NASA	72

GLI follow-on Global Imager follow-on JAXA	72

GLM GEO Lightning Mapper NOAA	72

GMI GPM Microwave Imager NASA	72

GMS Comms Communications package on GMS JAXA (JMA)	72

GOES Comms Communications package on GOES NOAA	72

GOLPE GPS Occultation and Passive reflection Experiment NASA	73

GOME Global Ozone Monitoring Experiment ESA	73

GOME-2 Global Ozone Monitoring Experiment - 2 EUMETSAT (ESA)	73

GOMOS Global Ozone Monitoring by Occultation of Stars ESA (CNES)	73

GPS (ESA) GPS receiver ESA	73

GPS (GRACE) Global Positioning System Receiver NASA	73

GPS receiver  CRCSS	73

GPSDR GPS Demonstration Receiver CONAE (NASA)	74

GRAS GNSS Receiver for Atmospheric Sounding EUMETSAT (ESA)	74

HAIRS High Accuracy Inter-satellite Ranging System NASA	74

HALOE Halogen Occultation Experiment NASA	74

HES Hyperspectral Environmental Suite NOAA	74

HiRDLS High Resolution Dynamics Limb Sounder NASA (BNSC)	75

HIRS/2 High Resolution Infra-red Sounder/2 NOAA	75

HIRS/3 High Resolution Infra-red Sounder/3 NOAA	75

HIRS/4 High Resolution Infra-red Sounder/4 NOAA	75

HRDI High Resolution Doppler Imager NASA	75

HRG High Resolution Geometry CNES	76

HRMS High Resolution Multi-spectral Scanner CONAE	76

HR-PAN High Resolution Panchromatic Camera ISRO	76

HRS High Resolution Stereoscopy CNES	76

HRTC High Resolution Panchromatic Camera CONAE	76

HRV High Resolution Visible CNES	76

HRVIR High Resolution Visible and Infra-red CNES	77

HSB Humidity Sounder/Brazil INPE (NASA)	77

HSC High Sensitivity Camera CONAE	77

HSI (HJ-1A) Hyper Spectrum Imager CAST	77

HSMS High Swath Multi-spectral Scanner CONAE	77

HSRS Hot Spot Recognition System DLR	77

HSS Hyper-spectral Scanner CONAE	77

HSTC High Sensitivity Technological Camera CONAE	77

HYC HYperspectral Camera ASI	78

HYDROS  NASA	78

Hyperion Hyperspectral Imager NASA	78

IAP Instrument for plasma analysis CNES	78

IASI Infra-red Atmospheric Sounding Interferometer CNES (EUMETSAT)	78

ICARE Influence of Space Radiation on Advanced Components CNES	78

ICE Instrument for Electric Field CNES	78

IDP Instrument For Plasma Detection CNES	79

IGPM radiometer IGPM microwave radiometer ASI	79

IGPM rain radar  ASI	79

IIR Imaging infrared radiometer CNES	79

IKFS-2 Fourier spectrometer ROSHYDROMET	79

IKOR-M The modernized measuring instrument of short-wave reflected radiation ROSKOSMOS	79

Imager  NOAA	79

Imager (INSAT)  ISRO	80

IMAGER/MTSAT-1R Imager/MTSAT JMA	80

IMAGER/MTSAT-2 Imager/MTSAT JMA	80

IMSC Instrument Search Coil Magnetometer CNES	80

IMWTS Improved MicroWave Temperature Sounder NRSCC (CAST)	80

INES Italian Navigation Experiment ASI	80

IR (HJ-1B) Infrared Camera CAST	80

IR Camera (SAOCOM)  CONAE	81

IRAS InfraRed Atmospheric Sounder NRSCC (CAST)	81

IR-MSS Infrared Multispectral Scanner CAST (INPE)	81

IRS  CAST (INPE)	81

ISAMS Improved Stratospheric and Mesospheric Sounder instrument NASA	81

ISL Langmuir probes CNES	81

IST Italian Star Tracker ASI	81

IVISSR (FY-2) Improved Multispectral Visible and Infra-red Spin Radiometer (5 channels) NRSCC (CAST)	82

JMR 'JASON Microwave Radiometer NASA	82

KGI-4C Module for Geophysical Measurements ROSHYDROMET	82

Klimat Scanning IR radiometer ROSHYDROMET	82

KMSS Medium range multi-spectral scanner ROSHYDROMET (ROSKOSMOS)	82

LAC Laser Atmospheric Corrector NASA	82

Landsat Comms Communications package for Landsat USGS	82

Laser reflectors  CNES	83

Laser reflectors (ESA) Laser reflectors ESA	83

L-band SAR  INPE	83

LISS-III Linear Imaging Self Scanner - III ISRO	83

LISS-IV Linear Imaging Self Scanner - IV ISRO	83

LRA Laser Retroreflector Array NASA (ASI)	83

LRA (LAGEOS) Laser Retroreflector Array NASA (ASI)	83

L-SAR L-Band SAR BNSC	84

MADRAS  CNES	84

MAESTRO Measurements of Aerosol Extinction in the Stratosphere and Troposphere Retrieved by Occultation CSA	84

Magnetometer (NOAA) Magnetometer NOAA	84

MASTER  ESA	84

MBEI Multi-band Earth Imager NSAU	84

MCP Meteorological Communications Package (MCP) EUMETSAT	85

MERIS Medium-Resolution Imaging Spectrometer ESA	85

MERSI Moderate Resolution Spectral Imager NRSCC (CAST)	85

METEOSAT Comms Communications package for METEOSAT EUMETSAT	85

MHS Microwave Humidity Sounder EUMETSAT	85

MIPAS Michelson Interferometric Passive Atmosphere Sounder ESA	85

MIRAS Multichannel Infrared Atmospheric Sounder NRSCC (CAST)	86

MIRAS (SMOS) 2-D Passive L-Band Microwave Interferometer ESA	86

MIREI Middle IR Earth Imager NSAU	86

MISR Multi-angle Imaging SpectroRadiometer NASA	86

MIVZA Microwave scanning radiometer ROSHYDROMET	86

MLS Microwave Limb Sounder NASA	86

MMP Magnetic Mapping Payload CONAE (DSRI (Denmark))	87

MMRS Multispectral Medium Resolution Scanner CONAE	87

MOC Multi-spectral Optical Camera CONAE	87

MODIS MODerate-Resolution Imaging Spectroradiometer NASA	87

MOPITT Measurements Of Pollution In The Troposphere CSA	87

MPS Magnetospheric Particle Sensor NOAA	87

MR-2000M1 Scanning visible radiometer ROSHYDROMET	88

MS (GISTDA) Multi spectral imager GISTDA	88

MSC Multi-Spectral Camera KARI	88

MSG Comms Communications package for MSG EUMETSAT	88

MSGI-MKA Spectrometer ROSHYDROMET	88

MSI Multi Spectral Imager DLR	88

MSMR Multifrequency Scanning Microwave Radiometer ISRO	88

MSS Multispectral Scanner USGS	88

MSS (Roskosmos) Multispectral film-making system ROSKOSMOS	89

MSS-BIO Polyzonal scanning system of bioefficiency of sea water areas ROSKOSMOS	89

MSTE-5E Multichannel system of geoactive measurements ROSHYDROMET	89

MSU Microwave Sounding Unit NOAA	89

MSU-E Multispectral high resolution electronic scanner ROSHYDROMET	89

MSU-EU Multi-Spectral Radiometer with High Resolution NSAU	89

MSU-GS Multispectral scanning imager-radiometer ROSHYDROMET	89

MSU-M Multi-Spectral Low Resolution Scanning System NSAU	90

MSU-MR Images of clouds, snow, ice and land cover ROSHYDROMET	90

MSU-SM Multi-Spectral Medium Resolution Scanning System ROSHYDROMET	90

MTSAT Comms Communications package for MTSAT JMA (JAXA)	90

MTVZA Scanning microwave radiometer ROSHYDROMET	90

MTVZA-OK Scanning microwave radiometer ROSHYDROMET	90

MUX Multispectral CCD Camera CAST (INPE)	90

MVIRI METEOSAT Visible and Infra-Red Imager EUMETSAT (ESA)	91

MWHS MicroWave Humidity Sounder NRSCC (CAST)	91

MWR (BNSC) Microwave Radiometer BNSC	91

MWR (CONAE) Microwave radiometer CONAE	91

MWRI MicroWave Radiation Imager NRSCC (CAST)	91

MWTS MicroWave Temperature Sounder NRSCC (CAST)	91

NIRST New Infrared Sensor Technology CONAE	92

NISTAR NIST Advanced Radiometer NASA	92

NOAA Comms Communications package for NOAA NOAA	92

NVK Low-frequency wave complex ROSKOSMOS	92

OBA Observador Brasileiro da Amazonia INPE	92

OCM Ocean Colour Monitor ISRO	92

OCO Orbiting Carbon Observatory NASA	93

OEA Optical-electronic equipment ROSKOSMOS	93

OLS Operational Linescan System NOAA (US DoD)	93

OMI Ozone Measuring Instrument NASA (NIVR (Netherland))	93

OMPS Ozone Mapping and Profiler Suite NOAA	93

OP Ozone Profiler NRSCC (CAST)	93

OSIRIS Optical Spectrograph and Infra-Red Imaging System CSA	94

OSMI Ocean Scanning Multispectral Imager KARI	94

PALSAR Phased Array type L-band Synthetic Aperture Radar JAXA (METI (Japan))	94

Pamela  ROSKOSMOS	94

PAN Panchromatic and multispectral imager CAST	94

PAN (Cartosat-1) Panchromatic sensor ISRO	94

PAN (GISTDA) Panchromatic imager GISTDA	95

PEM Particle Environment Monitor NASA	95

Plasma-Mag  NASA	95

Pleiades HR High Resolution Optical Imaging CNES	95

POLDER-P POLarization and Directionality of the Earth's Reflectances (PARASOL version) CNES	95

POSEIDON-1 (SSALT-1) Positioning Ocean Solid Earth Ice Dynamics Orbiting Navigator  (Single frequency solid state radar altimeter) CNES	95

POSEIDON-2 (SSALT-2) Positioning Ocean Solid Earth Ice Dynamics Orbiting Navigator (Single frequency solid state radar altimeter) CNES	96

POSEIDON-3 Positioning Ocean Solid Earth Ice Dynamics Orbiting Navigator (Single frequency solid state radar altimeter) CNES	96

PREMOS PREcision Monitoring of Solar variability CNES	96

PRISM Panchromatic Remote-sensing Instrument for Stereo Mapping JAXA	96

PSA Panchromatic film-making equipment ROSKOSMOS	96

PSS Panchromatic film-making system ROSKOSMOS	96

RA Radar Altimeter ESA	97

RA-2 Radar Altimeter - 2 ESA	97

RADARSAT DTT X band (downlink of payload) CSA	97

RADARSAT TTC S band (Tracking, Telemetry and Command) CSA	97

Radiomet  ROSKOSMOS	97

RBE  ROSKOSMOS	97

RCHA  ROSKOSMOS	97

RDSA The film-making equipment of the allocated access ROSKOSMOS	97

RIMS-M Mass-spectrometer ROSHYDROMET	98

RLSBO Side looking microwave radar ROSKOSMOS (NIIRI)	98

RM-08 Scanning Microwave Radiometer ROSHYDROMET (NSAU)	98

ROSA formerly called Lagrange ASI	98

RRA Retroreflector Array CNES	98

S&R (GOES) Search and Rescue NOAA	98

S&R (NOAA) Search and Rescue Satellite Aided Tracking NOAA	98

SABER Sounding of the Atmosphere usingBroadband Emission Radiometry NASA	99

SAGE II Stratospheric Aerosol and Gas Experiment-II NASA	99

SAGE III Stratospheric Aerosol and Gas Experiment-III NASA (ROSKOSMOS)	99

SAPHIR  CNES (ISRO)	99

SAR (RADARSAT) Synthetic Aperture Radar (CSA) C band CSA	100

SAR (RADARSAT-2) Synthetic Aperture Radar (CSA) C band CSA	100

SAR (RISAT)  ISRO	100

SAR (ROSHYDROMET) Synthetic Aperture Radar ROSHYDROMET (ROSKOSMOS)	101

SAR (SAOCOM) Synthetic Aperture Radar (CONAE) CONAE	101

SAR 2000 Multi-Mode Synthetic Aperture Radar ASI	101

SARSAT Search and Rescue Satellite Aided Tracking NOAA	101

S-band SAR S-band Synthetic Aperture Radar CAST	101

SBUV/2 Solar Backscattter Ultra-Violet Instrument/2 NOAA	102

ScaRaB Scanner for Earth's Radiation Budget CNES (NPO "PLANETA")	102

Scatterometer (ISRO)  ISRO	102

Scatterometer (JAXA) Scatterometer JAXA	102

SCIAMACHY Scanning Imaging Absorption Spectrometer for Atmospheric Chartography ESA	102

SeaWinds  NASA (JAXA)	102

SEM (GOES) Space Environment Monitor NOAA	102

SEM (POES) Space Environment Monitor NOAA	103

SESS Space Environmental Sensor Suite NOAA	103

SEVIRI Spinning Enhanced Visible and Infra-Red Imager EUMETSAT (ESA)	103

SFM-2 UV limb spectrometer ROSHYDROMET	103

SGPS Solar and Galactic Proton Sensor NOAA	103

SIM Spectral Irradiance Monitor NASA	104

SIRAL SAR Interferometer Radar Altimeter ESA	104

SKL-M Solar ray spectrometer ROSHYDROMET	104

SMR Submillimetre Radiometer SNSB	104

SODAD Orbital System for an Active Detection of Debris CNES	104

SODISM SOlar Diameter Imager and Surface Mapper CNES	104

SOLSTICE SOLar STellar Irradiance Comparison Experiment NASA	105

Sounder  NOAA	105

Sounder (INSAT)  ISRO	105

SOVAP SOlar Variability Picard radiometer CNES	105

SPECTRA Surface Processes and Ecosystem Changes Through Response Analysis ESA	105

SSB/X-2 Special Sensor Gamma Ray Particle Detector NOAA (US DoD)	105

SSIES-2 Special Sensor Ionospheric Plasma Drift/Scintillation Meter NOAA (US DoD)	106

SSIES-3 Special Sensor Ionospheric Plasma Drift/Scintillation Meter NOAA (US DoD)	106

SSJ/4 Special Sensor Precipitating Plasma Monitor NOAA (US DoD)	106

SSJ/5 Special Sensor Precipitating Plasma Monitor NOAA (US DoD)	106

SSM Special Sensor Magnetometer NOAA (US DoD)	106

SSM/I Special Sensor Microwave Imager NOAA (US DoD)	106

SSM/T-1 Special Sensor Microwave Temperature Sounder NOAA (US DoD)	107

SSM/T-2 Special Sensor Microwave Water Vapor Sounder NOAA (US DoD)	107

SSMIS Special Sensor Microwave Imager Sounder NOAA (US DoD)	107

SSU Stratospheric Sounding Unit NOAA	107

SSULI Special Sensor Ultraviolet Limb Imager NOAA	107

SSUSI Special Sensor Ultraviolet Spectrographic Imager NOAA	107

SSZ  NOAA (US DoD)	108

STR Star Tracker ESA	108

SUSIM (UARS) Solar Ultraviolet Irradiance Monitor NASA	108

SXI Solar X-ray Imager NOAA (USAF)	108

SXS Solar X-Ray Sensor NOAA	108

TerraSAR-X X-Band Synthetic Aperture Radar DLR	108

TES Tropospheric Emission Spectrometer NASA	109

TIM Total Irradiance Monitor NASA	109

TIS (CONAE) Thermal IR Scanner CONAE	109

TM Thematic Mapper USGS	109

TMR TOPEX Microwave Radiometer NASA	109

TOM Total Ozone Mapper NRSCC (CAST)	109

TOPEX TOPEX NASA Radar Altimeter NASA	109

TOPSAT telescope  BNSC	110

TRSR Turbo-Rogue Space Receiver NASA	110

TSIS Total Solar Irradiance Sensor NOAA	110

Variant  ROSKOSMOS	110

VEGETATION  CNES (EEC)	110

VFM Vector Magnetometer ESA	110

VHRR Very High Resolution Radiometer ISRO	110

VIIRS Visible/Infrared Imager Radiometer Suite NOAA (NASA)	111

VIRR Multispectral Visible and Infra-red Scan Radiometer (10 channels) NRSCC (CAST)	111

VISSR (GMS-5) Visible and Infra-red Spin Scan Radiometer (GMS-5) JAXA (JMA)	111

WAOSS-B Wide-Angle Optoelectronic Stereo Scanner DLR	111

WEFAX Weather Facsimile NOAA	111

WFC Wide Field Camera NASA	111

WFI Wide Field Imager CAST (INPE)	111

WFI-2 Wide Field Imager 2 CAST (INPE)	112

WiFS Wide Field Sensor ISRO	112

WINDII  CNES (NASA)	112

WTE Whale Tracker Experiment CONAE	112

XPS XUV Photometer System NASA	112

| ACRIMSAT (Active Cavity Radiometer Irradiance Monitor) NASA | Currently being flown | 20 Dec 99 | 01 Oct 07 | Will sustain long-term solar luminosity database by providing measurements of total solar irradiance and the solar constant | ACRIM III | Type: Sun-synchronous Altitude: 716 km Period: 90 mins Inclination: 98.13 deg Repeat cycle: LST: 1050 Longitude (if geo): Asc/desc: Ascending URL: acrim.jpl.nasa.gov/ |
| --- | --- | --- | --- | --- | --- | --- |
| ADM-Aeolus (Atmospheric Dynamics Mission (Earth Explorer Core Mission)) ESA | Approved | 15 Oct 07 | 15 Oct 10 | Will provide wind profile measurements for global 3-D wind field products used for study of atmospheric dynamics, including global transport of energy, water, aerosols, and chemicals | ALADIN | Type: Sun-synchronous Altitude: 408 km Period: Inclination: 96.99 deg Repeat cycle: 7 days LST: Longitude (if geo): Asc/desc: TBD URL: www.esa.int/export/esaLP/aeolus.html |
| ALOS (Advanced Land Observing Satellite) JAXA | Approved | 01 Sep 05 | 01 Sep 10 | Cartography, digital terrain models, environmental monitoring, disaster monitoring, civil planning, agriculture and forestry, Earth resources, land surface | AVNIR-2, PALSAR, PRISM | Type: Sun-synchronous Altitude: 692 km Period: 98.7 mins Inclination: 98.16 deg Repeat cycle: 3 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: alos.jaxa.jp/index-e.html |
| Aqua (Aqua (formerly EOS PM-1)) NASA | Currently being flown | 04 May 02 | 04 May 07 | Atmospheric dynamics/water and energy cycles, cloud formation, precipitation and radiative properties, air/seafluxes of energy and moisture, sea ice extent and heat exchange with the atmosphere. Option of 705km or 438km orbit altitude. | AIRS, AMSR-E, AMSU-A, CERES, HSB, MODIS | Type: Sun-synchronous Altitude: 705 km Period: 98.8 mins Inclination: 98.2 deg Repeat cycle: 16 days LST: 1330 Longitude (if geo): Asc/desc: Ascending URL: eos-pm.gsfc.nasa.gov |
| Aura (Aura (formerly EOS Chemistry)) NASA | Currently being flown | 15 Jul 04 | 15 Jul 10 | Chemistry and dynamics of Earth’s atmosphere from the ground through the mesosphere. | HiRDLS, MLS (EOS-Aura), OMI, TES | Type: Sun-synchronous Altitude: 705 km Period: 98.8 mins Inclination: 98.2 deg Repeat cycle: 16 days LST: 1345 Longitude (if geo): Asc/desc: Ascending URL: aura.gsfc.nasa.gov/ |
| Baumanets ROSKOSMOS | Planned | 05 Dec 05 | 31 Dec 06 | Experimental satellite for data transmission, remote sensing, and spacecraft management. | OEA | Type: Sun-synchronous Altitude: 700 km Period: Inclination: 98 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.federalspace.ru |
| BelKA ROSKOSMOS | Planned | 01 Jan 06 | 31 Dec 11 | Regular imaging of terrestrial sites in visible and near IR ranges with high spatial resolution | MSS (Roskosmos), PSS | Type: Sun-synchronous Altitude: 505 km Period: Inclination: 97.4 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.federalspace.ru |
| BIRD (Bi-spectral Infrared Detection) DLR | Currently being flown | 22 Oct 01 | 31 Dec 05 | Small satellite mission with technical and scientific objectives (Study of thermal processes on the Earth surface) objectives | HSRS, WAOSS-B | Type: Sun-synchronous Altitude: 572 km Period: Inclination: 97.8 deg Repeat cycle: LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.fire.uni-freiburg.de/iffn/tech/tech_9.htm |
| BISSAT ((Bistatic SAR mission)) ASI | Considered | 01 Jan 06 | 01 Jan 08 | Evaluation of bistatic radar cross section of natural and man-made targets, image classification, land surface. Receive-only satellite in formation with main mission COSMO-Skymed | BISSAT | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| CALIPSO (Cloud-Aerosol Lidar and Infrared Pathfinder Satellite Observations) NASA | Approved | 15 Apr 05 | 15 Apr 08 | Measurements of aerosol & cloud properties for climate predictions, using a 3 channel lidar and passive instruments in formation with Aqua and CloudSat for coincident observations of radiative fluxes and atmospheric state. | CALIOP, IIR, WFC | Type: Sun-synchronous Altitude: 705 km Period: 98.8 mins Inclination: 98.2 deg Repeat cycle: LST: 1330 Longitude (if geo): Asc/desc: Ascending URL: www-calipso.larc.nasa.gov/ |
| CARTOSAT-1 (Indian Remote Sensing Satellite - P5) ISRO | Approved | 15 Mar 05 | 01 Jul 09 | High precision large-scale cartographic mapping of 1:10000 scale and thematic applications (with merged XS data) at 1:4000 scales | PAN (Cartosat-1) | Type: Sun-synchronous Altitude: 630 km Period: 97.178 mins Inclination: 97.87 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| CARTOSAT-2 ISRO | Approved | 31 Dec 05 | 01 Jan 10 | High precision large-scale cartographic mapping of 1:10000 scale and thematic applications (with merged XS data) at 1:4000 scales | HR-PAN | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| CBERS-2 (China Brazil Earth Resources Satellite - 2) CAST | Currently being flown | 22 Oct 03 | 18 Aug 07 | Earth resources, environmental monitoring, land surface | CCD (CBERS), DCS (CAST), IR-MSS, WFI | Type: Sun-synchronous Altitude: 778 km Period: 100.26 mins Inclination: 98.5 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ & www.cbers.inpe.br/en/programas/cbers1-2.htm |
| CBERS-2B (China Brazil Earth Resources Satellite - 2B) CAST | Approved | 20 Oct 06 | 20 Oct 08 | Earth resources, environmental monitoring, land surface | CCD (CBERS), DCS (CAST), IR-MSS, WFI | Type: Sun-synchronous Altitude: 778 km Period: Inclination: 98.5 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ & www.cbers.inpe.br/en/programas/cbers1-2.htm |
| CBERS-3 (China Brazil Earth Resources Satellite - 3) CAST | Approved | 20 Oct 08 | 20 Oct 11 | Earth resources, environmental monitoring, land surface | DCS (CAST), IRS, MUX, PAN, WFI-2 | Type: Sun-synchronous Altitude: 778 km Period: 100.26 mins Inclination: 98.5 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ & www.cbers.inpe.br/en/programas/cbers3-4.htm |
| CBERS-4 (China Brazil Earth Resources Satellite - 4) CAST | Approved | 20 Oct 11 | 20 Oct 14 | Earth resources, environmental monitoring, land surface | DCS (CAST), IRS, MUX, PAN, WFI-2 | Type: Sun-synchronous Altitude: 778 km Period: 100.26 mins Inclination: 98.5 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ & www.cbers.inpe.br/en/programas/cbers3-4.htm |
| CHAMP (Challenging Mini-Satellite Payload for Geophysical Research and Application) DLR | Currently being flown | 15 Jul 00 | 15 Jul 05 | Gravity field, Precise geoid, Magnetic field, Atmospheric physics | CHAMP GPS Sounder, CHAMP gravity package (Accelerometer+GPS), CHAMP magnetometry package (1 Scalar + 2 Vector Magnetometer) | Type: Inclined, non-sunsynchronous Altitude: 470 km Period: Inclination: 87 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: op.gfz-potsdam.de/champ/index_CHAMP.html |
| CloudSat (CloudSat) NASA | Approved | 15 Apr 05 | 15 Feb 07 | CloudSat will use advanced radar to "slice" through clouds to see their vertical structure, providing a completely new observational capability from space. One of first satellites to study clouds on global basis. Will fly in formation with Aqua and CALIPSO. | CPR (Cloudsat) | Type: Sun-synchronous Altitude: 705 km Period: 98.8 mins Inclination: 98.2 deg Repeat cycle: LST: 1335 Longitude (if geo): Asc/desc: Ascending URL: cloudsat.atmos.colostate.edu/ |
| COSMO - SkyMed (COnstellation of small Satellites for Mediterranean basin Observation) ASI | Planned | 31 Dec 06 | 31 Dec 20 | Environmental monitoring, surveillance and risk management applications, environmental resources management, maritime management, earth topographic mapping, law enforcement, informative / science applications | SAR 2000 | Type: Sun-synchronous Altitude: 619 km Period: 97.86 mins Inclination: Repeat cycle: 16 days LST: 600 Longitude (if geo): Asc/desc: Ascending URL: www.alespazio.it/program/tlr/cosmo/cosmo.htm |
| CRYOSAT (CryoSat (Earth Explorer Opportunity Mission)) ESA | Approved | 31 Mar 05 | 31 Mar 08 | A radar altimetry mission to determine variations in the thickness of the Earth’s continental ice sheets and marine ice cover. Primary objective is to test the prediction of thinning arctic ice due to global warming | DORIS-NG, Laser reflectors (ESA), SIRAL | Type: Inclined, non-sunsynchronous Altitude: 717 km Period: Inclination: 92 deg Repeat cycle: 369 days LST: Longitude (if geo): Asc/desc: TBD URL: www.esa.int/export/esaLP/cryosat.html |
| DEMETER (Detection of Electro-Magnetic Emissions Transmitted from Earthquake Regions) CNES | Approved | 29 Jun 04 | 29 Jun 06 | Micro-satellite to study; ionospheric disturbances related to seismic activity, ionospheric disturbances related to human activity, pre and post-seismic effects in the ionosphere, global information on the Earth's electromagnetic environment | IAP, ICE, IDP, IMSC, ISL | Type: Sun-synchronous Altitude: 800 km Period: Inclination: Repeat cycle: LST: 1030 Longitude (if geo): Asc/desc: TBD URL: smsc.cnes.fr/DEMETER/index.htm |
| Diademe 1&2 CNES | Currently being flown | 15 Feb 67 | 31 Dec 50 | Geodetic measurements using satellite laser ranging | RRA | Type: Inclined, non-sunsynchronous Altitude: 1200 km Period: 108 mins Inclination: 40 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: galileo.crl.go.jp/ilrs/diademe.html |
| DMSP F-13 (Defense Meteorological Satellite Program F-13) NOAA | Currently being flown | 01 Mar 97 | 30 Sep 05 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide atmospheric, oceanographic, solar-geophyscial, and cloud cover data on a daily basis. (Primary operational satellite) | OLS, SSB/X-2, SSIES-2, SSJ/4, SSM, SSM/I, SSM/T-1, SSM/T-2, SSZ | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: LST: 1812 Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DMSP F-15 (Defense Meteorological Satellite Program F-15) NOAA | Currently being flown | 12 Dec 99 | 30 Sep 06 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide cloud cover data on a daily basis. (Primary operational satellite) | OLS, SSB/X-2, SSIES-2, SSJ/4, SSM, SSM/I, SSM/T-1, SSM/T-2, SSZ | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.9 deg Repeat cycle: LST: 2029 Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DMSP F-16 (Defense Meteorological Satellite Program F-16) NOAA | Approved | 15 Oct 03 | 15 Oct 07 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide cloud cover data on a daily basis. | OLS, SSB/X-2, SSIES-2, SSIES-3, SSJ/4, SSJ/5, SSM, SSM/I, SSM/T-1, SSM/T-2, SSMIS, SSULI, SSUSI, SSZ | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.9 deg Repeat cycle: LST: 2132 Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DMSP F-17 (Defense Meteorological Satellite Program F-17) NOAA | Approved | 15 Apr 05 | 01 Jun 08 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide cloud cover data on a daily basis. | OLS, SSIES-3, SSJ/5, SSM, SSM/T-1, SSMIS, SSULI, SSUSI | Type: Sun-synchronous Altitude: 850 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DMSP F-18 (Defense Meteorological Satellite Program F-18) NOAA | Approved | 15 Oct 07 | 15 Oct 10 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide cloud cover data on a daily basis. | OLS, SSIES-3, SSJ/5, SSM, SSM/T-1, SSMIS, SSULI, SSUSI | Type: Sun-synchronous Altitude: 850 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DMSP F-19 (Defense Meteorological Satellite Program F-19) NOAA | Approved | 15 Apr 09 | 15 Apr 12 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide cloud cover data on a daily basis. | OLS, SSIES-3, SSJ/5, SSM, SSM/T-1, SSMIS, SSULI, SSUSI | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DMSP F-20 (Defense Meteorological Satellite Program F-20) NOAA | Approved | 15 Oct 11 | 15 Oct 14 | The long-term meteorological programme of the US Department of Defense (DoD) - with the objective to collect and disseminate worldwide cloud cover data on a daily basis. | OLS, SSIES-3, SSJ/5, SSM, SSM/T-1, SSMIS, SSULI, SSUSI | Type: Sun-synchronous Altitude: 850 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Ascending URL: dmsp.ngdc.noaa.gov/dmsp.html |
| DSCOVR (DSCOVR (formerly Triana)) NASA | Approved | 01 Jan 08 | 01 Jan 12 | Continuously observes the sunlit Earth (full disk) – transmitting an image every 15 minutes for distribution by internet. Studies how solar radiation affects climate. Will be positioned at the Langrange point between Earth and sun. | EPIC, NISTAR, Plasma-Mag | Type: TBD Altitude: 1500000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: triana.gsfc.nasa.gov/home/www-pm.larc.nasa.gov/triana.html |
| Elektro-L (Geostationary Operational Meteorological Satellite - 2) ROSHYDROMET | Approved | 01 Dec 06 | 31 Dec 12 | Hydrometeorology, climatology, disaster management, space environment, ice and snow, land surface, space environment, data collection and communication. | DCS (ROSHYDROMET), GGAK-E, MSU-GS | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -76 Asc/desc: N/A URL: sputnik1.infospace.ru/ |
| Envisat (Environmental Satellite) ESA | Currently being flown | 01 Mar 02 | 01 Mar 07 | Physical oceanography, land surface, ice and snow, atmospheric chemistry, atmospheric dynamics/water and energy cycles | AATSR, ASAR, ASAR (image mode), ASAR (wave mode), DORIS-NG, ENVISAT Comms, GOMOS, MERIS, MIPAS, MWR (BNSC), RA-2, SCIAMACHY | Type: Sun-synchronous Altitude: 782 km Period: 100.5 mins Inclination: 98.52 deg Repeat cycle: 35 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: envisat.esa.int/ |
| ERBS (Earth Radiation Budget Satellite) NASA | Currently being flown | 05 Oct 84 | 30 Apr 05 | Earth radiation budget measurements. | ERBE, SAGE II | Type: Inclined, non-sunsynchronous Altitude: 585 km Period: 96.3 mins Inclination: 57 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: asd-www.larc.nasa.gov/erbe/erbs.html |
| ERS-2 (European Remote Sensing satellite - 2) ESA | Currently being flown | 21 Apr 95 | 31 Dec 05 | Earth resources plus physical oceanography, ice and snow, land surface, meteorology, geodesy/gravity, environmental monitoring, atmospheric chemistry | AMI/SAR/Image, AMI/SAR/wave, AMI/scatterometer, ATSR/M, ATSR-2, ERS Comms, GOME, MWR (BNSC), RA | Type: Sun-synchronous Altitude: 782 km Period: 100.5 mins Inclination: 98.52 deg Repeat cycle: 35 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.esa.int/export/esaEO/SEMGWH2VQUD_index_0_m.html |
| ESA Future Missions (ESA Future Missions) ESA | Considered | 01 Jan 08 | 01 Jan 18 | Physical Oceanogreaphy, land surface, ice and snow, atmospheric dynamics/water and energy cycles | ATLID, CPR, MASTER, SPECTRA | Type: TBD Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.esa.int/export/esaLP/index.html |
| FedSat (Federation Satellite) CSIRO | Currently being flown | 14 Dec 02 | 14 Dec 05 | Communications, data relay, near Earth environment, upper atmospheric physics, meteorology | Communications payload (Ka and UHF band), Fluxgate magnetometer, GPS receiver | Type: Sun-synchronous Altitude: 803 km Period: 101 mins Inclination: 98.6 deg Repeat cycle: LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.crcss.csiro.au/ |
| FY-2C (FY-2C Geostationary Meteorological Satellite) NRSCC | Currently being flown | 19 Oct 04 | 19 Oct 07 | Meteorology and environmental monitoring Data collection and redistribution | IVISSR (FY-2) | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -105 Asc/desc: TBD URL: |
| FY-2D (FY-2D Geostationary Meteorological Satellite) NRSCC | Planned | 31 Dec 06 | 31 Dec 09 | Meteorology and environmental monitoring Data collection and redistribution | IVISSR (FY-2) | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -105 Asc/desc: TBD URL: |
| FY-2E (FY-2E Geostationary Meteorological Satellite) NRSCC | Planned | 31 Dec 09 | 31 Dec 12 | Meteorology and environmental monitoring Data collection and redistribution | IVISSR (FY-2) | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -105 Asc/desc: TBD URL: |
| FY-3A (FY-3A Polar-orbiting Meteorological Satellite) NRSCC | Planned | 01 Jan 06 | 01 Jan 08 | Meteorology and environmental monitoring Data collection and redistribution | IRAS, MERSI, MWRI, MWTS, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| FY-3B (FY-3B Polar-orbiting Meteorological Satellite) NRSCC | Planned | 31 Dec 06 | 31 Dec 08 | Meteorology and environmental monitoring Data collection and redistribution | IRAS, MERSI, MWRI, MWTS, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| FY-3C (FY-3C Polar-orbiting Meteorological Satellite) NRSCC | Planned | 31 Dec 08 | 31 Dec 10 | Meteorology and environmental monitoring Data collection and redistribution | IMWTS, IRAS, MERSI, MIRAS, MWHS, MWRI, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| FY-3D (FY-3D Polar-orbiting Meteorological Satellite) NRSCC | Planned | 31 Dec 10 | 31 Dec 12 | Meteorology and environmental monitoring Data collection and redistribution | IMWTS, IRAS, MERSI, MIRAS, MWHS, MWRI, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| FY-3E (FY-3E Polar-orbiting Meteorological Satellite) NRSCC | Planned | 31 Dec 12 | 31 Dec 14 | Meteorology and environmental monitoring Data collection and redistribution | IMWTS, IRAS, MERSI, MIRAS, MWHS, MWRI, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| FY-3F (FY-3F Polar-orbiting Meteorological Satellite) NRSCC | Planned | 31 Dec 14 | 31 Dec 16 | Meteorology and environmental monitoring Data collection and redistribution | IMWTS, IRAS, MERSI, MIRAS, MWHS, MWRI, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| FY-3G (FY-3G Polar-orbiting Meteorological Satellite) NRSCC | Planned | 31 Dec 16 | 31 Dec 18 | Meteorology and environmental monitoring Data collection and redistribution | IMWTS, IRAS, MERSI, MIRAS, MWHS, MWRI, OP, TOM, VIRR | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| GCOM-C (Global Climate Observation Mission-C) JAXA | Considered | 01 Jan 10 | 01 Jan 15 | Atmospheric and terrestrial observation | GLI follow-on | Type: Sun-synchronous Altitude: 800 km Period: Inclination: Repeat cycle: LST: 1330 Longitude (if geo): Asc/desc: Descending URL: |
| GCOM-W (Global Climate Observation Mission-W) JAXA | Considered | 01 Jan 09 | 01 Jan 14 | Sea surface observation | AMSR follow-on, Scatterometer (JAXA) | Type: Sun-synchronous Altitude: 800 km Period: Inclination: Repeat cycle: LST: 1330 Longitude (if geo): Asc/desc: Descending URL: |
| Glory (Glory) NASA | Planned | 01 Dec 07 | 01 Dec 10 | Concentration and nature of both natural and anthropogenic aerosols (BC, sulfates, etc.) with accuracy and coverage sufficient for quantification of the aerosol effect on climate, the anthropogenic component of this effect, and the long-term change of this effect caused by natural and anthropogenic factors | APS, TIM | Type: Sun-synchronous Altitude: 824 km Period: 101 mins Inclination: 1030 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Descending URL: |
| GMS-5 (Geostationary Meteorogical Satellite - 5) JAXA | Currently being flown | 18 Mar 95 | 01 Jun 05 | Meteorology | DCS (JAXA), GMS Comms, VISSR (GMS-5) | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -140 Asc/desc: N/A URL: spaceinfo.jaxa.jp/db/kaihatu/eisei/eisei_e/gms_5_e.html |
| GOCE (Gravity Field and Steady-State Ocean Circulation Explorer (Earth Explorer Core Mission)) ESA | Approved | 15 Feb 06 | 15 Feb 08 | Research in steady-state ocean circulation, physics of Earth's interior and levelling systems (based on GPS). Will also provide unique data set required to formulate global and regional models of the Earth's gravity field and geoid. | EGG, GPS (ESA), Laser reflectors (ESA) | Type: Sun-synchronous Altitude: 250 km Period: Inclination: 96.5 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.esa.int/export/esaLP/goce.html |
| GOES-9 (Geostationary Operational Environmental Satellite - 9) NOAA | Currently being flown | 23 May 95 | 15 Jan 05 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection, platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 255 Asc/desc: N/A URL: www.oso.noaa.gov/goes/ |
| GOES-10 (Geostationary Operational Environmental Satellite - 10) NOAA | Currently being flown | 25 Apr 97 | 15 Jan 06 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 135 Asc/desc: N/A URL: www.oso.noaa.gov/goes/ |
| GOES-11 (Geostationary Operational Environmental Satellite - 11) NOAA | Currently being flown | 03 May 00 | 15 Jul 11 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 103 Asc/desc: N/A URL: www.oso.noaa.gov/goes/ |
| GOES-12 (Geostationary Operational Environmental Satellite - 12) NOAA | Currently being flown | 23 Jul 01 | 15 Jan 11 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, SXI, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 75 Asc/desc: N/A URL: www.oso.noaa.gov/goes/ |
| GOES-N (Geostationary Operational Environmental Satellite - N) NOAA | Approved | 12 Feb 05 | 12 Feb 17 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, SXI, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 75 Asc/desc: N/A URL: www.oso.noaa.gov/goes/ |
| GOES-O (Geostationary Operational Environmental Satellite - O) NOAA | Approved | 07 Apr 07 | 07 Apr 19 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 75 Asc/desc: TBD URL: www.oso.noaa.gov/goes/ |
| GOES-P (Geostationary Operational Environmental Satellite - P) NOAA | Approved | 15 Oct 08 | 15 Oct 20 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | DCS (NOAA), GOES Comms, Imager, S&R (GOES), SEM (GOES), Sounder, SXI, WEFAX | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 135 Asc/desc: TBD URL: www.oso.noaa.gov/goes/ |
| GOES-R (Geostationary Operational Environmental Satellite - R) NOAA | Approved | 31 Oct 12 | 31 Oct 20 | Meteorology (primary mission), search and rescue, space environment monitoring, data collection platform, data gathering, WEFAX | ABI, EHIS, EUVS, Geomicrowave sounder, GLM, HES, Magnetometer (NOAA), MPS, SGPS, SXI, SXS | Type: Geostationary Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): 135 Asc/desc: URL: www.osd.noaa.gov/goes_R/index.htm |
| GOSAT (Greenhouse gases Observing Satellite) JAXA | Planned | 01 Feb 08 | 01 Feb 13 | Observation of Greenhouse gases | Cloud Sensor, GHG Sensor | Type: Sun-synchronous Altitude: 666 km Period: 98 mins Inclination: 98 deg Repeat cycle: 3 days LST: Longitude (if geo): Asc/desc: TBD URL: www.jaxa.jp/missions/projects/sat/eos/gosat/index_e.html |
| GPM Constellation (Global Precipitation Measurement Mission Constellation spacecraft) NASA | Planned | 01 Nov 10 | 01 Nov 14 | Study of global precipitation, evaporation, and cycling of water are changing. The mission comprises a primary spacecraft with active and passive microwave instruments, and a number of ‘constellation spacecraft with passive microwave instruments. | GMI | Type: Inclined, non-sunsynchronous Altitude: 600 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: gpm.gsfc.nasa.gov/ |
| GPM Core (Global Precipitation Measurement Mission Core spacecraft) NASA | Planned | 01 Nov 09 | 01 Nov 13 | Study of global precipitation, evaporation, and cycling of water are changing. The mission comprises a primary spacecraft with active and passive microwave instruments, and a number of ‘constellation spacecraft with passive microwave instruments | DPR, GMI | Type: Inclined, non-sunsynchronous Altitude: 400 km Period: Inclination: 65 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: gpm.gsfc.nasa.gov/gpm.gsfc.nasa.gov/ |
| GRACE (Gravity Recovery and Climate Experiment) NASA | Currently being flown | 17 Mar 02 | 01 Mar 07 | Extremely high precision gravity measurements for use in construction of gravity field models | GPS (GRACE), HAIRS | Type: Inclined, non-sunsynchronous Altitude: 400 km Period: 94 mins Inclination: 89 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.csr.utexas.edu/grace/ |
| HJ-1A (Disaster and Environment Monitoring and Forecast Small Satellite A) CAST | Planned | 01 Dec 06 | 01 Dec 09 | Disaster and Environment Monitoring and Forecast | CCD (HJ, HY), HSI (HJ-1A) | Type: Sun-synchronous Altitude: 649 km Period: Inclination: 97.9 deg Repeat cycle: 31 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ |
| HJ-1B (Disaster and Environment Monitoring and Forecast Small Satellite B) CAST | Planned | 01 Dec 06 | 01 Dec 09 | Disaster and Environment Monitoring and Forecast | CCD (HJ, HY), IR (HJ-1B) | Type: Sun-synchronous Altitude: 649 km Period: Inclination: 97.9 deg Repeat cycle: 31 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ |
| HJ-1C (Disaster and Environment Monitoring and Forecast Small Satellite B) CAST | Planned | 01 May 07 | 01 May 10 | Disaster and Environment Monitoring and Forecast | S-band SAR | Type: Sun-synchronous Altitude: 499 km Period: Inclination: 97.3 deg Repeat cycle: 31 days LST: 600 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ |
| HY-1B (Ocean color satellite B) CAST | Planned | 01 Dec 06 | 01 Dec 09 | Detecting ocean color and sea surface temperature | COCTS, CZI | Type: Altitude: 798 km Period: Inclination: 98.6 deg Repeat cycle: 7 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.cast.cn/ |
| HYDROS (Hydrosphere State) NASA | Planned | 01 Dec 10 | 01 Dec 14 | Measure soil moisture content and freeze-thaw state | HYDROS | Type: Sun-synchronous Altitude: 670 km Period: Inclination: 98 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: hydros.gsfc.nasa.gov/ |
| Hyperspectral Mission (Hyperspectral Earth Observer) ASI | Considered | 01 Jan 09 | 31 Dec 14 | Land surface, agriculture and forestry, regional geology, land use studies, water resources, vegetation studies, coastal studies and soils | CIA, HYC | Type: Sun-synchronous Altitude: 620 km Period: 97 mins Inclination: 91.87 deg Repeat cycle: 16 days LST: 1000 Longitude (if geo): Asc/desc: Descending URL: www.ifac.cnr.it/ot/hyperspectral_workshop_2004.html |
| ICESat (Ice, Cloud, and Land Elevation Satellite) NASA | Currently being flown | 12 Jan 03 | 30 Jun 05 | Monitors mass balance of polar ice sheets and their contribution to global sea level change. Secondary goals: cloud heights and vertical structure of clouds/aerosols; roughness, reflectivity, vegetation heights, snow-cover. | GLAS | Type: Inclined, non-sunsynchronous Altitude: 600 km Period: 97 mins Inclination: 94 deg Repeat cycle: 183 days LST: Longitude (if geo): Asc/desc: N/A URL: icesat.gsfc.nasa.gov/ |
| IGPM ASI | Considered | 01 Jan 06 | 01 Jan 08 | To detect and measure rain and snowfall, to demonstrate the feasibility of high quality measurements of light rain and snow from space | IGPM radiometer, IGPM rain radar | Type: Sun-synchronous Altitude: 510 km Period: Inclination: Repeat cycle: LST: 1430 Longitude (if geo): Asc/desc: TBD URL: |
| INSAT-2E (Indian National Satellite - 2E) ISRO | Currently being flown | 03 Apr 99 | 04 Mar 11 | Meteorology, data collection and communication, search and rescue | CCD camera, VHRR | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -83 Asc/desc: TBD URL: www.isro.org/ |
| INSAT-3A (Indian National Satellite - 3A) ISRO | Currently being flown | 10 Apr 03 | 10 Apr 13 | Meteorology, data collection and communication, search and rescue | CCD camera, VHRR | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -94 Asc/desc: TBD URL: www.isro.org/ |
| INSAT-3D (Indian National Satellite - 3D) ISRO | Approved | 01 Jul 06 | 01 Jul 15 | Meteorology, data collection and communication, search and rescue | Imager (INSAT), Sounder (INSAT) | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -83 Asc/desc: TBD URL: www.isro.org/ |
| IRS-P4 (OCEANSAT-1) ISRO | Currently being flown | 26 May 99 | 31 Dec 06 | Ocean biology, physical oceanography | MSMR, OCM, WiFS | Type: Sun-synchronous Altitude: 720 km Period: 99.31 mins Inclination: 98.28 deg Repeat cycle: 2 days LST: 1215 Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| Jason (Ocean surface topography) NASA | Currently being flown | 07 Dec 01 | 01 Oct 07 | Physical oceanography, geodesy/gravity, climate monitoring, marine meteorology | DORIS-NG, JMR, LRA, POSEIDON-2 (SSALT-2), TRSR | Type: Inclined, non-sunsynchronous Altitude: 1336 km Period: 112.4 mins Inclination: 66 deg Repeat cycle: 10 days LST: Longitude (if geo): Asc/desc: N/A URL: topex-www.jpl.nasa.gov/mission/jason-1.html |
| Jason-2 (also known as OSTM) (Ocean Surface Topography Mission) NASA | Planned | 07 Dec 06 | 07 Dec 11 | Physical oceanography, geodesy/gravity, climate monitoring, marine meteorology | DORIS-NG, JMR, LRA, POSEIDON-3, TRSR | Type: Inclined, non-sunsynchronous Altitude: 1336 km Period: 112.4 mins Inclination: 66 deg Repeat cycle: 10 days LST: Longitude (if geo): Asc/desc: N/A URL: topex-www.jpl.nasa.gov/mission/mission.html |
| KALAPANA (Meteorological satellite) ISRO | Currently being flown | 09 Dec 02 | 09 Dec 12 | Meteorological applications | VHRR | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -83 Asc/desc: TBD URL: www.isro.org/ |
| Kanopus-Vulkan ROSKOSMOS | Planned | 01 Jan 06 | 31 Dec 11 | Hydrology, hydrometeorology, monitoring man-made and natural accidents, research into short-term forecasting of earthquakes | ECHO-V, GID-12T, MTVZA-OK, NVK, RBE, RCHA | Type: Sun-synchronous Altitude: 700 km Period: Inclination: 97 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.federalspace.ru |
| KOMPSAT-1 (Korea Multi-Purpose Satellite 1) KARI | Currently being flown | 21 Dec 99 | 21 Dec 05 | Cartography, land use and planning, disaster monitoring, Global marine resource and environmental monitoring, ocean contamination and chlorophyll detection | EOC, OSMI | Type: Sun-synchronous Altitude: 685 km Period: 98.5 mins Inclination: 28 deg Repeat cycle: 1050 days LST: Longitude (if geo): Asc/desc: Ascending URL: kompsat.kari.re.kr/english/index.asp |
| KOMPSAT-2 (Korea Multi-Purpose Satellite 2) KARI | Approved | 01 Oct 05 | 01 Oct 08 | Cartography, land use and planning, disaster monitoring | MSC | Type: Sun-synchronous Altitude: 685 km Period: 98.5 mins Inclination: 28 deg Repeat cycle: 1050 days LST: Longitude (if geo): Asc/desc: Ascending URL: kompsat.kari.re.kr/english/index.asp |
| LAGEOS-1 (Laser Geodynamics Satellite - 1) NASA | Currently being flown | 04 May 76 | 04 May 16 | Geodesy, crustal motion and gravity field measurements by laser ranging | LRA (LAGEOS) | Type: Inclined, non-sunsynchronous Altitude: 6000 km Period: 225 mins Inclination: 110 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: ilrs.gsfc.nasa.gov/satellite_missions/list_of_satellites/lagoes.html |
| LAGEOS-2 (Laser Geodynamics Satellite - 2) NASA | Currently being flown | 22 Oct 92 | 22 Oct 32 | Geodesy, crustal motion and gravity field measurements by laser ranging | LRA (LAGEOS) | Type: Inclined, non-sunsynchronous Altitude: 5900 km Period: 223 mins Inclination: 52 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: ilrs.gsfc.nasa.gov/satellite_missions/list_of_satellites/lagoes.htmlNASA\NASA_Agency_Missions1x2.doc |
| LAGEOS-3 (Laser Geodynamics Satellite - 3) NASA | Planned | 01 Jan 06 | 01 Jan 46 | Geodesy, crustal motion and gravity field measurements by laser ranging. Launch TBD - dates given are for illustration only. | LRA (LAGEOS) | Type: Inclined, non-sunsynchronous Altitude: 5900 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.laeff.esa.es/eng/laeff/activity/lageos3.html |
| Landsat-5 USGS | Currently being flown | 01 Mar 84 | 31 Dec 09 | Earth resources, land surface, environmental monitoring, agriculture and forestry, disaster monitoring and assessment, ice and snow cover | Landsat Comms, MSS, TM | Type: Sun-synchronous Altitude: 705 km Period: 98.9 mins Inclination: 98.2 deg Repeat cycle: 16 days LST: 945 Longitude (if geo): Asc/desc: Descending URL: landsat7.usgs.gov/ |
| Landsat-7 USGS | Currently being flown | 15 Apr 99 | 31 Dec 10 | Earth resources, land surface, environmental monitoring, agriculture and forestry, disaster monitoring and assessment, ice and snow cover | ETM+, Landsat Comms | Type: Sun-synchronous Altitude: 705 km Period: 98.8 mins Inclination: 98.2 deg Repeat cycle: 16 days LST: 1000 Longitude (if geo): Asc/desc: Descending URL: landsat7.usgs.gov/ |
| MEGHA-TROPIQUES CNES | Approved | 01 Jan 09 | 01 Jan 14 | Study of the inter-tropical zone and its convective systems (water and energy cycles). | MADRAS, SAPHIR, ScaRaB | Type: Sun-synchronous Altitude: 867 km Period: 100 mins Inclination: 20 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Descending URL: |
| METEOR-3M N1 ROSHYDROMET | Currently being flown | 10 Dec 01 | 31 Dec 05 | Hydrometeorology, climatology, land surface, physical oceanography, heliogeophysics and space environment, sounding of the atmosphere, agriculture. (Expected operational during 2002). | KGI-4C, Klimat, MIVZA, MR-2000M1, MSTE-5E, MSU-E, MSU-SM, MTVZA, SAGE III, SFM-2 | Type: Sun-synchronous Altitude: 1018 km Period: 105.3 mins Inclination: 99.6 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Ascending URL: sputnik1.infospace.ru/ |
| METEOR-3M N2 ROSHYDROMET | Approved | 01 Dec 05 | 31 Dec 09 | Hydrometeorology, climatology, land surface, physical oceanography, heliogeophysics and space environment, data collection, sounding of the atmosphere, agriculture | DCS (ROSHYDROMET), IKFS-2, KMSS, MSGI-MKA, MSU-MR, MTVZA, SAR (ROSHYDROMET) | Type: Sun-synchronous Altitude: 1024 km Period: 105.3 mins Inclination: 99.6 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Ascending URL: sputnik1.infospace.ru/ |
| Meteor-M No1 ROSHYDROMET | Planned | 01 Jan 05 | 01 Jan 12 | Meteorology, hydrology, climate and environmental monitoring | GALS-M, GGAK-M, IKFS-2, IKOR-M, KMSS, MSGI-MKA, MSS-BIO, MSU-MR, MTVZA, Radiomet, RIMS-M, SKL-M | Type: Sun-synchronous Altitude: 835 km Period: Inclination: 98.8 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.federalspace.ru |
| Meteor-M No2 ROSHYDROMET | Planned | 01 Jan 07 | 01 Jan 14 | Meteorology, hydrology, climate and environmental monitoring | GALS-M, GGAK-M, IKFS-2, IKOR-M, KMSS, MSGI-MKA, MSS-BIO, MSU-MR, MTVZA, Radiomet, RIMS-M, SKL-M | Type: Sun-synchronous Altitude: 835 km Period: Inclination: 98.8 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.federalspace.ru |
| METEOSAT-5 (Meteosat-5) EUMETSAT | Currently being flown | 02 Mar 91 | 31 Dec 05 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | METEOSAT Comms, MVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -63 Asc/desc: N/A URL: umetsat.de/en/dps/news/spacecraft.html |
| METEOSAT-6 (Meteosat-6) EUMETSAT | Currently being flown | 20 Nov 93 | 01 Jun 08 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | METEOSAT Comms, MVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 9 Asc/desc: N/A URL: www.eumetsat.de/en/dps/news/spacecraft.html |
| METEOSAT-7 (Meteosat-7) EUMETSAT | Currently being flown | 03 Sep 97 | 01 Jun 09 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | METEOSAT Comms, MVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 0 Asc/desc: N/A URL: www.eumetsat.de/en/mtp/index.html |
| METEOSAT-8 (Meteosat Second Generation-1) EUMETSAT | Currently being flown | 13 Aug 02 | 13 Aug 09 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | GERB, MSG Comms, SEVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 0 Asc/desc: N/A URL: www.eumetsat.de/en/area4/topic1.html |
| METEOSAT-9 (Meteosat Second Generation-2) EUMETSAT | Approved | 01 Jun 05 | 01 Jun 12 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | GERB, MSG Comms, SEVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 0 Asc/desc: N/A URL: www.eumetsat.de/en/area4/topic1.html |
| METEOSAT-10 (Meteosat Second Generation-3) EUMETSAT | Approved | 01 Jun 08 | 01 Jun 15 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | GERB, MSG Comms, SEVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 0 Asc/desc: N/A URL: www.eumetsat.de/en/area4/topic1.html |
| METEOSAT-11 (Meteosat Second Generation-4) EUMETSAT | Approved | 01 Dec 11 | 01 Dec 18 | Meteorology, climatology, Atmospheric dynamics/water and energy cycles. Meteosat 1-7 are first generation. Meteosat 8-11 are second generation and known as MSG in the development phase | GERB, MSG Comms, SEVIRI | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): 0 Asc/desc: N/A URL: www.eumetsat.de/en/area4/topic1.html |
| METOP-1 (Meteorological Operational Polar Satellite - 1) EUMETSAT | Approved | 01 Dec 05 | 01 Dec 10 | Meteorology, climatology | AMSU-A, ARGOS, ASCAT, AVHRR/3, GOME-2, GRAS, HIRS/4, IASI, MCP, MHS, S&R (NOAA) | Type: Sun-synchronous Altitude: 840 km Period: 101.7 mins Inclination: 98.8 deg Repeat cycle: 5 days LST: 930 Longitude (if geo): Asc/desc: Descending URL: www.eumetsat.de/en/area4/topic2.html |
| METOP-2 (Meteorological Operational Polar Satellite - 2) EUMETSAT | Approved | 31 Dec 09 | 31 Dec 14 | Meteorology, climatology | AMSU-A, ARGOS, ASCAT, AVHRR/3, GOME-2, GRAS, HIRS/4, IASI, MCP, MHS, S&R (NOAA), SEM (POES) | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: 930 Longitude (if geo): Asc/desc: N/A URL: www.eumetsat.de/en/area4/topic2.html |
| METOP-3 (Meteorological Operational Polar Satellite - 3) EUMETSAT | Approved | 01 Jun 14 | 01 Jun 19 | Meteorology, climatology | AMSU-A, ARGOS, ASCAT, AVHRR/3, GOME-2, GRAS, HIRS/4, IASI, MCP, MHS | Type: Sun-synchronous Altitude: 840 km Period: 101.7 mins Inclination: 98.8 deg Repeat cycle: 5 days LST: 930 Longitude (if geo): Asc/desc: Descending URL: www.eumetsat.de/en/area4/topic2.html |
| Monitor-E ROSKOSMOS | Planned | 01 Apr 05 | 31 Dec 10 | Agriculture and forestry, hydrology, environmental monitoring, hydrometeorology, ice and snow, land surface, meteorology | PSA, RDSA | Type: Sun-synchronous Altitude: 540 km Period: Inclination: 97.5 deg Repeat cycle: LST: 540 Longitude (if geo): Asc/desc: TBD URL: www.federalspace.ru |
| MTSAT-1R (Multi-functional Transport Satellite) JMA | Approved | 01 Feb 05 | 31 Dec 10 | Meteorology, aeronautical applications | IMAGER/MTSAT-1R, MTSAT Comms | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -140 Asc/desc: N/A URL: |
| MTSAT-2 (Multi-functional Transport Satellite) JMA | Approved | 01 Feb 06 | 31 Dec 15 | Meteorology, aeronautical applications | IMAGER/MTSAT-2, MTSAT Comms | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -140 Asc/desc: N/A URL: |
| NMP EO-1 (New Millenium Program Earth Observing-1) NASA | Currently being flown | 21 Nov 00 | 30 Sep 05 | Land surface, earth resources | ALI, Hyperion, LAC | Type: Sun-synchronous Altitude: 705 km Period: 99 mins Inclination: 98.2 deg Repeat cycle: 16 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: eo1.gsfc.nasa.gov/ |
| NMP EO-3 GIFTS (New Millenium Program EO-3 - Geosynchronous Imaging Fourier Transform Spectrometer - (GIFTS)) NASA | Considered | 01 Oct 06 | 01 Oct 08 | Continuous observation of atmospheric temperature, water vapour content and distribution, and the concentration of certain other atmospheric gases as a function of altitude over time - providing a new way to observe weather and the changing atmosphere. | GIFTS | Type: Geostationary Altitude: 36000 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): -83 Asc/desc: N/A URL: nmp.jpl.nasa.gov/eo3/index.html |
| NOAA-12 (National Oceanic and Atmospheric Administration - 12) NOAA | Currently being flown | 14 May 91 | 31 Dec 05 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, total ozone studies, space environment, solar flux analysis | ARGOS, AVHRR/2, HIRS/2, MSU, NOAA Comms, SEM (POES), SSU | Type: Sun-synchronous Altitude: 850 km Period: 101.3 mins Inclination: 98.5 deg Repeat cycle: LST: 449 Longitude (if geo): Asc/desc: Descending URL: www.oso.noaa.gov/poes/ |
| NOAA-14 (National Oceanic and Atmospheric Administration - 14) NOAA | Currently being flown | 30 Dec 94 | 31 Dec 05 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, total ozone studies, space environment, solar flux analysis | ARGOS, AVHRR/2, HIRS/2, MSU, NOAA Comms, S&R (NOAA), SBUV/2, SEM (POES), SSU | Type: Sun-synchronous Altitude: 850 km Period: 102.1 mins Inclination: 99.1 deg Repeat cycle: LST: 1752 Longitude (if geo): Asc/desc: Ascending URL: www.oso.noaa.gov/poes/ |
| NOAA-15 (National Oceanic and Atmospheric Administration - 15) NOAA | Currently being flown | 01 May 98 | 31 Dec 06 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, space environment, solar flux analysis, search and rescue | AMSU-A, AMSU-B, ARGOS, AVHRR/3, HIRS/3, NOAA Comms, S&R (NOAA), SBUV/2, SEM (POES) | Type: Sun-synchronous Altitude: 813 km Period: 101.4 mins Inclination: 98.6 deg Repeat cycle: LST: 708 Longitude (if geo): Asc/desc: Descending URL: www.oso.noaa.gov/poes/ |
| NOAA-16 (National Oceanic and Atmospheric Administration - 16) NOAA | Currently being flown | 21 Sep 00 | 31 Dec 06 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, total ozone studies, space environment, solar flux analysis, search and rescue | AMSU-A, AMSU-B, ARGOS, AVHRR/3, HIRS/3, NOAA Comms, S&R (NOAA), SBUV/2, SEM (POES) | Type: Sun-synchronous Altitude: 870 km Period: 102 mins Inclination: 98.8 deg Repeat cycle: LST: 1354 Longitude (if geo): Asc/desc: Ascending URL: www.oso.noaa.gov/poes/ |
| NOAA-17 (National Oceanic and Atmospheric Administration - M) NOAA | Currently being flown | 24 Jun 02 | 01 Mar 06 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, total ozone studies, space environment, solar flux analysis, search and rescue | AMSU-A, AMSU-B, ARGOS, AVHRR/3, HIRS/3, NOAA Comms, S&R (NOAA), SBUV/2, SEM (POES) | Type: Sun-synchronous Altitude: 833 km Period: 101.4 mins Inclination: 98.75 deg Repeat cycle: LST: 1000 Longitude (if geo): Asc/desc: Descending URL: www.oso.noaa.gov/poes/ |
| NOAA-N (National Oceanic and Atmospheric Administration - N) NOAA | Approved | 11 Feb 05 | 30 Nov 08 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, total ozone studies, space environment, solar flux analysis, search and rescue | AMSU-A, ARGOS, AVHRR/3, HIRS/4, MHS, NOAA Comms, S&R (NOAA), SBUV/2, SEM (POES) | Type: Sun-synchronous Altitude: 870 km Period: 102.1 mins Inclination: 98.75 deg Repeat cycle: LST: 1400 Longitude (if geo): Asc/desc: Ascending URL: www.oso.noaa.gov/poes/ |
| NOAA-N' (National Oceanic and Atmospheric Administration - N') NOAA | Approved | 30 Nov 08 | 01 Dec 11 | Meteorology, agriculture and forestry, environmental monitoring, climatology, physical oceanography, Volcanic eruption monitoring, ice and snow cover, total ozone studies, space environment, solar flux analysis, search and rescue | AMSU-A, ARGOS, AVHRR/3, HIRS/4, MHS, NOAA Comms, S&R (NOAA), SBUV/2, SEM (POES) | Type: Sun-synchronous Altitude: 870 km Period: 102.1 mins Inclination: 98.75 deg Repeat cycle: LST: 1400 Longitude (if geo): Asc/desc: Ascending URL: www.oso.noaa.gov/poes/ |
| NPOESS-1 (National Polar-orbiting Operational Environmental Satellite System - 1) NOAA | Approved | 30 Nov 09 | 01 Nov 15 | Meteorological, climatic, terrestrial, oceanographic, and solar-geophysical applications; global and regional environmental monitoring, search and rescue, data collection. | A-DCS, APS, CMIS, SARSAT, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.75 deg Repeat cycle: 2130 days LST: Longitude (if geo): Asc/desc: Ascending URL: www.npoess.noaa.gov/ |
| NPOESS-2 (National Polar-orbiting Operational Environmental Satellite System - 2) NOAA | Approved | 30 Jun 11 | 01 Jun 17 | Meteorological, climatic, terrestrial, oceanographic, and solar-geophysical applications; global and regional environmental monitoring, search and rescue, data collection. | A-DCS, ATMS, CERES, CMIS, CrIS, OMPS, S&R (NOAA), SARSAT, SESS, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.75 deg Repeat cycle: 1330 days LST: Longitude (if geo): Asc/desc: Ascending URL: www.npoess.noaa.gov/ |
| NPOESS-3 (National Polar-orbiting Operational Environmental Satellite System - 3) NOAA | Approved | 04 Jun 13 | 09 Jun 18 | Meteorological, climatic, terrestrial, oceanographic, and solar-geophysical applications; global and regional environmental monitoring, search and rescue, data collection. | A-DCS, ALT, CMIS, ERBS, S&R (NOAA), SARSAT, SESS, TSIS, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.75 deg Repeat cycle: 1730 days LST: Longitude (if geo): Asc/desc: Ascending URL: www.npoess.noaa.gov/ |
| NPOESS-4 (National Polar-orbiting Operational Environmental Satellite System - 4) NOAA | Approved | 01 Nov 15 | 06 Nov 20 | Meteorological, climatic, terrestrial, oceanographic, and solar-geophysical applications; global and regional environmental monitoring, search and rescue, data collection. | A-DCS, APS, CMIS, SARSAT, SESS, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.75 deg Repeat cycle: 2130 days LST: Longitude (if geo): Asc/desc: Ascending URL: www.npoess.noaa.gov/ |
| NPOESS-5 (National Polar-orbiting Operational Environmental Satellite System - 4) NOAA | Approved | 01 Jan 18 | 01 Jun 23 | Meteorological, climatic, terrestrial, oceanographic, and solar-geophysical applications; global and regional environmental monitoring, search and rescue, data collection. | A-DCS, ATMS, CERES, CMIS, CrIS, OMPS, S&R (NOAA), SARSAT, SESS, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.75 deg Repeat cycle: 1330 days LST: Longitude (if geo): Asc/desc: Ascending URL: www.npoess.noaa.gov/ |
| NPOESS-6 (National Polar-orbiting Operational Environmental Satellite System - 4) NOAA | Approved | 09 May 19 | 01 May 24 | Meteorological, climatic, terrestrial, oceanographic, and solar-geophysical applications; global and regional environmental monitoring, search and rescue, data collection. | A-DCS, ALT, CMIS, ERBS, S&R (NOAA), SARSAT, SESS, TSIS, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 98.75 deg Repeat cycle: 1730 days LST: Longitude (if geo): Asc/desc: Ascending URL: www.npoess.noaa.gov/ |
| NPP (NPOESS (National Polar-orbiting Operational Environmental Satellite System) Preparatory Project) NOAA | Approved | 31 Oct 06 | 26 Oct 11 | Meteorological, climatic, terrestrial, and oceanographic applications; global and regional environmental monitoring. (Joint mission with NASA) | ATMS, CrIS, OMPS, VIIRS | Type: Sun-synchronous Altitude: 833 km Period: 101 mins Inclination: 1030 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: Descending URL: jointmission.gsfc.nasa.gov/ |
| OCEANSAT-2 (Ocean satellite-2) ISRO | Planned | 01 Jan 07 | 01 Jan 11 | Ocean and atmosphere applications | OCM, Scatterometer (ISRO) | Type: Sun-synchronous Altitude: 720 km Period: 99.31 mins Inclination: 98.28 deg Repeat cycle: 2 days LST: 1200 Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| OCO (Orbiting Carbon Observatory) NASA | Planned | 01 Aug 07 | 01 Aug 09 | High resolution carbon dioxide measurements to characterize sources and sinks on regional scales and quantify their variability over the seasonal cycle | OCO | Type: Sun-synchronous Altitude: 705 km Period: 98.8 mins Inclination: 98.2 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: essp.gsfc.nasa.gov/oco/index.html |
| Odin SNSB | Currently being flown | 20 Feb 01 | 30 Mar 05 | Atmospheric research, stratospheric ozone chemistry, mesospheric ozone science, summer mesospheric science | OSIRIS, SMR | Type: Sun-synchronous Altitude: 590 km Period: 97.6 mins Inclination: 97.8 deg Repeat cycle: LST: 1800 Longitude (if geo): Asc/desc: Ascending URL: www.ssc.se |
| PARASOL (Polarization and Anisotropy of Reflectances for Atmospheric Science coupled with Observations from a LIDAR) CNES | Approved | 10 Dec 04 | 01 Dec 06 | Micro-satellite with the aim of characterisation of the clouds and aerosols microphysical and radiative properties, needed to understand and model the radiative impact of clouds and aerosols. | POLDER-P | Type: Sun-synchronous Altitude: 700 km Period: 98.8 mins Inclination: Repeat cycle: LST: 1200 Longitude (if geo): Asc/desc: TBD URL: smsc.cnes.fr/PARASOL/index.htm |
| PICARD CNES | Approved | 06 Jan 08 | 01 Aug 10 | Simultaneous measurements of solar diameter, differential rotation, solar constant, and variability. | PREMOS, SODISM, SOVAP | Type: TBD Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www-projet.cst.cnes.fr:8060/PICARD/index.html |
| Pleiades 1 CNES | Approved | 01 Jul 08 | 01 Jul 13 | Cartography, land use, risk, agriculture and forestry, civil planning and mapping, digital terrain models, defence | Pleiades HR | Type: Sun-synchronous Altitude: 694 km Period: Inclination: Repeat cycle: 26 days LST: 1015 Longitude (if geo): Asc/desc: Descending URL: smsc.cnes.fr/PLEIADES/Fr/index.htm |
| Pleiades 2 CNES | Approved | 31 Dec 09 | 31 Dec 14 | Cartography, land use, risk,agriculture and forestry, civil planning and mapping, digital terrain models, defense | Pleiades HR | Type: Sun-synchronous Altitude: 694 km Period: Inclination: Repeat cycle: LST: 1015 Longitude (if geo): Asc/desc: Descending URL: smsc.cnes.fr/PLEIADES/Fr/index.htm |
| QuikSCAT (Quick Scatterometer) NASA | Currently being flown | 19 Jun 99 | 01 Oct 07 | Acquires accurate, high-resolution, global measurements of sea-surface wind vectors in 1 to 2 day repeat cycles for studies of tropospheric dynamics and air-sea interaction processes, including air-sea momentum transfer. End of life date TBD. | SeaWinds | Type: Sun-synchronous Altitude: 803 km Period: 101 mins Inclination: 98.6 deg Repeat cycle: LST: 600 Longitude (if geo): Asc/desc: Ascending URL: winds.jpl.nasa.gov/missions/quikscat/index.cfm |
| RADARSAT-1 (Radar satellite-1) CSA | Currently being flown | 04 Nov 95 | 31 Dec 05 | Environmental monitoring, physical oceanography, ice and snow, land surface | RADARSAT DTT, RADARSAT TTC, SAR (RADARSAT) | Type: Sun-synchronous Altitude: 798 km Period: 100.7 mins Inclination: 98.594 deg Repeat cycle: 24 days LST: 1800 Longitude (if geo): Asc/desc: Ascending URL: www.space.gc.ca/csa_sectors/earth_environment/radarsat/default.asp |
| RADARSAT-2 (Radar satellite-2) CSA | Approved | 31 Dec 05 | 31 Dec 12 | Environmental monitoring, physical oceanography, ice and snow, land surface | SAR (RADARSAT-2) | Type: Sun-synchronous Altitude: 798 km Period: 100.7 mins Inclination: 98.6 deg Repeat cycle: 24 days LST: 1800 Longitude (if geo): Asc/desc: Ascending URL: www.space.gc.ca/csa_sectors/earth_environment/radarsat2/default.asp |
| RapidEye (RapidEye) DLR | Approved | 01 Jan 07 | 01 Jan 14 | System of 5 satellites for cartography, land surface, digital terrain models, disaster management, environmental monitoring. | MSI | Type: Sun-synchronous Altitude: 600 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.rapideye.de/ |
| RESOURCESAT-1 (Resource satellite-1) ISRO | Currently being flown | 01 Oct 03 | 01 Oct 08 | Natural Resources Management; Agricultural applications; Forestry | AWiFS, LISS-III, LISS-IV | Type: Sun-synchronous Altitude: 817 km Period: 102 mins Inclination: 98.72 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| RESOURCESAT-2 (Resource satellite-2) ISRO | Planned | 01 Jul 06 | 01 Jul 11 | Natural Resources Management; Agricultural applications; Forestry | AWiFS, LISS-III, LISS-IV | Type: Sun-synchronous Altitude: 817 km Period: 102 mins Inclination: 98.72 deg Repeat cycle: 26 days LST: Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| Resurs DK ROSKOSMOS | Planned | 01 Jun 05 | 31 Dec 08 | Agriculture and forestry, hydrology, environmental monitoring, hydrometeorology, ice and snow, land surface, meteorology | Arina, Geoton-L1, Pamela | Type: Inclined, non-sunsynchronous Altitude: 480 km Period: Inclination: 70.4 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: sputnik1.infospace.ru/ |
| RISAT-1 (Radar Imaging Satellite) ISRO | Approved | 01 Jul 06 | 01 Jul 11 | Land surface, agriculture and forestry, regional geology, land use studies, water resources, vegetation studies, coastal studies and soils - Specially during cloud season | SAR (RISAT) | Type: Sun-synchronous Altitude: 586 km Period: 96.5 mins Inclination: 12 deg Repeat cycle: 600 days LST: Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| SAC-C CONAE | Currently being flown | 21 Nov 00 | 31 Dec 05 | Earth Observation, studies the structure and dynamics of the Earth’s surface, atmosphere, ionosphere and geomagnetic field. | GOLPE, HRTC, HSTC, ICARE, INES, IST, MMP, MMRS, WTE | Type: Sun-synchronous Altitude: 705 km Period: 98 mins Inclination: 98.2 deg Repeat cycle: 9 days LST: 1015 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAC-D/Aquarius CONAE | Approved | 11 Sep 08 | 11 Sep 11 | Earth observation studies; measurement of ocean salinity; emergency management | Aquarius, HSC, ICARE, MWR (CONAE), NIRST, ROSA, SODAD | Type: Sun-synchronous Altitude: 705 km Period: 98 mins Inclination: 98.2 deg Repeat cycle: 9 days LST: 1015 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAC-E/SABIA CONAE | Planned | 21 Nov 09 | 01 Dec 14 | Food production;environmental monitoring; inner coastal and water quality | MOC | Type: Sun-synchronous Altitude: 705 km Period: 98 mins Inclination: 98.2 deg Repeat cycle: 9 days LST: 1015 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAC-F CONAE | Planned | 21 Nov 07 | 01 Dec 11 | Earth observation studies; emergency management;landscape epidemiology | HRMS, HSMS, HSS, TIS (CONAE) | Type: Sun-synchronous Altitude: 705 km Period: 98 mins Inclination: 98.2 deg Repeat cycle: 9 days LST: 1015 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAOCOM 1A CONAE | Approved | 01 Oct 07 | 01 Oct 11 | Earth Observation and Emergency management with an L-band SAR | IR Camera (SAOCOM), SAR (SAOCOM) | Type: Sun-synchronous Altitude: 629 km Period: 96 mins Inclination: 98 deg Repeat cycle: 16 days LST: 600 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAOCOM 1B CONAE | Approved | 01 Oct 08 | 01 Oct 12 | Earth Observation and Emergency management with an L-band SAR | IR Camera (SAOCOM), SAR (SAOCOM) | Type: Sun-synchronous Altitude: 629 km Period: 96 mins Inclination: 98 deg Repeat cycle: 16 days LST: 600 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAOCOM-2B (1) CONAE | Planned | 01 Oct 13 | 01 Oct 17 | Earth Observation and Emergency management with an L-band SAR | IR Camera (SAOCOM), SAR (SAOCOM) | Type: Sun-synchronous Altitude: 629 km Period: 96 mins Inclination: 98 deg Repeat cycle: 16 days LST: 600 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SAOCOM-2B (2) CONAE | Planned | 01 Oct 12 | 01 Oct 16 | Earth Observation and Emergency management with an L-band SAR | IR Camera (SAOCOM), SAR (SAOCOM) | Type: Sun-synchronous Altitude: 629 km Period: 96 mins Inclination: 98 deg Repeat cycle: 16 days LST: 600 Longitude (if geo): Asc/desc: Descending URL: www.conae.gov.ar/ |
| SCD-1 (Data Collecting Satellite 1) INPE | Currently being flown | 09 Feb 93 | 01 Dec 05 | Data collection and communication | DCP (SCD) | Type: Inclined, non-sunsynchronous Altitude: 750 km Period: 100 mins Inclination: 25 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.inpe.br/programas/mecb/default.htm |
| SCD-2 (Data Collecting Satellite 2) INPE | Currently being flown | 22 Oct 98 | 01 Dec 05 | Data collection and communication | DCP (SCD) | Type: Inclined, non-sunsynchronous Altitude: 750 km Period: 100 mins Inclination: 25 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.inpe.br/programas/mecb/default.htm |
| SCISAT-1 (SCISAT-I/ACE) CSA | Currently being flown | 12 Aug 03 | 20 Dec 07 | To improve our understanding of the depletion of the ozone layer, particularly over Canada and the Arctic. | ACE-FTS, MAESTRO | Type: Sun-synchronous Altitude: 650 km Period: Inclination: 74 deg Repeat cycle: 15 days LST: Longitude (if geo): Asc/desc: TBD URL: www.space.gc.ca/scisat1 |
| SICH-1M NSAU | Approved | 31 Dec 04 | 31 Dec 07 | Physical Oceanography, Hydrometeorology, Land Observation | MSU-EU, MSU-M, MTVZA-OK, RLSBO, RM-08 | Type: Inclined, non-sunsynchronous Altitude: 650 km Period: 98 mins Inclination: 82.5 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: |
| SICH-2 NSAU | Planned | 31 Dec 05 | 31 Dec 10 | Land Observation | MBEI, MIREI | Type: Sun-synchronous Altitude: 668 km Period: 98 mins Inclination: 98 deg Repeat cycle: 4 days LST: 1050 Longitude (if geo): Asc/desc: TBD URL: |
| SMOS (Soil Moisture and Ocean Salinity (Earth Explorer Opportunity Mission)) ESA | Approved | 15 Feb 07 | 15 Feb 10 | Overall objectives are to provide global observations of two crucial variables for modelling the weather and climate, Soil Moisture and Ocean Salinity. It will also monitor the vegetation water content, snow cover and ice structure. | MIRAS (SMOS) | Type: Sun-synchronous Altitude: 756 km Period: Inclination: 98.45 deg Repeat cycle: 165 days LST: 600 Longitude (if geo): Asc/desc: Ascending URL: www.esa.int/export/esaLP/smos.html |
| SORCE (Solar Radiation and Climate Experiment) NASA | Currently being flown | 25 Jan 03 | 25 Jan 09 | Continues the precise, long-term measurements of total solar irradiance at UV and VNIR wavelengths. Daily measurements of solar UV. Precise measurements of visible solar irradiance for climate studies. | SIM, SOLSTICE, TIM, XPS | Type: Inclined, non-sunsynchronous Altitude: 600 km Period: Inclination: 40 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: lasp.colorado.edu/sorce/ |
| SPOT-2 (Satellite Pour l'Observation de la Terre - 2) CNES | Currently being flown | 22 Jan 90 | 31 Dec 05 | Cartography, land surface, agriculture and forestry, civil planning and mapping, digital terrain models, environmental monitoring | DORIS, HRV | Type: Sun-synchronous Altitude: 832 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.spotimage.fr/html/_167_224_229_.php |
| SPOT-4 (Satellite Pour l'Observation de la Terre - 4) CNES | Currently being flown | 24 Mar 98 | 31 Dec 05 | Cartography, land surface, agriculture and forestry, civil planning and mapping, digital terrain models, environmental monitoring | DORIS, HRVIR, VEGETATION | Type: Sun-synchronous Altitude: 832 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.spotimage.fr/html/_167_224_229_.php |
| SPOT-5 (Satellite Pour l'Observation de la Terre - 5) CNES | Currently being flown | 04 May 02 | 04 May 07 | Cartography, land surface, agriculture and forestry, civil planning and mapping, digital terrain models, environmental monitoring | DORIS-NG, HRG, HRS, VEGETATION | Type: Sun-synchronous Altitude: 832 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: 26 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: www.spotimage.fr/html/_167_224_229_.php |
| SSR-1 (Remote Sensing Satellite 1) INPE | Approved | 01 Dec 07 | 01 Dec 11 | Earth resources, environmental monitoring, land surface | OBA | Type: Inclined, non-sunsynchronous Altitude: 905 km Period: 103.2 mins Inclination: 0 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: www.inpe.br/programas/mecb/default.htm |
| SSR-2 (Remote Sensing Satellite 2) INPE | Planned | 01 Dec 12 | 01 Dec 15 | Earth resources, environmental monitoring, land surface | L-band SAR, OBA | Type: Inclined, non-sunsynchronous Altitude: 905 km Period: 103 mins Inclination: 0 deg Repeat cycle: 16 days LST: Longitude (if geo): Asc/desc: TBD URL: www.inpe.br/programas/mecb/default.htm |
| STARLETTE CNES | Currently being flown | 06 Feb 75 | 31 Dec 50 | Geodesy/gravity Study of the Earth’s gravitational field and its temporal variations | Laser reflectors | Type: Inclined, non-sunsynchronous Altitude: 812 km Period: 104 mins Inclination: 49.83 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: |
| STELLA CNES | Currently being flown | 30 Sep 93 | 31 Dec 50 | Geodesy/gravity Study of the Earth’s gravitational field and its temporal variations | Laser reflectors | Type: Inclined, non-sunsynchronous Altitude: 830 km Period: 101 mins Inclination: 98 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: |
| Swarm (Earth's Magnetic Field and Environment Exploreres; Constellation of three satellites) ESA | Approved | 01 Jan 09 | 01 Jan 13 | To provide the best ever survey of the geomagnetic field and its temporal evolution, and gain new insights into improving our knowledge of the Earth’s interior and climate. | ACC, ASM, EFI, GPS (ESA), STR, VFM | Type: Inclined, non-sunsynchronous Altitude: 450 km Period: Inclination: 87.4 deg Repeat cycle: LST: 600 Longitude (if geo): Asc/desc: URL: www.esa.int/export/esaLP/swarm.html |
| Terra (Terra (formerly EOS AM-1)) NASA | Currently being flown | 18 Dec 99 | 18 Dec 05 | Atmospheric dynamics/water and energy cycles, Atmospheric chemistry, Physical and radiative properties of clouds, airland exchanges of energy, carbon and water, vertical profiles of CO and methane vulcanology | ASTER, CERES, MISR, MODIS, MOPITT | Type: Sun-synchronous Altitude: 705 km Period: 99 mins Inclination: 98.2 deg Repeat cycle: 16 days LST: 1030 Longitude (if geo): Asc/desc: Descending URL: terra.nasa.gov/ |
| TerraSAR-L (TerraSAR L band) BNSC | Considered | 01 Jan 06 | 01 Jan 11 | SAR imagery in support of agriculture, forestry etc. | L-SAR | Type: TBD Altitude: 660 km Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.infoterra-global.com/terrasar.html |
| TerraSAR-X (TerraSAR-X) DLR | Approved | 27 Oct 05 | 01 Mar 11 | Cartography, land surface, civil planning and mapping, digital terrain models, environmental monitoring. | TerraSAR-X | Type: Sun-synchronous Altitude: 514 km Period: 94.85 mins Inclination: 97.4 deg Repeat cycle: 11 days LST: 1800 Longitude (if geo): Asc/desc: Ascending URL: www.terrasar.de/ |
| TES (Technology Experimental Satellite) ISRO | Currently being flown | 22 Oct 01 | 31 Dec 05 | For demonstrating many satellite technologies for future Cartosat satellites |  | Type: Sun-synchronous Altitude: Period: Inclination: Repeat cycle: LST: Longitude (if geo): Asc/desc: Descending URL: www.isro.org/ |
| THEOS (Thailand Earth Observation System) GISTDA | Approved | 01 Jul 07 | 01 Jul 12 | Earth Resources, Land surface and Disaster Monitoring, Civil Planning | MS (GISTDA), PAN (GISTDA) | Type: Sun-synchronous Altitude: 822 km Period: 101 mins Inclination: 98.7 deg Repeat cycle: 35 days LST: 1000 Longitude (if geo): Asc/desc: Descending URL: www.gistda.or.th |
| TIMED (Thermosphere Ionosphere Mesosphere Energetics and Dynamics mission) NASA | Currently being flown | 07 Dec 01 | 07 Dec 20 | Investigates the influences of the sun and humans on the least explored and understood region of the Earth's atmosphere - the mesosphere and lower thermosphere/ionosphere (MLTI) | SABER | Type: Inclined, non-sunsynchronous Altitude: 625 km Period: Inclination: 74.1 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.timed.jhuapl.edu/ |
| Topex-Poseidon (Topographic Experiment/Poseidon) NASA | Currently being flown | 10 Aug 92 | 01 Oct 05 | Physical oceanography, geodesy/gravity | DORIS, GPSDR, LRA, POSEIDON-1 (SSALT-1), TMR, TOPEX | Type: Inclined, non-sunsynchronous Altitude: 1336 km Period: 112.4 mins Inclination: 66 deg Repeat cycle: 10 days LST: Longitude (if geo): Asc/desc: N/A URL: topex-www.jpl.nasa.gov/mission/tp-launch.html |
| TopSat (Optical Imaging Satellite) BNSC | Approved | 01 May 05 | 01 May 06 | Prototype low-cost high-resolution imager | TOPSAT telescope | Type: Sun-synchronous Altitude: 600 km Period: Inclination: 98 deg Repeat cycle: LST: 1030 Longitude (if geo): Asc/desc: TBD URL: www.qinetiq.com/industries/space/spacecraft_technology/case_study_topsat/index.asp |
| UARS (Upper Atmosphere Research Satellite) NASA | Currently being flown | 15 Sep 91 | 30 Apr 05 | Atmospheric chemistry (middle to upper atmosphere), atmospheric dynamics/water and energy cycles. HALOE, HRDI, MLS, PEM instruments still functioning. End date TBD. | ACRIM II, CLAES, HALOE, HRDI, ISAMS, PEM, SOLSTICE, SUSIM (UARS), WINDII | Type: Inclined, non-sunsynchronous Altitude: 585 km Period: 95.9 mins Inclination: 57 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: N/A URL: umpgal.gsfc.nasa.gov/uars-science.html |
| UK-DMC (UK Disaster Monitoring Constellation) BNSC | Currently being flown | 27 Sep 03 | 31 Dec 06 | Medium resolution visible imager for support of disaster management | DMC Imager | Type: TBD Altitude: 785 km Period: Inclination: 98.2 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: TBD URL: www.sstl.co.uk/index.php?loc=113 |
| Vulkan-Kompas-2 ROSKOSMOS | Planned | 01 Jan 05 | 31 Dec 06 | Monitoring of Earth's seismic activity for earthquake and volcanic eruption forecasting | DRF, GID-12T, NVK, RBE, RCHA | Type: Inclined, non-sunsynchronous Altitude: 500 km Period: Inclination: 79 deg Repeat cycle: LST: Longitude (if geo): Asc/desc: URL: www.federalspace.ru |

| AATSR Advanced Along-Track Scanning Radiometer BNSC | Envisat | Operational | Imaging multi-spectral radiometers (vis/IR) & Multiple direction/polarisation radiometers | Measurements of sea surface temperature, land surface temperature, cloud top temperature, cloud cover, aerosols, vegetation, atmospheric water vapour and liquid water content | Waveband: VIS - NIR: 0.555, 0.659, 0.865µm, SWIR: 1.6µm, MWIR: 3.7µm, TIR: 10.85, 12µm Spatial resolution: IR ocean channels: 1km x 1km, Visible land channels: 1km x 1km Swath width: 500 km Accuracy: Sea surface temperature: <0.5K over 0.5 deg x 0.5 deg (lat/long) area with 80% cloud cover Land surface temperature: 0.1K (relative) |
| --- | --- | --- | --- | --- | --- |
| ABI Advanced Baseline Imager NOAA | GOES-R | Approved | Imaging multi-spectral radiometers (vis/IR) | Measures cloud cover, atmospheric radiance, winds, atmospheric stability, rainfall estimates. Used to provide severe storm warnings/ monitoring day and night (type, amount, storm features) | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| ACC Accelerometer ESA | Swarm | Operational | Gravity & Space environment | Measures the non-gravitational accelerations, caused for example by air-drag, winds, Earth albedo and solar radiation pressure acting on the satellites. In-situ air density measurements together with magnetic data can be used to obtain new insights on the geomagnetic forcing of the upper atmosphere. | Waveband: N/A Spatial resolution: 0.1nm/s2 Swath width: N/A Accuracy: 0.1nm/s2 |
| ACE-FTS Atmospheric Chemistry Experiment (ACE) mission CSA | SCISAT-1 | Operational | Atmospheric chemistry | Objective is to measure and understand the chemical processes that control the distribution of ozone in the Earth's atmosphere, especially at high altitudes. | Waveband: SWIR - TIR: 2 - 5.5 µm, 5.5 - 13 µm (0.02cm-1 resolution) Spatial resolution: Swath width: Accuracy: |
| ACRIM II Active Cavity Radiometer Irradiance Monitor NASA | UARS | Not operational | Earth radiation budget radiometer | Measurements of solar luminosity and solar constant. Data used as record of ime variation of total solar irradiance, from extreme UV through to infra-red | Waveband: UV-FIR:1nm-50µm Spatial resolution: Not applicable Swath width: Not applicable Accuracy: Measures integrated flux of solar radiation to <0.1% |
| ACRIM III Active Cavity Radiometer Irradiance Monitor NASA | ACRIMSAT | Operational | Earth radiation budget radiometer | Measurements of solar luminosity and solar constant. Data used as record of time variation of total solar irradiance, from extreme UV through to infra-red | Waveband: UV - MWIR: 0.15 - 5 µm Spatial resolution: 5 deg FOV Swath width: 55 mins per orbit of full solar disk data Accuracy: 0.1% of full scale |
| A-DCS ARGOS-Data Collection System NOAA | NPOESS-1, NPOESS-2, NPOESS-3, NPOESS-4, NPOESS-5, NPOESS-6 | Being developed | Data collection | Data collection and communication system for receiving and retransmitting data from ocean and land-based remote observing platforms/transponders | The Argos DCS is a data collection relay system and not an Earth observing instrument. |
| AIRS Atmospheric Infra-red Sounder NASA | Aqua | Operational | Atmospheric temperature and humidity sounders | High spectral resolution measurement of temperature and humidty profiles in the atmosphere. Long-wave Earth surface emissivity. Cloud diagnostics. Trace gas profiles. Surface temperatures. | Waveband: VIS - TIR: 0.4 - 1.7µm, 3.4 - 15.4µm, Has approximately 2382 bands from VIS to TIR Spatial resolution: 1.1 degree (13X13 Km at nadir) Swath width: +/-48.95 degrees Accuracy: Humidity: 20%, Temperature: 1K |
| ALADIN Atmospheric Laser Doppler Instrument ESA | ADM-Aeolus | Prototype | Lidars | Primary objective is to provide wind profile measurements for an improved analysis of global 3-D wind fields. Measures Doppler shift information from molecules and particles advected by the wind | Waveband: UV: 355nm Spatial resolution: 50km (footprint: 70m) Swath width: Accuracy: 0.5ms-1(0 to 2km), 1ms-1(2 to 16km), 2ms-1 (above 16km) |
| ALI Advanced Land Imager NASA | NMP EO-1 | Operational | High resolution optical imagers | Measurement of Earth surface reflectance. Will validate new technologies contributing to cost reduction and increased capabilities for future missions. ALI comprises a wide field telescope and multispectral and panchromatic instrument | Waveband: 10 bands: VIS&NIR: 0.480-0.690µm, 0.433-0.453µm, 0.450-0.515µm, 0.525-0.605µm, 0.630-0.690µm, 0.775-0.805µm, 0.845-0.890µm, 1.200-1.300µm, SWIR: 1.550-1.750µm, 2.080-2.350µm Spatial resolution: PAN: 10m, VNIR&SWIR: 30m Swath width: 37km Accuracy: SNR @ 5% surf refl Pan:220, Multi 1: 215, Multi 2: 280, Multi 3: 290, Multi 4:240, Multi 4':190, Multi 5':130, Multi 5:175, Multi 7:170 (prototype instrument exceeds ETM+ SNR by a factor of 4 - 8) |
| ALT Altimeter NOAA | NPOESS-3, NPOESS-6 | Being developed | Radar altimeters | Obtains precise altimeter height measurements over world's oceans | Waveband: 13.6 and 5.3 GHZ Spatial resolution: Along track 15km Swath width: 15km Accuracy: SST height 4cm |
| AMI/SAR/Image Active Microwave Instrumentation. Image Mode ESA | ERS-2 | Operational | Imaging microwave radars | All-weather images of ocean, ice and land surfaces. Monitoring of coastal zones, polar ice, sea state, geological features, vegetation (including forests), land surface processes, hydrology. | Waveband: Microwave: 5.3 GHz, C band, VV polarisation, bandwidth 15.5 ± 0.06 MHz Spatial resolution: 30m Swath width: 100km Accuracy: Landscape topography: 3m, Bathymetry: 0.3m, Sea ice type: 3 classes |
| AMI/SAR/wave Active Microwave Instrumentation. Wave mode ESA | ERS-2 | Operational | Imaging microwave radars | Provides measurements of ocean wave spectra | Waveband: Microwave: 5.3GHz (C-band), VV polarisation Spatial resolution: 30m Swath width: Accuracy: Sea surface wind speed: 3m/s, Significant wave height: 0.2m |
| AMI/scatterometer Active Microwave Instrumentation. Wind mode ESA | ERS-2 | Operational | Scatterometers | Provides measurements of wind fields at the ocean surface, wind direction (range 0-360 deg), wind speed (range 1m/s - 30m/s) | Waveband: Microwave: 5.3GHz (C-band), VV polarisation Spatial resolution: Cells of 50km x 50km at 25km intervals Swath width: 500km Accuracy: Sea surface wind speed: 3m/s, Sea ice type: 2 classes |
| AMSR follow-on Advanced Microwave Scanning Radiometer follow-on JAXA | GCOM-W | Prototype | Imaging multi-spectral radiometers (passive microwave) | Provides measurements of water vapour, cloud liquid water, precipitation, winds, sea surface temperature, sea ice concentration, snow cover, soil moisture | Waveband: Microwave: 6.925, 10.65, 18.7, 23.8, 36.5, 50.3, 52.8, 89.0 GHz Spatial resolution: 5-50km (dependent on frequency) Swath width: 1600km Accuracy: Sea surface temparature: 0.5K, Sea ice cover: 10%, Cloud liquid water: 0.05kg/m2, Precipitation rate: 10%, Water vapour: 3.5kg/m2 through total column, Sea surface wind speed 1.5m/s |
| AMSR-E Advanced Microwave Scanning Radiometer-EOS JAXA (NASA) | Aqua | Prototype | Imaging multi-spectral radiometers (passive microwave) | Provides measurements of water vapour, cloud liquid water, precipitation, winds, sea surface temperature, sea ice concentration, snow cover and soil moisture | Waveband: Microwave: 6.925, 10.65, 18.7, 23.8, 36.5, 89.0 GHz Spatial resolution: 5-50km (dependent on frequency) Swath width: 1445km Accuracy: Sea surface temparature: 0.5K, Sea ice cover: 10%, Cloud liquid water: 0.05kg/m2, Precipitation rate: 10%, Water vapour: 3.5kg/m2 through total column, Sea surface wind speed 1.5m/s |
| AMSU-A Advanced Microwave Sounding Unit-A NOAA (BNSC) | Aqua, METOP-1, METOP-2, METOP-3, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Operational | Atmospheric temperature and humidity sounders | Provides all weather night-day temperature sounding to an altitude of 45km | Waveband: Microwave: 15 channels, 23.8-89.0GHz Spatial resolution: 48km Swath width: 2054km Accuracy: Temperature profile: 2K, Humidity: 3kg/m2, Ice & snow cover: 10% |
| AMSU-B Advanced Microwave Sounding Unit-B NOAA (BNSC) | NOAA-15, NOAA-16, NOAA-17 | Operational | Atmospheric temperature and humidity sounders | Provides all weather night-day humidity sounding | Waveband: Microwave: 89GHz, 150GHz, 183.3± 1.0 GHz (2bands), 183.3± 3.0 GHz (2bands), 183.3± 7.0 GHz (2bands) Spatial resolution: 16km Swath width: 2200km Accuracy: Humidity profile: 1kg/m2, |
| APS Aerosol Polarimetry Sensor NOAA | Glory, NPOESS-1, NPOESS-4 | Proposed | Atmospheric chemistry | Global distribution of natural and anthropogenic aerosols for quantification of the aerosol effect on climate, the anthropogenic component of this effect, and the long-term change of this effect caused by natural and anthropogenic factors | Waveband: 9 bands: VIS&SWIR; 0.412, 0.488, 0.555, 0.672, 0.910, 0.865, 1.378, 1.610, 2.250 µm Spatial resolution: 10km Swath width: 10km Accuracy: AOT Ocean .02, land .04 |
| Aquarius NASA (CONAE) | SAC-D/Aquarius | Proposed | Imaging multi-spectral radiometers (passive microwave) & Scatterometers | The Aquarius mission will measure global sea surface salinity with unprecedented resolution. The instruments include a set of three radiometers that are sensitive to salinity (1.413 GHz; L-band). The scatterometer corrects for the ocean's surface roughness. | Waveband: L Band (1.413-1.260 GHz Spatial resolution: 100km Swath width: 300km Accuracy: .2 psu |
| ARGOS CNES (NASA) | METOP-1, METOP-2, NOAA-12, NOAA-14, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Operational | Data collection & Precision orbit | Provides location data by Doppler measurements | The Argos DCS is a data collection relay system and not an Earth observing instrument. |
| Arina ROSKOSMOS | Resurs DK |  | Space Environment | Space particle detection experiment | Arina is an instrument for observation of solar magnetosphere variations of charged particle fluxes. |
| ASAR Advanced Synthetic-Aperture Radar ESA | Envisat | Operational | Imaging microwave radars | Provides all weather images of ocean, land and ice for monitoring of land surface processes, sea and polar ice, sea state, and geological and hydrological applications. Has 2 stripmap modes (Image and Wave (for ocean wave spectra)) and 3 ScanSAR modes | Waveband: Microwave: C-band, with choice of 5 polarisation modes (VV, HH, VV/HH, HV/HH, or VH/VV) Spatial resolution: Image, wave and alternating polarisation modes: approx 30m x 30m, Wide swath mode: 150m x 150m, Global monitoring mode: 950mm x 950m Swath width: Image and alternating polarisation modes: up to 100km, Wave mode: 5km, Wide swath and global monitoring modes: 400km or more Accuracy: Radiometric resolution in range: 1.5-3.5 dB, Radiometric accuracy: 0.65 dB |
| ASAR (image mode) Advanced Synthetic Aperture Radar (Image mode) ESA | Envisat | Operational | Imaging microwave radars | Provides all weather images of ocean, land and ice for monitoring of land surface processes, sea and polar ice, sea state, and geological and hydrological applications | See above. |
| ASAR (wave mode) Advanced Synthetic Aperture Radar (Wave mode) ESA | Envisat | Operational | Imaging microwave radars | Provides measurements of ocean wave spectra | See above. |
| ASCAT Advanced Scatterometer EUMETSAT (ESA) | METOP-1, METOP-2, METOP-3 | Being developed | Scatterometers | Provides sea ice cover, sea ice type and wind speed over sea surface measurements. Air pressure over ocean, Polar ice contours, Ice/snow imagery, Soil moisture. | Waveband: Microwave: C Band, 5.256Ghz Spatial resolution: Hi-res mode: 25-37km, Nominal mode: 50km Swath width: Continuous Accuracy: Wind speeds in range 4-24m/s: 2m/s and direction accuracy of 20deg |
| ASM Absolute Scalar Magnetometer ESA (CNES) | Swarm | Being developed | Magnetic field | The objective of the Absolute Scalar Magnetometer (ASM) is to calibrate the vector field magnetometer (VFM) to maintain the absolute accuracy in the multi-year geomagnetic field mission. | Waveband: N/A Spatial resolution: 0.016pT Swath width: N/A Accuracy: 0.3nT |
| ASTER Advanced Spaceborne Thermal Emission and Reflection Radiometer METI (Japan) (NASA) | Terra | Operational | High resolution optical imagers | Surface and cloud imaging with high spatial resolution, stereoscopic observation of local topography, cloud heights, volcanic plumes, and generation of local surface digital elevation maps. Surface temperature and emissivity | Waveband: VIS&NIR: 3 bands in 0.52-0.86µm, SWIR: 6 bands in 1.6-2.43µm, TIR: 5 bands in 8.125-11.65µm Spatial resolution: VNIR: 15m, stereo: 15m horizontally and 25m vertical, SWIR: 30m, TIR: 90m Swath width: 60km Accuracy: VNIR and SWIR: 4% (absolute), TIR: 4K, Geolocation: 7m |
| ATLID ATmospheric LIDar ESA | ESA Future Missions | Prototype | Lidars | Provides measurements of cloud top heights, aerosol properties, troposphere height, vertical distribution of cloud, boundary layer height. | Waveband: UV: 355nm Spatial resolution: footprint: 30m Swath width: Nadir Accuracy: Detection of cirrus cloud with optical thickness 1 with 15% error |
| ATMS Advanced Technology Microwave Sounder NOAA (NASA) | NPOESS-2, NPOESS-5, NPP | Approved | Atmospheric temperature and humidity sounders | Collects microwave radiance data that when combined with the CrIS data will permit calculation of atmospheric temperature and water vapor profiles. | Waveband: Microwave: 22 bands, 23-184 GHz Spatial resolution: 5.2 deg - 1.1 deg Swath width: 2300 km Accuracy: 0.75 K - 3.60 K |
| ATSR/M CNES | ERS-2 | Operational | Imaging multi-spectral radiometers (passive microwave) | Part of the ATSR payload on board ERS1 and ERS2 | See ATSR-2. |
| ATSR-2 Along Track Scanning Radiometer - 2 BNSC (CSIRO) | ERS-2 | Operational | Imaging multi-spectral radiometers (vis/IR) & Multiple direction/polarisation radiometers | Provides measurements of sea surface temperature, land surface temperature, cloud top temperature and cloud cover, aerosols, vegetation, atmospheric water vapour and liquid water content | Waveband: VIS-SWIR: 0.65, 0.85, 1.27, and 1.6µm, SWIR-TIR: 1.6, 3.7, 11 and 12µm, Microwave: 23.8, 36.5GHz (bandwidth of 400MHz) Spatial resolution: IR ocean channels: 1km x 1km, Microwave near-nadir viewing: 20km instantaneous field of view Swath width: 500km Accuracy: Sea surface temperature to <0.5K over 0.5 deg x 0.5 deg (lat/long) area with 80% cloud cover, Land surface temperature: 0.1K |
| AVHRR/2 Advanced Very High Resolution Radiometer/2 NOAA | NOAA-12, NOAA-14 | Operational | Imaging multi-spectral radiometers (vis/IR) | Provides measurements of land and sea surface temperature, cloud cover, snow and ice cover, soil moisture and vegetation indices. Data also used for volcanic eruption monitoring | Waveband: VIS: 0.58-0.68µm, NIR: 0.725-1.1µm, MWIR: 3.55-3.93µm, TIR: 10.3-11.3µm, 11.5-12.5µm Spatial resolution: 1.1km Swath width: 3000km approx Accuracy: |
| AVHRR/3 Advanced Very High Resolution Radiometer/3 NOAA | METOP-1, METOP-2, METOP-3, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Operational | Imaging multi-spectral radiometers (vis/IR) | Provides measurements of land and sea surface temperature, cloud cover, snow and ice cover, soil moisture and vegetation indices. Data also used for volcanic eruption monitoring | Waveband: VIS: 0.58-0.68µm, NIR: 0.725-1.1µm, SWIR: 1.58-1.64µm, MWIR: 3.55-3.93µm, TIR: 10.3-11.3µm, 11.5-12.5µm Spatial resolution: 1.1km Swath width: 3000km approx, Ensures full global coverage twice daily Accuracy: |
| AVNIR-2 Advanced Visible and Near Infra-red Radiometer type 2 JAXA | ALOS | Being developed | High resolution optical imagers | High resolution multi-spectral imager for land applications which include environmental monitoring, agriculture and forestry, disaster monitoring | Waveband: VIS: 0.42-0.50µm, 0.52-0.60µm, 0.61-0.69µm, NIR: 0.76-0.89µm Spatial resolution: 10m Swath width: 70km Accuracy: |
| AWiFS Advanced Wide Field Sensor ISRO | RESOURCESAT-1, RESOURCESAT-2 | Operational | High resolution optical imagers | Vegetation and crop monitoring, resource assessment (regional scale), forest mapping, land cover/ land use mapping, and change detection | Waveband: VIS: 0.52-0.59 & 0.62-0.68µm, NIR:0.77-0.86µm, SWIR: 1.55-1.7µm Spatial resolution: 55m Swath width: 730km Accuracy: 10 bit data |
| BISSAT Bissat Passive Radar ASI | BISSAT | TBD | Imaging microwave radars | Evaluation of bistatic radar cross section of natural and man-made targets, image classification, land surface. Passive instrument flown with main SAR mission. | Waveband: Microwave: X-band (passive) Spatial resolution: Swath width: Accuracy: |
| CALIOP Cloud-Aerosol Lidar with Orthogonal Polarization NASA | CALIPSO | Approved | Lidars | Two-wavelength, polarization lidar capable of providing aerosol and cloud profiles and properties | Waveband: 532 nm (polarization-sensitive), 1064 nm, VIS - NIR Spatial resolution: Vertical sampling: 30 m, 0 – 40 km Swath width: 333 m along-track Accuracy: 5% (532 nm) |
| CCD (CBERS) High Resolution CCD Camera CAST (INPE) | CBERS-2, CBERS-2B | Operational | High resolution optical imagers | Provides measurements of cloud type and extent and land surface reflectance, and used for global land surface applications | Waveband: VIS: 0.45-0.52µm, 0.52-0.59µm, 0.63-0.69µm, NIR: 0.77-0.89µm, PAN: 0.51-0.71µm Spatial resolution: 20m Swath width: 113km Accuracy: |
| CCD (HJ, HY) CCD camera CAST | HJ-1A, HJ-1B |  | High resolution optical imagers | Land surface applications | Waveband: 0.43-0.90µm Spatial resolution: 30m Swath width: 360km (per set)700km (two sets) Accuracy: |
| CCD camera ISRO | INSAT-2E, INSAT-3A | Operational | Imaging multi-spectral radiometers (vis/IR) | Cloud and Vegetation monitoring | Waveband: VIS: 0.62-0.68µm, NIR: 0.77-0.86µm, SWIR: 1.55-1.69µm Spatial resolution: 1X1km Swath width: Normal: 6000km (N-S) X 6000km (E-W) anywhere on earth disc, Program: 6000km (N-S) X (n X 300) km (E-W) : n and number of frames programmable Accuracy: |
| CERES Cloud and the Earth's Radiant Energy System NASA | Aqua, NPOESS-2, NPOESS-5, Terra | Operational | Earth radiation budget radiometer | Long term measurement of the Earth's radiation budget and atmospheric radiation from the top of the atmosphere to the surface; provision of an accurate and self-consistent cloud and radiation database. | Waveband: 3 channels: 0.3-5 µm, 0.3 -100 µm, 8-12 µm, UV-FIR Spatial resolution: 20km Swath width: Accuracy: 0.5%, 1%, 1% (respectively for the 3 channels) |
| CHAMP GPS Sounder GPS TurboRogue Space Receiver (TRSR) NASA (DLR) | CHAMP | Operational | Atmospheric temperature and humidity sounders & Precision orbit | Temperature and water vapour profiles | Uses GPS frequencies for sounding of temperature and water profiles of the atmosphere. CHAMP provides temperature profiles in the troposphere up to the middle stratosphere, and water vapour profiles in the troposphere only. |
| CHAMP gravity package (Accelerometer+GPS) STAR Accelerometer CNES (DLR) | CHAMP | Operational | Gravity | Earth gravity field measurements | Since the advent of CHAMP, the first in a series of low-altitude satellites being almost continuously and precisely tracked by GPS, a new generation of long-wavelength gravitational geopotential models have been derived. |
| CHAMP magnetometry package (1 Scalar + 2 Vector Magnetometer) Overhauser Magnetometer and Fluxgate Magnetometer DLR | CHAMP | Operational | Magnetic field | Earth magnetic field measurements | A high performance Fluxgate magnetometer set measuring the three components of the ambient magnetic field in the instrument frame combined with a star camera determining the attitude of the assembly with respect to a stellar frame and a Overhauser scalar magnetometer serving as magnetic reference. |
| CIA Advanced Hyperspectral camera ASI | Hyperspectral Mission |  | Imaging multi-spectral radiometers (vis/IR) | Pancromatic and Hyperspectral data for complex land ecosystem studies | Waveband: HYC spectral range + MIR and TIR channels Spatial resolution: Improved (wrt HYC) resolution PAN 2-3m Swath width: Greater swath Accuracy: |
| CLAES Cryogenic Limb Array Etalon Spectrometer instrument NASA | UARS | Not operational | Earth radiation budget radiometer | Measures many of the chemical species which are involved in stratospheric chemistry as well as global distribution of statospheric aerosols. | Waveband: SWIR: 3.5µm, 6µm, TIR: 8µm, 12.7µm Spatial resolution: Vert 2.8km, Horiz 480km Swath width: 50.7km vert limb Accuracy: 20%, 3K |
| Cloud Sensor Cloud and aerosol sensor JAXA | GOSAT |  | Cloud profile and rain radars | Will contribute to GOSAT main mission of CO2 profile measurement - which requires detection and removal of contaminating signals from clouds and aerosols | No data yet available. |
| CMIS Conical-scanning Microwave Imager/Sounder NOAA | NPOESS-1, NPOESS-2, NPOESS-3, NPOESS-4, NPOESS-5, NPOESS-6 | Being developed | Imaging multi-spectral radiometers (passive microwave) & Atmospheric temperature and humidity sounders | Collects microwave radiometry and sounding data. Data types include atmospheric temperature and moisture profiles, clouds, sea surface winds, and all-weather land/water surfaces. | Waveband: Microwave: 190Ghz Spatial resolution: 15-50km depending on frequency Swath width: 1700km Accuracy: Temperature Profiles to 1.6K, water vapor 20% |
| COCTS Ocean colour scanner CAST | HY-1B | Being developed | Ocean colour instruments | Ocean chlorophyll, Ocean yellow substance absorbance, Sea-ice surface temperature | Waveband: B1: 0.402-0.422, B2: 0.433-0.453, B3: 0.480-0.500, B4: 0.510-0.530, B5: 0.555-0.575, B6: 0.660-0.680, B7: 0.740-0.760, B8: 0.845-0.885, B9: 10.30-11.40, B10: 11.40-12.50µm Spatial resolution: 1.1km Swath width: 3083km Accuracy: |
| Communications payload (Ka and UHF band) CSIRO | FedSat | Operational | Communications |  | Waveband: up 313.55MHz, down 400.4MHz |
| CPR Cloud Profiling Radar ESA | ESA Future Missions | Prototype | Cloud profile and rain radars | Measures cloud characteristics including base height | Waveband: Microwave: 94GHz Spatial resolution: 750m Swath width: nadir only Accuracy: 98% detection of radiatively significant ice cloud |
| CPR (Cloudsat) Cloud Profiling Radar NASA | CloudSat | Approved | Cloud profile and rain radars | Primary goal is to provided data needed to evaluate and improve the way clouds are represented in global climate models. Measures vertical profile of clouds | Waveband: Microwave: 94Ghz Spatial resolution: Vertical: 500m, Cross-track: 1.4km, Along-track: 2.5km Swath width: Instantaneous Footprint < 2km Accuracy: Cloud liquid water content<=50%; ice water content within +100%, -50%; detect all single layer clouds with optical depth>=1.0 |
| CrIS Cross-track Infrared Sounder NOAA (NASA) | NPOESS-2, NPOESS-5, NPP | Prototype | Atmospheric temperature and humidity sounders | Daily measurements of vertical atmospheric distribution of temperature, moisture, and pressure | Waveband: MWIR-TIR: 3.92-4.4µm, 5.7-8.62µm, 9.1-14.7µm, 1300 spectral channels Spatial resolution: IFOV 14km diameter, 1km vertical layer resolution Swath width: 2200km Accuracy: Temperature profiles: to 0.9K, Moisture profiles: 20-35%, Pressure profiles: 1% |
| CZI Coast region imager CAST | HY-1B | Being developed | Imaging multi-spectral radiometers (vis/IR) | Coastal Zone monitoring and environmental applications | Waveband: B1: 0.433-0.453, B2: 0.555-0.575, B3: 0.655-0.675, B4: 0.675-0.695μm Spatial resolution: 250m Swath width: 500km Accuracy: |
| DCP (SCD) Data Collecting Platform Transponder INPE | SCD-1, SCD-2 | Operational | Data collection | Environmental data collection from ground based data collecting platforms | Data collection and relay system. |
| DCS (CAST) Data Collecting System Transponder (CAST) CAST | CBERS-2, CBERS-2B, CBERS-3, CBERS-4 | Operational | Data collection | Data collection and communication | Data collection and relay system. |
| DCS (JAXA) Data Collection System (JAXA) JAXA | GMS-5 | Prototype | Data collection | Data Collection System, Receives in-situ data from data collection platforms worldwide and transmits to ground station | Data collection and relay system. |
| DCS (NOAA) Data Collection System (NOAA) NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Operational | Data collection | Collects data on temperature (air/water), atmospheric pressure, humidity and wind speed/direction, speed and direction of ocean and river currents | Data collection and relay system. |
| DCS (ROSHYDROMET) Data Collection System ROSHYDROMET (ROSKOSMOS) | Elektro-L, METEOR-3M N2 | Operational | Data collection | Collects data on temperature (air/water), atmospheric pressure, humidity and wind speed/direction, speed and direction of ocean and river currents | Data collection and relay system. |
| DMC Imager Disaster Management Constellation Imager BNSC | UK-DMC | Operational | High resolution optical imagers | Visible and NIR imagery in support of disaster management | Waveband: VIS and NIR Spatial resolution: 32m Swath width: 2 beams of 300km Accuracy: |
| DORIS Doppler Orbitography and Radio-positioning Integrated by Satellite CNES | SPOT-2, SPOT-4, Topex-Poseidon | Operational | Precision orbit | Orbit determination | Waveband: Spatial resolution: Swath width: Accuracy: Orbit error ~2.5cm |
| DORIS-NG Doppler Orbitography and Radio-positioning Integrated by Satellite-NG CNES | CRYOSAT, Envisat, Jason, Jason-2 (also known as OSTM), SPOT-5 | Operational | Precision orbit | Precise orbit determination Real time onboard orbit determination (navigation) | Waveband: 401.25MHz, 2036.25MHz Spatial resolution: Swath width: FOV :130 degrees Accuracy: Orbit error ~1cm |
| DPR Dual-frequency Precipitation Radar JAXA (NASA) | GPM Core | TBD | Cloud profile and rain radars | Measures rain rate classified by rain and snow, in latitudes up to 70 degrees | Waveband: Microwave: 13.6 GHz (Ku band) and 35.5 GHz (Ka band) Spatial resolution: Range resolution: 4-5 km Horizontal Swath width: 245 km (Ku-band), 100km (Ka band) Accuracy: rainfall rate 0.2mm/h |
| DRF ROSKOSMOS | Vulkan-Kompas-2 |  | Space Environment | Space radiation and ultraviolet measurements | Waveband: UV: 0.2-0.35µm, Ee>30keV, Ep>7keV Spatial resolution: Swath width: Accuracy: |
| ECHO-V ROSKOSMOS | Kanopus-Vulkan |  | Space Environment | Space particle detection experiment | Waveband: Ee 3-30MeV, Ee 30-100MeV Spatial resolution: Swath width: Accuracy: |
| EFI Electric Field Instrument ESA (CSA) | Swarm | Being developed | Gravity & Space environment | Measures ion density, drift velocity and electric field | Waveband: N/A Spatial resolution: 0.3mV/m Swath width: N/A Accuracy: <3mV/m |
| EGG 3-Axis Electrostatic Gravity Gradiometer ESA | GOCE | Being developed | Gravity & Precision orbit | The main objective of EGG is to measure the 3 components of the gravity-gradient tensor (ie gradiometer data) | Designed specifically for determining the stationary gravity field. The measured signal is the difference in gravitational acceleration at the test-mass location inside the spacecraft caused by gravity anomalies from attracting masses of the Earth. |
| EHIS Energetic Heavy Ion Sensor NOAA | GOES-R | Approved | Space Environment | Space particle detection | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| ENVISAT Comms Communications package on ENVISAT ESA | Envisat | Operational | Communications | Communication package onboard ENVISAT series satellites | Data communication only. |
| EOC Electro-Optical Camera KARI | KOMPSAT-1 | Operational | High resolution optical imagers | High resolution stereo imager for land applications of cartography and disaster monitoring | Waveband: Panchromatic VIS: 0.51-0.73µm Spatial resolution: 6.6m Swath width: 17km Accuracy: |
| EPIC Earth PolyChromatic Imaging Camera NASA | DSCOVR | Proposed | Atmospheric chemistry | Measures ozone amounts, aerosol amounts, cloud height and phase, hotspot land properties, and UV radiation estimates at the Earth's surface. | Waveband: UV-NIR: 0.317-0.905µm 10 bands Spatial resolution: 8km Swath width: Accuracy: |
| ERBE Earth Radiation Budget Experiment (non-scanner) NASA | ERBS | Operational | Earth radiation budget radiometer | Radiation budget measurements - Total energy of Sun's radiant heat and light, Reflected solar radiation, Earth emitted radiation | Waveband: UV-FIR Spatial resolution: Narrow: 250km; Wide: 1000km Swath width: Medium and wide earth views Accuracy: Shortwave- 15%, Longwave- 5% |
| ERBS Earth Radiation Budget Sensor NOAA | NPOESS-3, NPOESS-6 | TBD | Earth radiation budget radiometer | Measures Earth radiation gains and losses on regional, zonal and global scales | Waveband: 0.3-50µm Spatial resolution: 25km Swath width: 2200Km Accuracy: DLR/DSR10 watts/m2net solar 3w/m2OLR 5w/m2 |
| ERS Comms Communication package for ERS ESA | ERS-2 | Operational | Communications | Communication package onboard ERS series satellites | Data communication only. |
| ETM+ Enhanced Thematic Mapper Plus USGS | Landsat-7 | Operational | Imaging multi-spectral radiometers (vis/IR) | Measures surface radiance and emittance, land cover state and change (eg vegetation type). Used as multi-purpose imagery for land applications | Waveband: VIS-TIR: 8 channels: 0.45-12.5µm, Panchromatic channel: VIS 0.5-0.9µm Spatial resolution: Pan: 15m, Vis-SWIR: 30m, TIR: 60m Swath width: 185km Accuracy: 50-250m systematically corrected geodetic accuracy |
| EUVS Extreme Ultraviolet Sensor NOAA | GOES-R | Approved | Other | Solar EUV radiation is a dominant energy source for the upper atmosphere and the ionizing radiation produces the ionosphere. Solar variability at these wavelengths is one of the primary drivers of thermospheric/ ionospheric variability. EUVS will measure this radiation. | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| Fluxgate magnetometer CRCSS | FedSat | Approved | Magnetic field | Measures electrical currents and perturbations in the Earth's magnetic field in the range 0.1Hz to 1kHz. | A high precision instrument designed to measure magnetic fields at all latitudes at an 800 km altitude over a range of ±65,000 nT. |
| GALS-M Galactic space rays detector ROSHYDROMET | Meteor-M No1, Meteor-M No2 | TBD | Space Environment | Space environment monitoring | Waveband: protons fluxes density > 600 MeV Spatial resolution: Swath width: Accuracy: |
| Geomicrowave sounder NOAA | GOES-R | Approved | Atmospheric temperature and humidity sounders | For geo oribit, will provides atmospheric soundings and data on atmospheric stability and thermal gradient winds | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| Geoton-L1 ROSKOSMOS | Resurs DK |  | Imaging multi-spectral radiometers (vis/IR) | Natural resource surveying, environmental monitoring | Waveband: 0.5-0.8µm Spatial resolution: 1-3m Swath width: 28.3-42km Accuracy: |
| GERB Geostationary Earth Radiation Budget EUMETSAT (ASI) | METEOSAT-8, METEOSAT-9, METEOSAT-10, METEOSAT-11 | Operational | Earth radiation budget radiometer | Measures long and short wave radiation emitted and reflected from the Earth's surface, clouds and top of atmosphere. Full Earth disk, all channels in 5 mins | Waveband: UV-MWIR: 0.32-4.0µm, UV-FIR: 0.32-30µm Spatial resolution: 44.6km x 39.3km Swath width: Full Earth disk Accuracy: Emitted radiation: 0.12-1.3 W/m2, Reflectance: 1% |
| GGAK-E Heliogeophysical hardware complex ROSKOSMOS | Elektro-L |  | Magnetic field & Space environment | Electromagnetic field measurements | Electro-L carries an array of solar and magnetic sensors providing data on solar activity and radiation levels needed for near-earth environment forecasts. |
| GGAK-M Heliogeophysical hardware complex ROSKOSMOS | Meteor-M No1, Meteor-M No2 |  | Magnetic field & Space environment | Electromagnetic field measurements | A complex of heliogeophysical instruments |
| GHG Sensor Greenhouse gases observing sensor JAXA | GOSAT | TBD | Atmospheric chemistry | This mission is in response to the Kyoto Protocol - and aims to observe Green House Gases (GHGs) including CO2 with 1% relative accuracy in sub-continental spatial resolution and to identify the GHGs sources and sinks in conjunction with data from ground instruments | No data yet available. |
| GID-12T ROSKOSMOS | Kanopus-Vulkan, Vulkan-Kompas-2 |  | Magnetic field & Space environment | Electromagnetic field measurements | Waveband: 1200MHz, 1600MHz Spatial resolution: Swath width: Accuracy: |
| GIFTS Geosynchronous Imaging Fourier Transform Spectrometer NASA | NMP EO-3 GIFTS | Proposed | Atmospheric temperature and humidity sounders | Measures temperature, water vapour, tracer winds, chemical composition with high spatial and temporal resolution for considerable improvements in weather observations and air quality monitoring. Tests next-generation met observing systems. | Waveband: MWIR-TIR: 1724 channels in the bands 4.45-6.06µm and 8.85-14.6µm Spatial resolution: Visible: 1km x 1km, IR: 4km x 4km Swath width: Full Earth disk Accuracy: |
| GLAS Geoscience Laser Altimeter System NASA | ICESat | Operational | Lidars | Provision of data on ice sheet height/thickness, land altitude, aerosol height distributions, cloud height and boundary layer height | Waveband: VIS-NIR: Laser emits at 1064nm (for altimetry) and 532nm (for atmospheric measurements) Spatial resolution: 66m spots separated by 170m Swath width: N/A Accuracy: Aerosol profile: 20%, Ice elevation: 20cm, Cloud top height: 75m, Land elevation: 20cm, geoid: 5m |
| GLI follow-on Global Imager follow-on JAXA | GCOM-C | Prototype | Imaging multi-spectral radiometers (vis/IR) & Ocean colour instruments | Measures water vapour, aerosols, cloud cover, cloud top height/temp, ocean colour, sea surface temperature, land surface temparature, glacier extent, icebergs, sea ice and snow cover, photosynthetically active radiation, vegetation type and land cover | Waveband: VIS&NIR: 23 bands (380-830nm), NIR-SWIR: 6 bands (1050-2215nm), MWIR-TIR: 7 bands (3.75-11.95µm) Spatial resolution: 1km for 28 bands, 250m for 6 bands Swath width: 1600km Accuracy: Specific humidity profile: 0.5g/m2 through total column, Surface temp 0.4-0.5K, Cloud top temp: 0.5K, Cloud cover: 3%, Cloud top height: 0.5km, Ice and snow cover: 5% |
| GLM GEO Lightning Mapper NOAA | GOES-R | Approved | Lightning imager |  | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| GMI GPM Microwave Imager NASA | GPM Constellation, GPM Core | Proposed | Imaging multi-spectral radiometers (passive microwave) | Measures rainfall rates over oceans and land, combined rainfall structure and surface rainfall rates with associated latent heating. Used to produce three hour, daily, and monthly total rainfall maps over oceans and land. | Waveband: Microwave: 10.65, 19.4, 21.3, 37, and 85.5 GHz Spatial resolution: Horizontal: 36 km cross-track at 10.65 GHz (required - Primary Spacecraft, goal - Constellation Spacecraft); 10 km along-track and cross-track (goal - Primary Spacecraft) Swath width: 800km (Primary Spacecraft) 1300 km (Constellation Spacecraft) Accuracy: NEDT 0.5 K - 1.0 K |
| GMS Comms Communications package on GMS JAXA (JMA) | GMS-5 | Prototype | Communications | Communication package onboard GMS series satellites | Data communication only. |
| GOES Comms Communications package on GOES NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Prototype | Communications |  | Data communication only. |
| GOLPE GPS Occultation and Passive reflection Experiment NASA | SAC-C | Operational | Precision orbit & Atmospheric temperature and humidity sounders | Measurements of atmospheric effects on GPS signals, and precise positioning information to assist gravitational measurements | Waveband: Uses GPS frequencies. Spatial resolution: Swath width: Accuracy: 0.05 K or better appears attainable |
| GOME Global Ozone Monitoring Experiment ESA | ERS-2 | Prototype | Atmospheric chemistry | Measures concentration of O3, NO, NO2, BrO, H2O, O2/O4, plus aerosols and polar stratospheric clouds, and other gases in special conditions | Waveband: UV-NIR: 0.24-0.79µm (resolution 0.2-0.4nm) Spatial resolution: Vertical: 5km (for O3), Horizontal: 40 x 40 km to 40 x 320 km Swath width: 120-960km Accuracy: |
| GOME-2 Global Ozone Monitoring Experiment - 2 EUMETSAT (ESA) | METOP-1, METOP-2, METOP-3 | Prototype | Atmospheric chemistry | Measurement of total column amounts and stratospheric and tropospheric profiles of ozone. Also amounts of H20, NO2, OClO, BrO, SO2 and HCHO. | Waveband: UV-NIR: 0.24-0.79µm (resolution 0.2-0.4nm) Spatial resolution: Horizontal: 40 x 40 km (960km swath) to 40 x 5 km (for polarization monitoring) Swath width: 120-960km Accuracy: Cloud top height: 1km (rms), Outgoing short wave radiation and solar irradiance: 5W/m2, Trace gas profile: 10-20%, Specific humidity profile: 10-50g/kg |
| GOMOS Global Ozone Monitoring by Occultation of Stars ESA (CNES) | Envisat | Operational | Atmospheric chemistry | Provides stratospheric profiles of temparature and of ozone, NO2, H20, aerosols and other trace species | Waveband: Spectrometers: UV-Vis: 248-371nm & 387-693nm,NIR: 750-776nm & 915-956nm, Photometers: 644-705nm & 466-528nm Spatial resolution: 1.7km vertical Swath width: Not applicable Accuracy: |
| GPS (ESA) GPS receiver ESA | GOCE, Swarm | TBD | Precision orbit | Satellite positioning | Used for precision satellite positioning only – not an Earth observing instrument. |
| GPS (GRACE) Global Positioning System Receiver NASA | GRACE |  | 0 | Microwave: 1227.60MHz, 1575.42MHz | Used for precision satellite positioning only – not an Earth observing instrument. |
| GPS receiver CRCSS | FedSat | Approved | Precision orbit & Atmospheric temperature and humidity sounders | Sounding data for study of physics of upper atmosphere, and water vapour, temparature and refractivity profiles | Waveband: Spatial resolution: 1 sample every 30 secs Swath width: Accuracy: |
| GPSDR GPS Demonstration Receiver CONAE (NASA) | Topex-Poseidon | Operational | Precision orbit & Atmospheric temperature and humidity sounders | Provides precise continuous tracking data of satellite to decimeter accuracy | Used for precision satellite positioning only – not an Earth observing instrument. |
| GRAS GNSS Receiver for Atmospheric Sounding EUMETSAT (ESA) | METOP-1, METOP-2, METOP-3 | Prototype | Atmospheric temperature and humidity sounders & Precision orbit | GNSS receiver for atmospheric temperature and humidty profile sounding | Waveband: Spatial resolution: Vertical: 150m (trophosphere) and 1.5km (stratosphere), Horizontal: 100km approx (troposphere), 300km approx (stratosphere) Swath width: Altitude range of 5-30km Accuracy: Temperature sounding to 1K rms |
| HAIRS High Accuracy Inter-satellite Ranging System NASA | GRACE | Operational | Gravity | Ranging instrument between the 2 GRACE spacecraft - to derive Earth gravity field measurements | Waveband: Microwave: K Band, Ka Band Spatial resolution: Swath width: Accuracy: 10 microns total at twice per revolution |
| HALOE Halogen Occultation Experiment NASA | UARS | Operational | Atmospheric chemistry | Provides data on vertical distributions of hydrofluoric and hydrochloric acids, methane, water vapour and members of the nitrogen family. It also provides atmospheric temperature versus pressure profiles from observations of carbon dioxide | Waveband: channels between 2.4µm - 10µm, SWIR - TIR Spatial resolution: 2km-4km Swath width: Accuracy: HCL: 12-24%, HF: 15-27%, CH4: 6-27%, NO: 14-30%, H2O: 14-30%, O3: 9-25%, NO2: 9-21%: Temperature: 3-5K, Aerosol Extinction: < 30% |
| HES Hyperspectral Environmental Suite NOAA | GOES-R | Approved | Imaging multi-spectral radiometers (vis/IR) | Will sense emitted thermal energy and reflected solar energy from sampled areas of the Earth's surface and atmosphere. These data are used to compute vertical profiles of temperature and moisture, surface and cloud-top temperatures, and winds, and provide information about the Earth surface and oceans. | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| HiRDLS High Resolution Dynamics Limb Sounder NASA (BNSC) | Aura | Approved | Atmospheric chemistry | Measures atmospheric temperature, concentrations of ozone, water vapour, methane, NOx, N2O, CFCs and other minor species, aerosol concentration, location of polar stratospheric clouds and cloud tops | Waveband: TIR: 6.12-17.76µm (21 channels) Spatial resolution: Vertical: 1km, Horizontal: 10km Swath width: Accuracy: Trace gas: 10%, Temparature: 1K, Ozone: 10% |
| HIRS/2 High Resolution Infra-red Sounder/2 NOAA | NOAA-12, NOAA-14 | Operational | Atmospheric temperature and humidity sounders | Measures atmospheric temperature, concentrations of ozone, water vapour, methane, NOx, N2O, CFCs and other minor species, aerosol concentration, location of polar stratospheric clouds and cloud tops | Waveband: VIS-TIR: 0.69-14.95µm (20 channels) Spatial resolution: 20.3km Swath width: 2240km Accuracy: |
| HIRS/3 High Resolution Infra-red Sounder/3 NOAA | NOAA-15, NOAA-16, NOAA-17 | Operational | Atmospheric temperature and humidity sounders | Provides atmospheric temperature profiles and data on cloud parameters, humidity soundings, water vapour, total ozone content, and surface temperatures | Waveband: VIS-TIR: 0.69-14.95µm (20 channels) Spatial resolution: 20.3km Swath width: 2240km Accuracy: |
| HIRS/4 High Resolution Infra-red Sounder/4 NOAA | METOP-1, METOP-2, METOP-3, NOAA-N, NOAA-N' | Operational | Atmospheric temperature and humidity sounders | Provides atmospheric temperature profiles and data on cloud parameters, humidity soundings, water vapour, total ozone content, and surface temperatures. Same as HIRS/3, with 10km IFOV | Waveband: VIS-TIR: 0.69-14.95µm (20 channels) Spatial resolution: 20.3km Swath width: 2240km Accuracy: |
| HRDI High Resolution Doppler Imager NASA | UARS | Operational | Atmospheric chemistry | Daytime wind measurements below 50km from Doppler shifts of molecular oxygen absorption lines. Day and night wind measurements above about 60km from Doppler shifts of neutral and ionised atomic oxygen emission lines. Also measures temperature | Waveband: 0.557-0.776µm Spatial resolution: Vertical (limb): 4km, Horizontal (limb): 80km Swath width: 5 to 100km (vertical coverage) Accuracy: Vector winds in the stratosphere, mesosphere and lower thermosphere during the day, and the lower thermosphere at night to an accuracy of 5 m/s |
| HRG High Resolution Geometry CNES | SPOT-5 | Operational | High resolution optical imagers | High resolution multispectral mapper. 2 HRG instruments on this mission can be processed to produce simulated imagery of 2.5m. Images are 60km x 60km in size | Waveband: VIS: B1:0.50-0.59µm, B2: 0.61-0.68µm, NIR: B3: 0.79-0.89µm, SWIR: 1.50-1.75µm, Panchromatic: 0.49-0.69µm Spatial resolution: Panchromatic: 2, 5m, Multispectral: 10m Swath width: 60km (1 instrument), 117km (2 instruments). Same as SPOT 4 with off-track steering capability (±27 deg) Accuracy: |
| HRMS High Resolution Multi-spectral Scanner CONAE | SAC-F | Approved | Imaging multi-spectral radiometers (vis/IR) |  | Waveband: Spatial resolution: Swath width: Accuracy: |
| HR-PAN High Resolution Panchromatic Camera ISRO | CARTOSAT-2 | Prototype | High resolution optical imagers | High resolution stereo images for large scale (better than 1:0000) mapping applications, urban applications, GIS ingest | Waveband: VIS: 0.5-0.75µm Spatial resolution: 1 m Swath width: 12 km Accuracy: |
| HRS High Resolution Stereoscopy CNES | SPOT-5 | Operational | High resolution optical imagers | High resolution stereo instrument | Waveband: Panchromatic: VIS 0.49-0.69µm Spatial resolution: Panchromatic: 10m, Altitude: 15m Swath width: 120km Accuracy: |
| HRTC High Resolution Panchromatic Camera CONAE | SAC-C | Operational | High resolution optical imagers | High resolution eath imagery to complement MMRS on the same mission | Waveband: VIS-NIR: 400-900nm Spatial resolution: 35m Swath width: 90km Accuracy: |
| HRV High Resolution Visible CNES | SPOT-2 | Operational | High resolution optical imagers | 2 HRV instruments on this mission provide 60km x 60km images for a range of land and coastal applications | Waveband: VIS: B1:0.5-0.59µm, B2:0.61-0.68µm, NIR: B3:0.79-0.89µm, Panchromatic: VIS 0.51-0.73µm Spatial resolution: 10m (panchromatic) or 20m Swath width: 117km (ie 60km + 60km with 3km overlap) - steerable up to ±27 deg off-track Accuracy: |
| HRVIR High Resolution Visible and Infra-red CNES | SPOT-4 | Operational | High resolution optical imagers | 2 HRVIR instruments on this mission provide 60km x 60km images for a range of land and coastal applications | Waveband: VIS: B1: 0.50-0.59µm, B2: 0.61-0.68µm, NIR: 0.79-0.89µm, SWIR: 1.58-1.75µm, Panchromatic:(B2) 0.61-0.68µm Spatial resolution: 10m (0.64µm) or 20m Swath width: 117km (ie 60km + 60km with 3km overlap). Steerable up to ±27 deg off-track Accuracy: |
| HSB Humidity Sounder/Brazil INPE (NASA) | Aqua | Not operational | Atmospheric temperature and humidity sounders | Humidity soundings for climatological and atmospheric dynamics applications | Waveband: Microwave: 5 discreet channels in the range of 150-183 MHz Spatial resolution: 13.5km Swath width: 1650km Accuracy: Temperature: 1.0-1.2k coverage of land and ocean surfaces, Humidity: 20% |
| HSC High Sensitivity Camera CONAE | SAC-D/Aquarius | Approved | Imaging multi-spectral radiometers (vis/IR) |  | Waveband: PAN: VIR-NIR: 450-900 nm Spatial resolution: 200-300m Swath width: > 700 km Accuracy: |
| HSI (HJ-1A) Hyper Spectrum Imager CAST | HJ-1A | Being developed | Imaging multi-spectral radiometers (vis/IR) | Hyperspectral imaging | Waveband: 0.45-0.95µm Spatial resolution: 100m Swath width: 50km Accuracy: |
| HSMS High Swath Multi-spectral Scanner CONAE | SAC-F | Approved | Imaging multi-spectral radiometers (vis/IR) |  | Waveband: Spatial resolution: Swath width: Accuracy: |
| HSRS Hot Spot Recognition System DLR | BIRD | Operational | Imaging multi-spectral radiometers (vis/IR) | Hot spot Detection (vegetation fires, volcanic activities, burning oil wells or coal seams | Waveband: MWIR: 3.4-4.2µm, TIR: 8.4-9.3µm Spatial resolution: 370m Swath width: 190km Accuracy: |
| HSS Hyper-spectral Scanner CONAE | SAC-F | Approved | Imaging multi-spectral radiometers (vis/IR) | Hyperspectral imaging | Waveband: Spatial resolution: Swath width: Accuracy: |
| HSTC High Sensitivity Technological Camera CONAE | SAC-C | Operational | Imaging multi-spectral radiometers (vis/IR) | Provides data to Monitor forest fires, electrical storms and geophysical sutudies of aurora borealis | Waveband: PAN: VIS-NIR: 450-850nm Spatial resolution: 250m Swath width: 900km Accuracy: |
| HYC HYperspectral Camera ASI | Hyperspectral Mission | TBD | Imaging multi-spectral radiometers (vis/IR) | Pancromatic and Hyperspectral data for complex land ecosystem studies | Waveband: VIS-NIR:400-900 nm, 400-1000nm; SWIR: 900-2500nm; Spectral resolution 10 nm, 220 bands Spatial resolution: PAN: 5m ; VNIR-SWIR:20m; Swath width: 20 Km Accuracy: |
| HYDROS NASA | HYDROS | Proposed | Multiple direction/polarisation radiometers | Microwave measurement of soil moisture and freeze/thaw timeline | Waveband: 1.26 GHz for the radar and 1.41 GHz for the radiometer and will be capable of both horizontal and vertical polarizations Spatial resolution: Radar 3km&10km, Radiometer 40km Swath width: 1000km Accuracy: |
| Hyperion Hyperspectral Imager NASA | NMP EO-1 | Operational | Imaging multi-spectral radiometers (vis/IR) | Hyperspectral imaging of land surfaces | Waveband: VIS-NIR: 400-1000nm; NIR-SWIR: 900-2500nm; 10nm spectral resolution for 220 bands Spatial resolution: 30m Swath width: 7.5km Accuracy: SNR @ 10% refl target: vis 10-40 swir 10-20 |
| IAP Instrument for plasma analysis CNES | DEMETER | Operational | Space Environment | Density, temperatures, speeds of major ions | Waveband: Spatial resolution: Swath width: Accuracy: Ion density: +5%, Temperature +5%, Speed +5% |
| IASI Infra-red Atmospheric Sounding Interferometer CNES (EUMETSAT) | METOP-1, METOP-2, METOP-3 | Being developed | Atmospheric temperature and humidity sounders & Atmospheric chemistry instruments | Measures tropospheric moisture and temperature, column integrated contents of ozone, carbon monoxide, methane, dinitrogen oxide and other minor gases which affect tropospheric chemistry. Also measures sea surface and land temperature | Waveband: MWIR-TIR: 3.4-15.5µm with gaps at 5µm and 9µm Spatial resolution: Vertical: 1-30km, Horizontal: 25km Swath width: 2052km Accuracy: Temperature: 0.5-2K, Specific humidity: 0.1-0.3g/kg, Ozone, trace gas profile: 10% |
| ICARE Influence of Space Radiation on Advanced Components CNES | SAC-C, SAC-D/Aquarius | Operational | Space Environment | Improvement of risk estimation models on latest generation of integrated circuits technology | Will measure high energy radiation environment, trapped particle intensities and energy distribution and correlate them with advanced electronic components degradation. ICARE will be able to conduct regular environment characterization campaigns for ten days every six months and exceptional ones during solar events. |
| ICE Instrument for Electric Field CNES | DEMETER | Operational | Space Environment | Electric field | Waveband: DC to 3MHz Spatial resolution: Swath width: Accuracy: DC field +3mV/m |
| IDP Instrument For Plasma Detection CNES | DEMETER | Operational | Space Environment | Energy spectrum of electrons | Waveband: Spatial resolution: Swath width: Accuracy: |
| IGPM radiometer IGPM microwave radiometer ASI | IGPM | TBD | Imaging multi-spectral radiometers (passive microwave) | Global water and energy cycle | No data available yet. |
| IGPM rain radar ASI | IGPM | TBD | Cloud profile and rain radars | Global water and energy cycle | No data available yet. |
| IIR Imaging infrared radiometer CNES | CALIPSO | TBD | Imaging multi-spectral radiometers (vis/IR) | Radiometer optimized for combined IIR/lidar retrievals of cirrus particle size | Waveband: TIR: 8.7, 10.5, and 12.0 µm (08.µm resolution) Spatial resolution: 1km Swath width: 64km Accuracy: 1K |
| IKFS-2 Fourier spectrometer ROSHYDROMET | METEOR-3M N2, Meteor-M No1, Meteor-M No2 | TBD | Atmospheric temperature and humidity sounders | Atmospheric temperature and humidity sounding and radiation budget assessment | Waveband: 5-15µm, 1300 spectral channels Spatial resolution: Swath width: 2500km Accuracy: 1K |
| IKOR-M The modernized measuring instrument of short-wave reflected radiation ROSKOSMOS | Meteor-M No1, Meteor-M No2 |  | Earth radiation budget radiometer |  | Waveband: Spatial resolution: Swath width: Accuracy: |
| Imager NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Operational | Imaging multi-spectral radiometers (vis/IR) | Measures cloud cover, atmospheric radiance, winds, atmospheric stability, rainfall estimates. Used to provide severe storm warnings/ monitoring day and night (type, amount, storm features) | Waveband: GOES 8-12; N,O,P: VIS: 1 channel (8 detectors), IR: 4 channels: 3.9, 6.7, 10.7 and 12µm, GOES 12-Q: VIS: 1 channel (8 detectors), IR: 4 channels: 3.9, 6.7, 10.7 and 13.3µm Spatial resolution: 1km in visible 4km in IR (8km for 13.3µm band (water vapour)) Swath width: Full Earth disk Accuracy: |
| Imager (INSAT) ISRO | INSAT-3D | TBD | Imaging multi-spectral radiometers (vis/IR) | Cloud cover, severe storm warnings/monitoring day and night (type, amount, storm features), atmospheric radiance winds, atmospheric stability rainfall | Waveband: VIS: 0.55-0.75µm, SWIR: 1.55-1.7µm, MWIR: 3.80-4.00µm, 6.50-7.00µm, TIR: 10.2-11.3µm, 11.5-12.5µm Spatial resolution: 1x1km (VIS & SWIR), 4x4km (MWIR, TIR), 8x8km (in 6.50-7.00µm) Swath width: Full Earth disc and space around, Normal Frame (50 deg. N to 40 deg. S and full E-W coverage), Program Frame (Programmable, E-W Full coverage) Accuracy: |
| IMAGER/MTSAT-1R Imager/MTSAT JMA | MTSAT-1R | Prototype | Imaging multi-spectral radiometers (vis/IR) | Measures cloud cover, cloud motion, cloud height, water vapour, rainfall, sea surface temparature and Earth radiation | Waveband: VIS-SWIR: 0.55-0.90µm, MWIR-TIR: 3.5-4µm, 6.5-7µm, 10.5-11.3µm, 11.5-12.5µm Spatial resolution: Visible: 1km, TIR: 4km Swath width: Full Earth disk every hour Accuracy: |
| IMAGER/MTSAT-2 Imager/MTSAT JMA | MTSAT-2 | Prototype | Imaging multi-spectral radiometers (vis/IR) | Measures cloud cover, cloud motion, cloud height, water vapour, rainfall, sea surface temparature and Earth radiation | Waveband: VIS-SWIR: 0.55-0.90µm, MWIR-TIR: 3.5-4µm, 6.5-7µm, 10.5-11.3µm, 11.5-12.5µm Spatial resolution: Visible: 1km, TIR: 4km Swath width: Full Earth disk every hour Accuracy: |
| IMSC Instrument Search Coil Magnetometer CNES | DEMETER | Operational | Magnetic field | Magnetic field | Waveband: 10Hz - 17.4kHz Spatial resolution: Swath width: Accuracy: |
| IMWTS Improved MicroWave Temperature Sounder NRSCC (CAST) | FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Approved | Atmospheric temperature and humidity sounders | Atmospheric temperature soundings for meteorological applications | Waveband: Microwave: 50-57GHz (4channels) Spatial resolution: 50km Swath width: ±48º Accuracy: |
| INES Italian Navigation Experiment ASI | SAC-C | Operational | Precision orbit | Composed of GPS Tensor and GNSS Lagrange Receiver to perform navigation experiment on precise orbit determination. | Precision positioning only – not an Earth observing instrument. |
| IR (HJ-1B) Infrared Camera CAST | HJ-1B | Being developed | Imaging multi-spectral radiometers (vis/IR) | Global environmental applications | Waveband: 0.75~1.10, 1.55~1.75, 3.50 ~3.90, 10.5 ~12.5µm Spatial resolution: 300m (10.5~12.5μm), 150m (the other bands) Swath width: 720km Accuracy: |
| IR Camera (SAOCOM) CONAE | SAOCOM 1A, SAOCOM 1B, SAOCOM-2B (1), SAOCOM-2B (2) | Being developed | Imaging multi-spectral radiometers (vis/IR) | Fires monitoring | Waveband: NIR-TIR Spatial resolution: 200m Swath width: Accuracy: |
| IRAS InfraRed Atmospheric Sounder NRSCC (CAST) | FY-3A, FY-3B, FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Approved | Atmospheric temperature and humidity sounders | Atmospheric sounding for weather forecasting | Waveband: VIS-TIR: 0.65-14.95µm (26 channels) Spatial resolution: 1.254km Swath width: ±49.5º Accuracy: |
| IR-MSS Infrared Multispectral Scanner CAST (INPE) | CBERS-2, CBERS-2B | Operational | High resolution optical imagers | Used for fire detection, fire extent and temperature measurement | Waveband: VIS-NIR: 0.5-1.1µm, NIR-SWIR: 1.55-1.75µm, 2.08-2.35µm, TIR: 10.4-12.5µm Spatial resolution: Visible, NIR, SWIR: 78m, TIR: 156m Swath width: 120km Accuracy: |
| IRS CAST (INPE) | CBERS-3, CBERS-4 | Operational | High resolution optical imagers | Used for fire detection, fire extent and temperature measurement | Waveband: VIS-NIR: 0.5-1.1µm, NIR-SWIR: 1.55-1.75µm, 2.08-2.35µm, TIR: 10.4-12.5µm Spatial resolution: Visible, NIR, SWIR: 78m, TIR: 156m Swath width: 120km Accuracy: |
| ISAMS Improved Stratospheric and Mesospheric Sounder instrument NASA | UARS | Not operational | Earth radiation budget radiometer | Concentrations of nitrogen chemical species, ozone, water vapour, methane, and carbon monoxide. Aerosols. Atmospheric temperature | Waveband: SWIR-TIR: 4.6-16.6µm Spatial resolution: vert 2.6km, horiz: 18km Swath width: 65km Accuracy: |
| ISL Langmuir probes CNES | DEMETER | Operational | Space Environment | Density of the plasma and electron temperature | Waveband: Spatial resolution: Swath width: Accuracy: Relative ion and electron density <5%, Absolute temperature <5%, Potential 10mV Ion direction +15° |
| IST Italian Star Tracker ASI | SAC-C | Operational | Precision orbit | Test of a fully autonomous system for attitude and orbit determination using a star tracker | Precision positioning only – not an Earth observing instrument. |
| IVISSR (FY-2) Improved Multispectral Visible and Infra-red Spin Radiometer (5 channels) NRSCC (CAST) | FY-2C, FY-2D, FY-2E | Approved | Imaging multi-spectral radiometers (vis/IR) | Meteorological | Waveband: VIS-TIR: 0.55-0.9, 10.3-11.3, 11.5-12.5, 6.5-7.0, 3.5-4.0µm (5 channels) Spatial resolution: 1.4km, 5km Swath width: Accuracy: |
| JMR 'JASON Microwave Radiometer NASA | Jason, Jason-2 (also known as OSTM) | Operational | Imaging multi-spectral radiometers (passive microwave) | Provides altimeter data to correct for errors caused by water vapour and cloud-cover. Also measures total water vapour and brightness temperature | Waveband: Microwave: 18.7GHz, 23.8GHz, 34GHz Spatial resolution: 41.6km at 18.7GHz, 36.1km at 23.8GHz, 22.9km at 34GHz Swath width: 120 deg cone centred on nadir Accuracy: Total water vapour: 0.2g/sq cm, Brightness temperature: 0.15 K |
| KGI-4C Module for Geophysical Measurements ROSHYDROMET | METEOR-3M N1 | Prototype | Earth radiation budget radiometer | Measures particle flux and electromagnetic emissions | Waveband: Electron flux density range: 0.15-3.2MeV, proton flux density range: 5- 90MeV, Protons density of energy more that 600 MeV (5-10 channels) Spatial resolution: 8-12km Swath width: 3100km Accuracy: 1.6K |
| Klimat Scanning IR radiometer ROSHYDROMET | METEOR-3M N1 | Operational | Imaging multi-spectral radiometers (vis/IR) | Provides images of cloud, ice and snow. Measures sea surface temparature | Waveband: TIR: 10.5-12.5µm Spatial resolution: 0.45km x 0.9km Swath width: 1300km Accuracy: |
| KMSS Medium range multi-spectral scanner ROSHYDROMET (ROSKOSMOS) | METEOR-3M N2, Meteor-M No1, Meteor-M No2 | Operational | Imaging multi-spectral radiometers (passive microwave) | Moderate resolution imaging applications | Waveband: Microwave:0.45-0.50, 0.535-0.575, 0.63-0.68, 0.76-0.9µm Spatial resolution: 70m Swath width: 1000-1200km Accuracy: |
| LAC Laser Atmospheric Corrector NASA | NMP EO-1 | Operational | Imaging multi-spectral radiometers (vis/IR) | Corrects high spatial resolution multispectral imager data for atmospheric effects | Waveband: 256 bands, NIR-SWIR: 0.89-1.58µm Spatial resolution: 250m Swath width: 185km Accuracy: |
| Landsat Comms Communications package for Landsat USGS | Landsat-5, Landsat-7 | Operational | Communications |  | Data communications only. |
| Laser reflectors CNES | STARLETTE, STELLA | Operational | Precision orbit | Measures distance between the satellite and the laser tracking stations | 24cm sphere covered in 60 retro-reflectors |
| Laser reflectors (ESA) Laser reflectors ESA | CRYOSAT, GOCE | TBD | Precision orbit | Measures distance between the satellite and the laser tracking stations | Cluster of 9 laser reflectors provide orbit determination with cm accuracy using laser ground stations. |
| L-band SAR INPE | SSR-2 | Proposed | Imaging microwave radars | Microwave imaging of land and ice for use in environmental monitoring, agriculture and forestry, disaster monitoring, Earth resource management and interferometry | Waveband: Spatial resolution: Swath width: Accuracy: |
| LISS-III Linear Imaging Self Scanner - III ISRO | RESOURCESAT-1, RESOURCESAT-2 | Operational | High resolution optical imagers | Data used for vegetation type assessment, resource assessment, crop stress detection, crop production forecasting, forestry, land use and land cover change | Waveband: VIS: Band 2: 0.52-0.59µm, Band 3: 0.62-0.68µm, NIR: Band 4: 0.77-0.86µm, SWIR: Band 5: 1.55-1.75µm Spatial resolution: Bands 2, 3 & 4: 23.5m, Band 5: 70.5m Swath width: 140km Accuracy: |
| LISS-IV Linear Imaging Self Scanner - IV ISRO | RESOURCESAT-1, RESOURCESAT-2 | Operational | High resolution optical imagers | Vegetation monitoring, improved crop discrimination, crop yield, disaster monitoring and rapid assessment of natural resources | Waveband: VIS: 0.52-0.59µm, 0.62-0.68µm, NIR: 0.77-0.86µm, Spatial resolution: 5.8m Swath width: 70km Accuracy: |
| LRA Laser Retroreflector Array NASA (ASI) | Jason, Jason-2 (also known as OSTM), Topex-Poseidon | Operational | Precision orbit | Provides baseline tracking data for precision orbit determination and/or geodesy. Also for calibration of radar altimeter bias. Several types used on various missions. (ASI involved in LAGEOS 2 development) | The LRA is an array of mirrors that provide a target for laser tracking measurements from the ground. By analyzing the round-trip time of the laser beam, we can locate very precisely where the satellite is on its orbit. |
| LRA (LAGEOS) Laser Retroreflector Array NASA (ASI) | LAGEOS-1, LAGEOS-2, LAGEOS-3 | Being developed | Precision orbit | Provides baseline tracking data for precision geodesy. Also for calibration of radar altimeter bias. Several types used on various missions. (ASI involved in LAGEOS 2 development) | The LAGEOS satellites are passive vehicles covered with retro-reflectors designed to reflect laser beams transmitted from ground stations. Accuracy: 2cm overhead ranging |
| L-SAR L-Band SAR BNSC | TerraSAR-L | Prototype | Imaging microwave radars | L-Band Sar for agriculture and forestry | Waveband: Microwave: L-band (2GHz) Spatial resolution: 5m Swath width: 10-200km depending on mode Accuracy: |
| MADRAS CNES | MEGHA-TROPIQUES | Operational | Imaging multi-spectral radiometers (passive microwave) | Studies precipitation and clouds properties | Data not yet available. |
| MAESTRO Measurements of Aerosol Extinction in the Stratosphere and Troposphere Retrieved by Occultation CSA | SCISAT-1 | Operational | Atmospheric chemistry | Will aid in the SCISAT-1 overall mission of increasing our understanding of the chemical processes involved in the depletion of the ozone layer. | Waveband: UV-NIR: 0.285 to 1.03um (1-2nm spectral resolution) Spatial resolution: Approx 1km vertical Swath width: Accuracy: |
| Magnetometer (NOAA) Magnetometer NOAA | GOES-R | Approved | Magnetic field | Measures magnitude and direction of Earth's ambient magnetic field in three orthogonal directions in an Earth referenced coordinate system. Will provide a map of the space environment that controls charged particle dynamics in the outer region of the magnetosphere. | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| MASTER ESA | ESA Future Missions | TBD | Atmospheric temperature and humidity sounders & Atmospheric chemistry instruments | Data for study of exchange mechanisms between stratosphere/troposphere, and information for studies on global change. Measures upper troposphere/ lower stratosphere profiles of O3, H2O, CO, HNO3, SO2, N2O, pressure and temperature | Waveband: Microwave: 199-207, 296-306, 318-326, 342-348GHz Spatial resolution: 3km Swath width: Accuracy: 199-207GHz channel: 1K, Other channels: 1.5K, 50MHz resolution, 0.3 secs integration time |
| MBEI Multi-band Earth Imager NSAU | SICH-2 | Approved | High resolution optical imagers | Multispectral scanner images of land surface | Waveband: VIS-NIR: 0.50-0.885µm, VIS: 0.50-0.59, 0.605-0.68µm, NIR: 0.785-0.885µm Spatial resolution: 7.8m Swath width: 46.6km pointable ±35° from nadir Accuracy: |
| MCP Meteorological Communications Package (MCP) EUMETSAT | METOP-1, METOP-2, METOP-3 | TBD | Communications | Meteorological Communications Package (MCP) onboard METOP series satellites | Data communication only. |
| MERIS Medium-Resolution Imaging Spectrometer ESA | Envisat | Operational | Imaging multi-spectral radiometers (vis/IR) | Main objective is monitoring marine biophysical and biochemical parameters. Secondary objectives are related to atmospheric properties such as cloud and water vapour and to vegetation conditions on land surfaces | Waveband: VIS-NIR: 15 bands selectable across range: 0.4-1.05µm (bandwidth programmable between 0.0025 and 0.03µm) Spatial resolution: Ocean: 1040m x 1200 m, Land & coast: 260m x 300m Swath width: 1150km, global coverage every 3 days Accuracy: Ocean colour bands typical S:N = 1700 |
| MERSI Moderate Resolution Spectral Imager NRSCC (CAST) | FY-3A, FY-3B, FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Approved | Imaging multi-spectral radiometers (vis/IR) | Measures surface temparature and cloud and ice cover. Used for snow and flood monitoring and surface temperature | Waveband: VIS-TIR: 0.47-12.5µm (20 channels) Spatial resolution: 250m-1.1km Swath width: 3200km Accuracy: |
| METEOSAT Comms Communications package for METEOSAT EUMETSAT | METEOSAT-5, METEOSAT-6, METEOSAT-7 | Prototype | Communications | Communication package onboard METEOSAT series satellites | Data communication only. |
| MHS Microwave Humidity Sounder EUMETSAT | METOP-1, METOP-2, METOP-3, NOAA-N, NOAA-N' | Prototype | Atmospheric temperature and humidity sounders | Provides atmospheric humidity profiles, cloud cover, cloud liquid, water content, ice boundaries and precipitation data | Waveband: Microwave: 89, 166GHz and 3 channels near 183Ghz Spatial resolution: Vertical: 3-7km, Horizontal: 30-50km Swath width: 1650km Accuracy: Cloud water profile: 10g/m2, Specific humidity profile: 10-20% |
| MIPAS Michelson Interferometric Passive Atmosphere Sounder ESA | Envisat | Operational | Atmospheric chemistry instruments & Atmospheric temperature and humidity sounders | Provides data on stratosphere chemistry (global/polar ozone), climate research (trace gases/clouds), transport dynamics, tropospheric chemistry. Primary/secondary species: O3, NO, NO2, HNO3, N2O5, ClONO2, CH4 | Waveband: MWIR-TIR: between 4.15 and 14.6µm Spatial resolution: Vertical resolution: 3km, vertical scan range 5-150km, Horizontal: 3km x 30km, Spectral resolution: 0.035 lines/cm Swath width: Accuracy: Radiometric precision: 685-970cm-1: 1%, 2410 cm-1: 3% |
| MIRAS Multichannel Infrared Atmospheric Sounder NRSCC (CAST) | FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Prototype | Imaging multi-spectral radiometers (passive microwave) | Atmospheric sounding for weather forecasting | No data available |
| MIRAS (SMOS) 2-D Passive L-Band Microwave Interferometer ESA | SMOS | Proposed | Multiple direction/polarisation radiometers & Imaging multi-spectral radiometers (passive microwave) | Objective is to demonstrate observations of sea surface salinity and soil moisture in suport of climate, meteorology, hydrology, and oceanography applications. | Waveband: Microwave: L-Band 1.41GHz (based on MIRAS concept) Spatial resolution: Requirements: Soil moisture: 30km (desired), Sea surface salinity: 200km (desired) Swath width: 934km (at 756km altitude), allowing a 3 day revisit time at the equator Accuracy: Radiometric accuracy: 3.5K for land, 2.5K for sea |
| MIREI Middle IR Earth Imager NSAU | SICH-2 | Approved | High resolution optical imagers | Scanner images of land surface | Waveband: NIR: 1.55-1.7µm Spatial resolution: 39.5m Swath width: 55.3 km pointable ±35° from nadir Accuracy: |
| MISR Multi-angle Imaging SpectroRadiometer NASA | Terra | Operational | Multiple direction/polarisation radiometers | Provides measurements of global surface albedo, aerosol and vegetation properties. Also provides multi-angle bidirectional data (1% angle-to-angle accuracy) for cloud cover and reflectances at the surface and aerosol opacities. Global and local modes. | Waveband: VIS: 0.44, 0.56, 0.67µm, NIR: 0.86µm Spatial resolution: 275m, 550m or 1.1km, Summation modes available on selected cameras/bands: 1x1, 2x2, 4x4, 1x4. 1 pixel = 275m x 275m Swath width: 360km common overlap of all 9 cameras Accuracy: 0.03% hemispherical albedo, 10% aerosol opacity, 1-2% angle to angle accuracy in bidirectional reflectance |
| MIVZA Microwave scanning radiometer ROSHYDROMET | METEOR-3M N1 | Prototype | Atmospheric temperature and humidity sounders | Microwave radiometer for humidity sounding of atmosphere | Waveband: Microwave:22-94 GHz, 5 channels Spatial resolution: 25-100km Swath width: 1500m Accuracy: |
| MLS Microwave Limb Sounder NASA | Aura | Operational | Atmospheric temperature and humidity sounders & Atmospheric chemistry instruments | Provides data on emissions of chlorine monoxide, water vapour and ozone. Data also used for determination of atmospheric pressure and temperatures as a function of altitude from observations of molecular oxygen emissions | Waveband: 118GHz, 190GHz, 240GHz, 640GHz, 2.5THz Spatial resolution: Measurements are performed along the sub-orbital track, and resolution varies for different parameters; 5 km cross-track x 500 km along-track x 3 km vertical are typical values. Swath width: 1.5 km vertical x 3 km cross-track x 300 km along-track at the limb tangent point Accuracy: Depends on measurement |
| MMP Magnetic Mapping Payload CONAE (DSRI (Denmark)) | SAC-C | Operational | Magnetic field | Measurement of the Earth’s magnetic field with a vector and a scalar magnetometer | Waveband: Scalar (SHM) 1nTeslaVectorial 3-5 nT Spatial resolution: Res angular 20 sec arc Swath width: Vector 0.5 nT Accuracy: |
| MMRS Multispectral Medium Resolution Scanner CONAE | SAC-C | Operational | Imaging multi-spectral radiometers (vis/IR) | Applications related to agriculture, environment, forestry, hydrology, oceanography, mineralogy and geology, desertification, contamination and protection of ecosystems. | Waveband: VIS-NIR: 480 - 500nm, 540-560nm, 630-690nm, 795-835nm, SWIR: 1550-1700nm Spatial resolution: 175m Swath width: 360km Accuracy: |
| MOC Multi-spectral Optical Camera CONAE | SAC-E/SABIA | Approved | Imaging multi-spectral radiometers (vis/IR) |  | Waveband: Spatial resolution: Swath width: Accuracy: |
| MODIS MODerate-Resolution Imaging Spectroradiometer NASA | Aqua, Terra | Operational | Imaging multi-spectral radiometers (vis/IR) & Ocean colour instruments | Data on biological and physical processes on the surface of the Earth and in the lower atmosphere, and on global dynamics. Surface temperatures of land and ocean, chlorophyll fluorescence, land cover measurements, cloud cover (day and night) | Waveband: VIS-TIR: 36 bands in range 0.4-14.4µm Spatial resolution: Cloud cover: 250m (day) and 1000m (night), Surface temperature: 1000m Swath width: 2330km Accuracy: Long wave radiance: 100nW/m2, Short wave radiance: 5%, Surface temperature of land: <1K, Surface temperature of ocean: <0.2K, Snow and ice cover: 10% |
| MOPITT Measurements Of Pollution In The Troposphere CSA | Terra | Prototype | Atmospheric chemistry | Measurements of greenhouse gases (CO, methane) in the troposhere | Waveband: SWIR-MWIR: 2.3, 2.4 and 4.7µm Spatial resolution: CO profile: 4km vertical, 22 x 22km horizontal, CO, CH4 column: 22x22km horizontal Swath width: 616km Accuracy: Carbon monoxide (4km layers): 10%, Methane column: 1% |
| MPS Magnetospheric Particle Sensor NOAA | GOES-R | Approved | Space Environment | Studies of natural radiation hazard to humans at high altitudes and in space, as well as risk assessment and warning of episodes of surface charging, deep dielectric charging, and single event upset of satellite systems. | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| MR-2000M1 Scanning visible radiometer ROSHYDROMET | METEOR-3M N1 | Prototype | Imaging multi-spectral radiometers (vis/IR) | TV camera images of cloud, snow and ice | Waveband: VIS-NIR: 0.5-0.8µm Spatial resolution: 1.5km Swath width: 3100km Accuracy: |
| MS (GISTDA) Multi spectral imager GISTDA | THEOS | Approved | Imaging multi-spectral radiometers (vis/IR) | Land surface applications | Waveband: 0.45-0.52, 0.53-0.60, 0.62-0.69, 0.77-0.90µm Spatial resolution: 15m Swath width: 90km Accuracy: |
| MSC Multi-Spectral Camera KARI | KOMPSAT-2 | Being developed | High resolution optical imagers | High resolution imager for land applications of cartography and disaster monitoring | Waveband: VIS-NIR: 0.50-0.92µm, VIS: 0.45-0.52µm, 0.52-0.60µm, 0.63-0.69µm, NIR: 0.76-0.90µm Spatial resolution: Pan: 1m, VNIR: 4m Swath width: 15km Accuracy: |
| MSG Comms Communications package for MSG EUMETSAT | METEOSAT-8, METEOSAT-9, METEOSAT-10, METEOSAT-11 | Being developed | Communications | Communication package onboard MSG series satellites | Data communication only. |
| MSGI-MKA Spectrometer ROSHYDROMET | METEOR-3M N2, Meteor-M No1, Meteor-M No2 | TBD | Other | Geoactive corpuscular emissions measurments | The MSGI-MKA instrument features four channels for the measurement of the following parameters: Electron fluxes in the energy range of 0.1-15 keV (high-sensitivity channel); Ion (proton) fluxes in the energy range of 0.1-15 keV (high-sensitivity channel); Electron fluxes in the energy range of 0.1-15 keV (low-sensitivity channel); Monitoring of integral electron fluxes with a threshold energy of 40 keV. The Field of View is 10º x 10º for each channel (3) and 20º x 20º for the integral electron flux. |
| MSI Multi Spectral Imager DLR | RapidEye | Approved | High resolution optical imagers | high resolution images with short observing cycle for commercial and scientific applications | Waveband: 4 VIS + 1 NIR band: 440-510nm, 520-590nm, 630-685nm, 690-730nm, 760-850nm Spatial resolution: 6.5m Swath width: 78km Accuracy: 2-3% |
| MSMR Multifrequency Scanning Microwave Radiometer ISRO | IRS-P4 | Operational | Imaging multi-spectral radiometers (passive microwave) | Sea state and meteorological parameter monitoring (sea surface temperature, surface wind speed, water vapour over ocean and liquid water content of the cloud) | Waveband: Microwave: 6.6, 10.6, 18 and 21GHz Spatial resolution: 40m at 21GHz to 120m at 6.6GHz, Wind speed: 75 x 75km, Sea surface temparature: 146 x 150km Swath width: 1360km Accuracy: Sea surface temparature: 1.5K, Sea surface wind speed: 1.5 m/s |
| MSS Multispectral Scanner USGS | Landsat-5 | Operational | Imaging multi-spectral radiometers (vis/IR) | Measures surface radiance. Data mostly used for land applications | Waveband: 0.5-1.1µm Spatial resolution: 82m Swath width: 185km Accuracy: |
| MSS (Roskosmos) Multispectral film-making system ROSKOSMOS | BelKA |  | Imaging multi-spectral radiometers (vis/IR) | Land surface applications | Waveband: VIS-NIR: 0.54-0.6, 0.63-0.69, 0.69-0.72, 0.75-0.86µm Spatial resolution: 12m Swath width: 20km Accuracy: |
| MSS-BIO Polyzonal scanning system of bioefficiency of sea water areas ROSKOSMOS | Meteor-M No1, Meteor-M No2 |  | Ocean colour instruments | Ocean biology applications | Waveband: 0.43-0.48, 0.5-0.58, 0.6-0.68, 0.7-0.9, 2.0-2.3µm Spatial resolution: 60-100m Swath width: 520km Accuracy: |
| MSTE-5E Multichannel system of geoactive measurements ROSHYDROMET | METEOR-3M N1 | TBD | Other | Geoactive Emission Measurements | Waveband: Ions energetic spectrum: 0.1 – 15 keV, 3 channels, Energy of electrons: 0.05 – 20 keV and more than 40 keV, 4 channels Spatial resolution: Swath width: Accuracy: |
| MSU Microwave Sounding Unit NOAA | NOAA-12, NOAA-14 | Operational | Atmospheric temperature and humidity sounders | Provides temperature sounding through cloud up to 20km in altitude | Waveband: 4 channels: 50.3 to 57.95 GHz Spatial resolution: 109.3 km Swath width: 2348 km Accuracy: |
| MSU-E Multispectral high resolution electronic scanner ROSHYDROMET | METEOR-3M N1 | Operational | Imaging multi-spectral radiometers (vis/IR) | Multispectral scanner images of land surface and ice cover | Waveband: VIS: 0.5-0.6, 0.6-0.7µm, NIR: 0.8-0.9µm Spatial resolution: 35-45m Swath width: 45km for one scanner, 80km for two scanners (pointable ±30 deg from nadir) Accuracy: |
| MSU-EU Multi-Spectral Radiometer with High Resolution NSAU | SICH-1M | Being developed | High resolution optical imagers | Multispectral scanner images of land surface | Waveband: VIS: 0.5-0.6, 0.6-0.7µm, NIR: 0.8-0.9µm Spatial resolution: Visible: 24x34m Swath width: 48km or 105km; pointable ±30° from nadir Accuracy: |
| MSU-GS Multispectral scanning imager-radiometer ROSHYDROMET | Elektro-L | TBD | Imaging multi-spectral radiometers (vis/IR) | Measurements of cloud cover, cloud top height, precipitation, cloud motion, vegetation, radiation fluxes, convection, air mass analysis, cirrus cloud discrimination, tropopause monitoring, stability monitoring, total ozone and sea surface temparature | Waveband: VIS: 0.5-0.65, 0.65-0.8µm, NIR: 0.9µm, SWIR: 1.5µm, MWIR: 3.5-4.01µm, TIR: 5.7-7.0, 8-8.7, 9.7, 10.2-11.2, 11.2-12.5µm Spatial resolution: 1km (at SSP) for visible and 4 km for IR channels Swath width: Full Earth disk Accuracy: |
| MSU-M Multi-Spectral Low Resolution Scanning System NSAU | SICH-1M | Prototype | Imaging multi-spectral radiometers (vis/IR) | Provide images of ocean surface and ice sheets | Waveband: VIS: 0.5-0.6, 0.6-0.7µm, NIR: 0.7-0.8, 0.8-1.1µm Spatial resolution: 1.7km x 1.8km Swath width: 1930km Accuracy: |
| MSU-MR Images of clouds, snow, ice and land cover ROSHYDROMET | METEOR-3M N2, Meteor-M No1, Meteor-M No2 | TBD | Imaging multi-spectral radiometers (vis/IR) | Images of clouds, snow, ice and land cover | Waveband: Visible: 0.5-0.7µm, NIR: 0.7-1.1µm, SWIR: 1.6-1.8µm, MWIR: 3.5-4.1µm, TIR: 10.5-11.5µm, 11.5-12.5µm Spatial resolution: 1km Swath width: 3000km Accuracy: VIS: 0.5%, IR: 0.1K |
| MSU-SM Multi-Spectral Medium Resolution Scanning System ROSHYDROMET | METEOR-3M N1 | TBD | Imaging multi-spectral radiometers (vis/IR) | Images of clouds, snow, ice and land cover | Waveband: VIS: 0.5-0.7µm, NIR: 0.7-1.1µm Spatial resolution: 225m Swath width: 2250km Accuracy: |
| MTSAT Comms Communications package for MTSAT JMA (JAXA) | MTSAT-1R, MTSAT-2 | Prototype | Communications |  | Data communication only |
| MTVZA Scanning microwave radiometer ROSHYDROMET | METEOR-3M N1, METEOR-3M N2, Meteor-M No1, Meteor-M No2 | Prototype | Atmospheric temperature and humidity sounders | Provision of atmospheric temparature and humidity profiles | Waveband: Microwave:18.7-183 GHz, 52-55 GHz, 19 channels Spatial resolution: 12x22km to 75x136km Swath width: 2200km Accuracy: |
| MTVZA-OK Scanning microwave radiometer ROSHYDROMET | Kanopus-Vulkan, SICH-1M | Approved | Atmospheric temperature and humidity sounders | Multi-Spectral Scanner Images of Earth Surface | Waveband: MW: 6.9, 10.6, 18.7, 23.8, 31.5, 36.7, 42, 48, 52.3-57.0, 89, 183.32 GHz, VIS: 0.37-0.45, 0.45-0.51, 0.58-0.68, 0.68-0.78µm, MWIR:3.55-3.93µm Spatial resolution: MW: 12-260km, VIS: 0.96km, MWIR:1.1km Swath width: MW: 2000km VIS: 1280km, MWIR: 1850km Accuracy: |
| MUX Multispectral CCD Camera CAST (INPE) | CBERS-3, CBERS-4 | Being developed | Imaging multi-spectral radiometers (vis/IR) | Earth resources, environmental monitoring, land use | Waveband: Spatial resolution: 20m Swath width: Accuracy: |
| MVIRI METEOSAT Visible and Infra-Red Imager EUMETSAT (ESA) | METEOSAT-5, METEOSAT-6, METEOSAT-7 | Operational | Imaging multi-spectral radiometers (vis/IR) | Measures cloud cover, motion, height, upper tropospheric humidity and sea surface temperature | Waveband: VIS-NIR: 0.5-0.9µm, TIR: 5.7-7.1µm (water vapour), 10.5-12.5µm Spatial resolution: Visible: 2.5km, Water vapour: 5km (after processing), TIR: 5 km Swath width: Full Earth disk in all three channels, every 30 minutes Accuracy: Cloud top height: 0.5km, Cloud top/ sea surface temperature: 0.7K, Cloud cover 15% |
| MWHS MicroWave Humidity Sounder NRSCC (CAST) | FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Approved | Atmospheric temperature and humidity sounders | Meteorological applications | Waveband: Microwave: 150-183GHz (5channels) Spatial resolution: 15km Swath width: ±48º Accuracy: |
| MWR (BNSC) Microwave Radiometer BNSC | Envisat, ERS-2 | Operational | Imaging multi-spectral radiometers (passive microwave) & Atmospheric temperature and humidity sounders | To provide multispectral analysis of hydrological, oceanographic, land use and meteorological parameters. Global imager & SST. Ocean colour | Waveband: Microwave: 23.8 and 36.5GHz Spatial resolution: 20km Swath width: 20km Accuracy: Temparature: 2.6K |
| MWR (CONAE) Microwave radiometer CONAE | SAC-D/Aquarius | Approved | Imaging multi-spectral radiometers (passive microwave) | The Aquarius mission will measure global sea surface salinity with unprecedented resolution. The instruments include a set of three radiometers that are sensitive to salinity (1.413 GHz; L-band). The scatterometer corrects for the ocean's surface roughness. | Waveband: Ka Band (23.8 and 36.56 GHz) Spatial resolution: 400km Swath width: 300km Accuracy: .5K |
| MWRI MicroWave Radiation Imager NRSCC (CAST) | FY-3A, FY-3B, FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Approved | Imaging multi-spectral radiometers (passive microwave) | Meteorological applications | Waveband: 10.65-89GHz (10channels) Spatial resolution: 15-80km Swath width: 1400km Accuracy: |
| MWTS MicroWave Temperature Sounder NRSCC (CAST) | FY-3A, FY-3B | Approved | Atmospheric temperature and humidity sounders | Meteorological applications | Waveband: Microwave: 50-57GHz (4channels) Spatial resolution: 50km Swath width: ±48º Accuracy: |
| NIRST New Infrared Sensor Technology CONAE | SAC-D/Aquarius | Approved | Imaging multi-spectral radiometers (vis/IR) | Fire area, Fire Temperature, Volcanic ash | Waveband: 3.5-4.5µm, 10.5-11.5µ, 11.5-12.5µm Spatial resolution: 150m Swath width: Normal mode: 75km, Accessible swath width: 700km Accuracy: |
| NISTAR NIST Advanced Radiometer NASA | DSCOVR | Approved | Earth radiation budget radiometer | Measures radiance output from the sunlit Earth over a broad spectrum (UV and VIS reflected and IR emitted) to detect energy balance changes in support of climate studies | Waveband: UV-FIR: 0.2-100µm, 0.2-4µm, 0.7-4µm, 0.3-1µm Spatial resolution: Swath width: Full Earth disk Accuracy: Total Earth reflected and emitted power to within 0.1% |
| NOAA Comms Communications package for NOAA NOAA | NOAA-12, NOAA-14, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Prototype | Communications |  | Data communication only. |
| NVK Low-frequency wave complex ROSKOSMOS | Kanopus-Vulkan, Vulkan-Kompas-2 |  | Other | Geomagnetic applications related to volcanoes and earthquakes | Waveband: 1Hz - 25kHz Spatial resolution: Swath width: Accuracy: |
| OBA Observador Brasileiro da Amazonia INPE | SSR-1, SSR-2 | Approved | Imaging multi-spectral radiometers (vis/IR) | Used for fire extent detection and temperature measurement, coastal and vegetation monitoring, land cover and land use mapping | Waveband: VIS: 0.45-0.50µm, 0.52-0.57µm, 0.63-0.69µm, NIR: 0.76-0.90µm, MWIR: 3.4-4.2µm Spatial resolution: VIS-NIR: 100m, MIR: 300m Swath width: 2200km (equatorial belt from latitude 5N to 15S) Accuracy: |
| OCM Ocean Colour Monitor ISRO | IRS-P4, OCEANSAT-2 | Operational | Ocean colour instruments | Ocean colour information, coastal zone monitoring, land resources monitoring | Waveband: VIS-NIR: 0.40-0.88µm (8 channels) Spatial resolution: 236m x 360m Swath width: 1440km Accuracy: |
| OCO Orbiting Carbon Observatory NASA | OCO |  | Atmospheric chemistry | Precise global maps of carbon dioxide (CO2) in the Earth's atmosphere. Scientists will analyse OCO data to improve our understanding of the natural processes and human activities that regulate the distribution of CO2 in the atmosphere. | The Orbiting Carbon Observatory (OCO) is a single instrument consisting of three high resolution grating spectrometers that flies on a dedicated spacecraft. Each spectrometer detects the intensity of radiation within a very specific narrow band at Near Infrared (NIR) wavelengths. |
| OEA Optical-electronic equipment ROSKOSMOS | Baumanets |  | Imaging multi-spectral radiometers (vis/IR) |  | Waveband: 0.5-0.9µm Spatial resolution: 50m Swath width: 100km Accuracy: |
| OLS Operational Linescan System NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19 | Operational | Imaging multi-spectral radiometers (vis/IR) | Day and night cloud cover imagery | Waveband: VIS-NIR: 0.4-1.1µm, TIR: 10.0-13.4µm, and 0.47-0.95µm Spatial resolution: 0.56km (fine), 5.4km (stereo products) Swath width: 3000km Accuracy: |
| OMI Ozone Measuring Instrument NASA (NIVR (Netherland)) | Aura | Operational | Atmospheric chemistry | Mapping of ozone columns, key air quality components (NO2, SO2, BrO, OClO and aerosols), measurements of cloud pressure and coverage, global distribution and trends in UV-B radiation | Waveband: UV: 270-314nm & 306-380nm, VIS: 350-500nm Spatial resolution: 13km x 24km or 36km x 48km depending on the product. Also has zoom modes (13km x 13km) for example for urban pollution detection Swath width: 2600km Accuracy: |
| OMPS Ozone Mapping and Profiler Suite NOAA | NPOESS-2, NPOESS-5, NPP | Being developed | Atmospheric chemistry | Measures total amount of ozone in the atmosphere and the ozone concentration variation with altitude | Waveband: Nadir Mapper: UV 0.3-0.38µm, Nadir profiler: UV 0.25-0.31µm, Limb soundings: UV-TIR 0.29-10µm Spatial resolution: Mapper: 50km, Profiler: 250km, Limb: 1km vertical Swath width: Mapper: 2800km, Profiler: 250km, Limb: 3 vertical slits along track +/- 250km Accuracy: Total Ozone 15 Dobson units.Profile Ozone10% between 15 and 60km20% between Tropopause and 15km |
| OP Ozone Profiler NRSCC (CAST) | FY-3A, FY-3B, FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Being developed | Atmospheric chemistry | Ozone chemistry measurements | Waveband: UV Spatial resolution: 200km Swath width: Accuracy: |
| OSIRIS Optical Spectrograph and Infra-Red Imaging System CSA | Odin | Prototype | Atmospheric chemistry | Detects aerosol layers and abundance of species such as O3, NO2, OClO, and NO. Consists of spectrograph and IR imager. Measures temperature for altitudes above 30km. | Waveband: Spectrograph: UV-NIR: 0.28-0.80µm, IR Imager, NIR: 1.26µm, 1.27µm, 1.52µm Spatial resolution: Spectrograph 1km at limb, Imager 1km in vertical Swath width: N/A, but measures in the altitude range 5-100 km Accuracy: Depends on species |
| OSMI Ocean Scanning Multispectral Imager KARI | KOMPSAT-1 | Operational | Imaging multi-spectral radiometers (vis/IR) & Ocean colour instruments | Ocean color measurements for biological oceanography | Waveband: VIS: 0.412µm, 0.443µm, 0.490µm, 0.555µm, NIR: 0.765µm, 0.865µm Spatial resolution: 1km Swath width: 800km Accuracy: |
| PALSAR Phased Array type L-band Synthetic Aperture Radar JAXA (METI (Japan)) | ALOS | Being developed | Imaging microwave radars | High resolution microwave imaging of land and ice for use in environmental monitoring, agriculture and forestry, disaster monitoring, Earth resource management and interferometry | Waveband: Microwave: L-Band 1270MHz Spatial resolution: Hi-res: 7-44m or 14-88m (depends on polarisation and looks), ScanSAR mode: <100m, Polarimetry 24-88m Swath width: High resolution mode: 70km, Scan SAR mode: 250-360km, Polarimetry: 30km Accuracy: Radiometric: ±1dB |
| Pamela ROSKOSMOS | Resurs DK |  | Space Environment | Measures the energy spectrum of antiprotons and positrons in the cosmic radiation. Will allow significant comparisons between competing models of antimatter production in our galaxy. | PAMELA consists of a time-of-flight / trigger system, transition radiation detector, a magnetic spectrometer with silicon tracking, an anticoincidence system, a silicon-tungsten imaging electromagnetic calorimeter, a shower-tail catcher and a neutron counter. |
| PAN Panchromatic and multispectral imager CAST | CBERS-3, CBERS-4 | Being developed | High resolution optical imagers | Provides measurements of cloud type and extent and land surface reflectance, and used for global land surface applications | Waveband: VIS: 0.52-0.59µm, 0.63-0.69µm, NIR: 0.77-0.89µm, PAN: 0.51-0.85µm Spatial resolution: 5m panchromatic and 10m multispectral Swath width: 60 km Accuracy: |
| PAN (Cartosat-1) Panchromatic sensor ISRO | CARTOSAT-1 | Operational | High resolution optical imagers | High resolution stereo images for study of topography, urban areas, development of DTM, run-off models etc. Urban sprawl, forest cover/timber volume, land use change | Waveband: Panchromatic VIS: 0.5-0.75µm Spatial resolution: 2.5m Swath width: Accuracy: |
| PAN (GISTDA) Panchromatic imager GISTDA | THEOS | Approved | High resolution optical imagers | Land surface applications | Waveband: 0.45-0.90µm Spatial resolution: 2m Swath width: 22km Accuracy: |
| PEM Particle Environment Monitor NASA | UARS | Operational | Magnetic field | PEM measures UV and charged particle energy inputs: determines type, amount, energy and distribution of charged particles injected into Earth's thermosphere, mesosphere and stratosphere | There are four PEM ‘instruments’, AXIS, HEPS, MEPS, and VMAG. Their purpose is to provide quantitative measurements of both local and global energy inputs into the Earth's atmosphere by charged particles and Joule dissipation – via measurements of x-rays, charged particles, and the magnetic field. |
| Plasma-Mag NASA | DSCOVR | Proposed | Magnetic field & Space environment | Sun-viewing instrument to measure the solar wind and magnetic field parameters. Also serves as early-warning for solar-event storms that could damage satellites and equipment on Earth | Plasma-Mag contains a triaxal fluxgate magnetometer that will investigate solar- wind magnetic fields with a sensitivity level of better than 0.1nT. |
| Pleiades HR High Resolution Optical Imaging CNES | Pleiades 1, Pleiades 2 |  | High resolution optical imagers | Cartography, land use, risk,agriculture and forestry, civil planning and mapping, digital terrain models, defense | Waveband: 4 bands:Near IR, Red, Green, Blue Spatial resolution: <1m Swath width: in vertical: 20km Accuracy: |
| POLDER-P POLarization and Directionality of the Earth's Reflectances (PARASOL version) CNES | PARASOL | Approved | Multiple direction/polarisation radiometers | Measures polarization, and directional and spectral characteristics of the solar light reflected by aerosols, clouds, oceans and land surfaces | Waveband: VIS-NIR: 0.490, 0.670 and 0.865µm at 3 polarisations, and 0.49, 0.565, 0.763, 0.765, 0.91µm, and 1.02µm with no polarisation Spatial resolution: 5.5km x 5.5km Swath width: 1600km Accuracy: Radiation budget, land surface, Reflectance: 2% |
| POSEIDON-1 (SSALT-1) Positioning Ocean Solid Earth Ice Dynamics Orbiting Navigator (Single frequency solid state radar altimeter) CNES | Topex-Poseidon | Operational | Radar altimeters | Nadir viewing sounding radar for provision of real-time high precision sea surface topography, ocean circulation and wave height data | Waveband: Microwave: Ku-band (13.575GHz) Spatial resolution: Swath width: Accuracy: |
| POSEIDON-2 (SSALT-2) Positioning Ocean Solid Earth Ice Dynamics Orbiting Navigator (Single frequency solid state radar altimeter) CNES | Jason | Operational | Radar altimeters | Nadir viewing sounding radar for provision of real-time high precision sea surface topography, ocean circulation and wave height data | Waveband: Microwave: Ku-band (13.575GHz), C-band (5.3GHz) Spatial resolution: Basic measurement: 1/sec (6km along track), Raw measurement: 10/sec (600m along track) Swath width: On baseline TOPEX/POSEIDON orbit (10 day cycle): 300km between tracks at equator Accuracy: Sea level: 3.9cm, Significant waveheight: 0.5m, Horizontal sea surface wind speed: 2m/s |
| POSEIDON-3 Positioning Ocean Solid Earth Ice Dynamics Orbiting Navigator (Single frequency solid state radar altimeter) CNES | Jason-2 (also known as OSTM) | Operational | Radar altimeters | Nadir viewing sounding radar for provision of real-time high precision sea surface topography, ocean circulation and wave height data | Waveband: Microwave: Ku-band (13.575GHz), C-band (5.3GHz) Spatial resolution: Basic measurement: 1/sec (6km along track), Raw measurement: 10/sec (600m along track) Swath width: On baseline TOPEX/POSEIDON orbit (10 day cycle): 300km between tracks at equator Accuracy: Sea level: 3.9cm, Significant waveheight: 0.5m, Horizontal sea surface wind speed: 2m/s |
| PREMOS PREcision Monitoring of Solar variability CNES | PICARD | TBD | Earth radiation budget radiometer | Solar UV and visible flux in selected wavelength bands. | Waveband: UV: 230nm, 311nm, 402nm; VIS: 548 nm Spatial resolution: Swath width: Accuracy: |
| PRISM Panchromatic Remote-sensing Instrument for Stereo Mapping JAXA | ALOS | Being developed | High resolution optical imagers | High resolution panchromatic stereo imager for land applications which include cartography, digital terrain models, civil planning, agriculture and forestry | Waveband: VIS-NIR: 0.52-0.77µm (panchromatic) Spatial resolution: 2.5m Swath width: 35km (triplet stereo observations), 70km (nadir observations) Accuracy: |
| PSA Panchromatic film-making equipment ROSKOSMOS | Monitor-E |  | Imaging multi-spectral radiometers (vis/IR) | High resolution thematic mapping, agriculture and forestry | Waveband: VIS-NIR: 0.51-0.85µm Spatial resolution: 8m Swath width: 90/730km Accuracy: |
| PSS Panchromatic film-making system ROSKOSMOS | BelKA |  | Imaging multi-spectral radiometers (vis/IR) | High resolution mapping, environmental, and resource survey applications | Waveband: VIS-NIR: 0.52-0.85µm Spatial resolution: 3.2m Swath width: 23km Accuracy: |
| RA Radar Altimeter ESA | ERS-2 | Operational | Radar altimeters | Measures wind speed, significant wave height, sea surface elevation, ice profile, land and ice topography,and sea ice boundaries | Waveband: Microwave: Ku-band: 13.8GHz Spatial resolution: Footprint is 16-20km Swath width: Accuracy: Wave height: 0.5m or 10% (whichever is smaller) Sea surface elevation: better than 10cm |
| RA-2 Radar Altimeter - 2 ESA | Envisat | Operational | Radar altimeters | Measures wind speed, significant wave height, sea surface elevation, ice profile, land and ice topography, and sea ice boundaries | Waveband: Microwave: 13.575Ghz (Ku-Band) & 3.2GHz (S-Band) Spatial resolution: Swath width: Accuracy: Altitude: better than 4.5cm, Wave height: better than 5% or 0.25m |
| RADARSAT DTT X band (downlink of payload) CSA | RADARSAT-1 | Operational | Communications |  | Data communication only. |
| RADARSAT TTC S band (Tracking, Telemetry and Command) CSA | RADARSAT-1 | Operational | Communications |  | Data communication only. |
| Radiomet ROSKOSMOS | Meteor-M No1, Meteor-M No2 |  | Atmospheric temperature and humidity sounders | Atmospheric sounding for weather forecasting | Waveband: 3cm, 32cm Spatial resolution: Swath width: Accuracy: |
| RBE ROSKOSMOS | Kanopus-Vulkan, Vulkan-Kompas-2 |  | Magnetic field & Space environment | Geomagnetic applications related to volcanoes and earthquakes | Waveband: 150MHz, 400MHz Spatial resolution: Swath width: Accuracy: |
| RCHA ROSKOSMOS | Kanopus-Vulkan, Vulkan-Kompas-2 |  | Other | Geomagnetic applications related to volcanoes and earthquakes | Waveband: 50kHz -15MHz Spatial resolution: Swath width: Accuracy: |
| RDSA The film-making equipment of the allocated access ROSKOSMOS | Monitor-E |  | Imaging multi-spectral radiometers (vis/IR) | Thematic mapping, agriculture and forestry | Waveband: VIS-NIR: 0.54-0.59, 0.63-0.68, 0.79-0.9µm Spatial resolution: 20/40m Swath width: 160/890km Accuracy: |
| RIMS-M Mass-spectrometer ROSHYDROMET | Meteor-M No1, Meteor-M No2 | TBD | Other | Ion composition in upper atmosphere | Waveband: 1-4 a.e.m., 5-20 a.e.m Spatial resolution: Swath width: Accuracy: |
| RLSBO Side looking microwave radar ROSKOSMOS (NIIRI) | SICH-1M | Prototype | Imaging microwave radars | Provides images of ocean surface and ice sheets | Waveband: Microwave: 3.0cm Spatial resolution: 1.3x2.5 km Swath width: 450km, 700km Accuracy: |
| RM-08 Scanning Microwave Radiometer ROSHYDROMET (NSAU) | SICH-1M | Prototype | Imaging multi-spectral radiometers (passive microwave) | Passive microwave images of ocean surface and ice sheets | Waveband: Microwave: 0.8cm Spatial resolution: 25x25km Swath width: 550km Accuracy: 3K temperature sensitivity |
| ROSA formerly called Lagrange ASI | SAC-D/Aquarius | TBD | Precision orbit & Atmospheric temperature and humidity sounders | GPS Receiver. Including specialized version equipped with limb sounding antenna and dedicated signal tracking capability for metereological,climate and space weather applications.. | Uses observations of GPS satellite occultations in order to supply information about the atmosphere temperature, pressure and water vapour content. |
| RRA Retroreflector Array CNES | Diademe 1&2 |  | Precision orbit | Satellite laser ranging for geodynamic measurements | The RRA consist of 2 flattened truncated cones with 77 cube corners per cone for a total of 144 cube corners. |
| S&R (GOES) Search and Rescue NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Prototype | Other | Satellite and ground based system to detect and locate aviators, mariners, and land-based users in distress. | Communications payload. |
| S&R (NOAA) Search and Rescue Satellite Aided Tracking NOAA | METOP-1, METOP-2, NOAA-14, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Operational | Other | Satellite and ground based system to detect and locate aviators, mariners, and land-based users in distress. | Communications payload. |
| SABER Sounding of the Atmosphere usingBroadband Emission Radiometry NASA | TIMED | Operational | Atmospheric temperature and humidity sounders & Atmospheric chemistry instruments | SABER provides measurements of the mesosphere and lower thermosphere globally to support investigations into the fundamental processes governing the energetics, chemistry, dynamics, and transport of the atmospheric region extending from 60 km to 180 km. | Waveband: NIR-FIR: 1.27µm - 17µm (10 channels) Spatial resolution: 2km vertical resolution Swath width: Accuracy: |
| SAGE II Stratospheric Aerosol and Gas Experiment-II NASA | ERBS | Operational | Atmospheric chemistry | Profiles of ozone, aerosols, NO2, and water vapor. Data suitable for atmospheric chemistry, ozone trend, and climate studies | Waveband: 7 channels, UV-NIR: 0.385 - 1.02 µm Spatial resolution: 0.75 km Swath width: N/A Accuracy: O3- 4%, Aerosol – 1%, NO2 – 15%, H2O- 20% in lower stratosphere |
| SAGE III Stratospheric Aerosol and Gas Experiment-III NASA (ROSKOSMOS) | METEOR-3M N1 | Operational | Atmospheric chemistry | Profiles of ozone, water vapor, NO2, NO3, OCIO, aerosols, temperature and pressure for atmospheric chemistry and climate studies using a 809 element CCD-based grating spectrometer and discrete photodiode channel at 1550 nm | Waveband: UV-NIR: 0.29-1.55µm Spatial resolution: 1-2km vertical resolution Swath width: N/A Accuracy: Temperature: 2K, Ozone: 6%, Humidity: 3-10%, Aerosol and trace gases: 5-10% |
| SAPHIR CNES (ISRO) | MEGHA-TROPIQUES | Approved | Atmospheric temperature and humidity sounders | Cross-track sounder with the objective of measuring water vapour profiles in the troposphere in six layers from 2-12km altitudes. | Waveband: Microwave: 183.3GHz (6 channels) Spatial resolution: 10km Swath width: Accuracy: |
| SAR (RADARSAT) Synthetic Aperture Radar (CSA) C band CSA | RADARSAT-1 | Operational | Imaging microwave radars | Provides all-weather images of ocean, ice and land surfaces. Used for monitoring of coastal zones, polar ice, sea ice, sea state, geological features, vegetation and land surface processes | Waveband: Microwave: C band: 5.3GHz, HH polarisation Spatial resolution: Standard: 25 x28 m (4 looks), Wide beam (1/2):48-30 x 28m/ 32-25 x 28m (4 looks), Fine resolution: 11-9 x 9m (1 look), ScanSAR (N/W): 50 x 50m/ 100 x 100m (2-4/4-8 looks), Extended (H/L): 22-19x28m/ 63-28 x 28m (4 looks) Swath width: Standard: 100km Wide: 150km Fine: 45km ScanSAR Narrow: 300km ScanSAR Wide: 500km Extended (H): 75km Extended (L): 170km Wide: 150km Fine: 45km ScanSAR Narrow: 300km ScanSAR Wide: 500km Extended (H): 75km Extended (L): 170km Accuracy: Geometric distortion: < 40m, Radiometric: 1.0dB |
| SAR (RADARSAT-2) Synthetic Aperture Radar (CSA) C band CSA | RADARSAT-2 | Being developed | Imaging microwave radars | Provides all-weather images of ocean, ice and land surfaces. Used for monitoring of coastal zones, polar ice, sea ice, sea state, geological features, vegetation and land surface processes | Waveband: Microwave: C band 5.405 GHz: HH, VV, HV, VH polarisation - includes fully polarimetric imaging modes, and left- and right-looking capability Spatial resolution: Standard: 25 x28 m (4 looks), Wide beam (1/2):48-30 x 28m/ 32-25 x 28m (4 looks), Fine resolution: 11-9 x 9m (1 look), ScanSAR (N/W): 50 x 50m/ 100 x 100m (2-4/4-8 looks), Extended (H/L): 22-19x28m/ 63-28 x 28m (4 looks), Ultrafine: 3m Swath width: Standard: 100km (20-49deg), Wide beam (1/2): 165km/ 150km (20-31/ 31-39deg), Fine resolution: 45km (37- 48deg), ScanSAR (W): 510km (20-49deg), Extended (H/L): 75km/170km (50-60/ 10-23deg), Ultrafine: 10-20km Accuracy: Geometric distortion: < 40m, Radiometric: 1.0dB |
| SAR (RISAT) ISRO | RISAT-1 | Proposed | Imaging microwave radars | Radar backscatter measurements of land, water and ocean surfaces for applications in soil moisture, crop applications (under cloud cover), terrain mapping etc | Waveband: C-Band (5.350 Ghz) Spatial resolution: 3-6m (FRS-1), 9-12m (FRS-2), 25/50m (MRS/CRS) Swath width: 10km (HRS), 30km (FRS-1/FRS-2), 120/240km (MRS/CRS) Accuracy: |
| SAR (ROSHYDROMET) Synthetic Aperture Radar ROSHYDROMET (ROSKOSMOS) | METEOR-3M N2 | Operational | Imaging microwave radars | Provides all-weather images of ocean, ice and land surfaces. Used for monitoring of coastal zones, polar ice, sea ice, sea state, geological features, vegetation and land surface processes | No data available. |
| SAR (SAOCOM) Synthetic Aperture Radar (CONAE) CONAE | SAOCOM 1A, SAOCOM 1B, SAOCOM-2B (1), SAOCOM-2B (2) | Being developed | Imaging microwave radars | Land and Ocean Emergencies | Waveband: Microwave: L-Band SAR 1.275 GHz Spatial resolution: 10x10m - 100x100m Swath width: Accuracy: 70m |
| SAR 2000 Multi-Mode Synthetic Aperture Radar ASI | COSMO - SkyMed | TBD | Imaging microwave radars | All weather images of ocean, land and ice for monitoring of land surface processes, ice, environmental monitoring, risk management, environmental resources, maritime management, earth topographic mapping. | Waveband: Microwave: X-band, with choice of 4 polarisation modes (VV, HH, VV/HH, HV/HH). Spatial resolution: Single polarisation mode; Stripmap: few metres, ScanSAR: from few tens to several tens of metres; Frame: resolution: order of the m Two polarisation mode· PING PONG: few metres Swath width: Single polarisation modes: Stripmap (tens of km), ScanSAR (hundreds of km), Frame (spot width several tens km2) Two polarisation modes: PING PONG (several tens of km) Accuracy: |
| SARSAT Search and Rescue Satellite Aided Tracking NOAA | NPOESS-1, NPOESS-2, NPOESS-3, NPOESS-4, NPOESS-5, NPOESS-6 | TBD | Data collection | Satellite and ground based system to detect and locate aviators, mariners, and land-based users in distress. | Waveband: UHF 406.0 MHZ |
| S-band SAR S-band Synthetic Aperture Radar CAST | HJ-1C | Being developed | Imaging microwave radars | All weather microwave 3-D images. | Waveband: Spatial resolution: 20m (4looks) Swath width: 100km Accuracy: 3dB |
| SBUV/2 Solar Backscattter Ultra-Violet Instrument/2 NOAA | NOAA-14, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Operational | Atmospheric chemistry | Provides data on trace gases including vertical profile ozone, and solar irradiance and total ozone concentration measurements | Waveband: UV: 0.16-0.4µm (12 channels) Spatial resolution: 170km Swath width: Accuracy: Absolute accuracy: 1% |
| ScaRaB Scanner for Earth's Radiation Budget CNES (NPO "PLANETA") | MEGHA-TROPIQUES | Operational | Earth radiation budget radiometer | Measures top-of-atmosphere shortwave radiation (0.2-4.0µm) and total radiation (0.2-50µm). Two additional narrow-band channels (0.5-0.7µm and 11-12µm) allow cloud detection and scene identification | Waveband: VIS window channel: 0.5-0.7µm, Solar channel UV-SWIR: 0.2-4µm, Total channel UV-FIR: 0.2-50µm, Thermal window channel: 10.5-12.5µm Spatial resolution: 60km Swath width: 2200km Accuracy: Absolute: ± 2.5W/m2/sr, Relative: ± 0.7W/m2/sr |
| Scatterometer (ISRO) ISRO | OCEANSAT-2 | TBD | Scatterometers | Mainly for wind measurements | Under definition. |
| Scatterometer (JAXA) Scatterometer JAXA | GCOM-W | TBD | Scatterometers | Ocean surface wind measurements | Under definition. |
| SCIAMACHY Scanning Imaging Absorption Spectrometer for Atmospheric Chartography ESA | Envisat | Operational | Atmospheric chemistry | Measures middle atmosphere temperature. Provides tropospheric and stratospheric profiles of O2, O3, O4, CO, N2O, NO2, CO2, CH4, H2O, and tropospheric and stratospheric profiles of aerosols and cloud altitude | Waveband: UV-SWIR: 240-314, 309-3405, 394-620, 604-805, 785-1050, 1000-1750, 1940-2040 and 2265-2380nm Spatial resolution: Limb vertical 3 x 132km, Nadir horizontal 32 x 215km Swath width: Limb and nadir mode: 1000km (max) Accuracy: Radiometric: <4% |
| SeaWinds NASA (JAXA) | QuikSCAT | Operational | Scatterometers | Measurement of surface wind speed and direction; lost power on-orbit in October 2003 | Waveband: Microwave: 13.402 GHz Spatial resolution: 25 km Swath width: 1600 km Accuracy: Speed: 2-3.5 m/s Direction: 20 deg |
| SEM (GOES) Space Environment Monitor NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Operational | Space Environment | Used for equipment failure analysis, solar flux measurement, solar storm warning, and magnetic and electric field measurement at satellite | The SEM System consists of a three-axis vector magnetometer, an Energetic Particle Sensor (EPS) and associated High-Energy Proton and Alpha Detector (HEPAD), and an X-Ray Sensor (XRS). This set of instruments is designed to provide real-time measurement of solar activity, the charged particle environment, and the Earth's magnetic field at synchronous orbit. |
| SEM (POES) Space Environment Monitor NOAA | METOP-2, NOAA-12, NOAA-14, NOAA-15, NOAA-16, NOAA-17, NOAA-N, NOAA-N' | Operational | Space Environment | Used for equipment failure analysis, solar flux measurement, solar storm warning, and magnetic and electric field measurement at satellite | The SEM consists of two separate sensor units: the Total Energy Detector (TED) and the Medium Energy Proton and Electron Detector (MEPED). The TED senses and quantifies the intensity in the sequentially selected energy bands. The particles of interest have energies ranging from 0.05 keV to 20 keV. The MEPED senses protons, electrons, and ions with energies from 30 keV to levels exceeding 6.9 MeV. |
| SESS Space Environmental Sensor Suite NOAA | NPOESS-2, NPOESS-3, NPOESS-4, NPOESS-5, NPOESS-6 | Being developed | Space environment & Magnetic field | Measures characteristics of auroral boundary, auroral energy deposition, auroral imagery, electric field, electron density profile, geomagnetic field, in-situ plasma fluctuations, ionosphere scintillation. Data aids future space system design. | Multiple sensors to measure auroral characteristics, geomagnetic field, electron density profile, and total electron content, 10-km vertical resolution from 60 km to 3000 km. |
| SEVIRI Spinning Enhanced Visible and Infra-Red Imager EUMETSAT (ESA) | METEOSAT-8, METEOSAT-9, METEOSAT-10, METEOSAT-11 | Prototype | Imaging multi-spectral radiometers (vis/IR) | Measurements of cloud cover, cloud top height, precipitation, cloud motion, vegetation, radiation fluxes, convection, air mass analysis, cirrus cloud discrimination, tropopause monitoring, stability monitoring, total ozone and sea surface temparature | Waveband: VIS: 0.56-0.71µm, 0.5-0.9µm (broadband), NIR: 0.74-0.88µm, SWIR 1.5-1.78µm, SWIR: 3.48-4.36µm, TIR: 5.35-7.15µm, 6.85-7.85µm, 8.3-9.1µm, 9.38-9.94µm, 9.8-11.8µm, 11-13µm, 12.4-14.46µm Spatial resolution: 1km (at SSP) for one broadband visible channel HRV, 5km (at SSP) for all other channels Swath width: Full Earth disk Accuracy: Cloud cover: 10%, Cloud top height: 1km, Cloud top temparature: 1K, Cloud type: 8 classes, Surface temparature: 0.7-2.0K, Specific humidity profile: 10%, Wind profile (horizontal component): 2-10m/s, Long wave Earth surface radiation: 5W/m2 |
| SFM-2 UV limb spectrometer ROSHYDROMET | METEOR-3M N1 | Operational | Atmospheric chemistry | Global ozone monitoring | Waveband: UV-VIS: 0.2-0.51µm (4 channels) Spatial resolution: Swath width: Accuracy: |
| SGPS Solar and Galactic Proton Sensor NOAA | GOES-R | Approved | Space Environment | Studies natural radiation hazard to humans at high altitudes and in space, as well as risk assessment and warning of episodes of surface charging, deep dielectric charging, and single event upset of satellite systems. | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| SIM Spectral Irradiance Monitor NASA | SORCE | Operational | Earth radiation budget radiometer | Measures solar spectral irradiance in the 200-2000nm range. | Waveband: UV-SWIR: 200-2000nm Spatial resolution: Swath width: Accuracy: |
| SIRAL SAR Interferometer Radar Altimeter ESA | CRYOSAT | Being developed | Radar altimeters | Objective is to observe ice sheet interiors, the ice sheet margins, for sea ice and other topography. | Waveband: Microwave: 13.575GHz (Ku-Band) Spatial resolution: Range resolution 45cm, along-track resolution 250m Swath width: Footprint 15km Accuracy: Arctic sea-ice: 1.6cm/year for 300kmx300km cells, Land ice (small scale): 3.3cm/year for 100km x 100km cells, Land ice (large scale): 0.17cm/year for Antarctica size area |
| SKL-M Solar ray spectrometer ROSHYDROMET | Meteor-M No1, Meteor-M No2 | TBD | 0 | Proton flux density | Waveband: 2, 4, 6 and > 6 MeV, 30, 50, 100, 300 and > 300 MeV Spatial resolution: Swath width: Accuracy: |
| SMR Submillimetre Radiometer SNSB | Odin | Operational | Atmospheric chemistry instruments & Atmospheric temperature and humidity sounders | Measures global distributions of ozone and species of importance for ozone chemisty, ClO, HNO3, H2O, N2O, (HO2, H2O2). Measures temperature in the height range 15-100km. | Waveband: Microwave: 118.7GHz + 4 bands in the region 480-580GHz: Tunable measures 2-3 x 1GHz regions at a time Spatial resolution: Vertical resolution 1.5-3km, along track 600km Swath width: Altitudes of 5-100km Accuracy: 2-40% depending on species and altitude |
| SODAD Orbital System for an Active Detection of Debris CNES | SAC-D/Aquarius | Approved | TBD | Space Debris | Instrument for the measurement of the properties of micrometeorites and space debris. |
| SODISM SOlar Diameter Imager and Surface Mapper CNES | PICARD | TBD | Earth radiation budget radiometer | Measures diameter and differential rotation of the sun - a whole Sun imager | Waveband: UV: 230nm, VIS: 548nm, Active regions: 160nm plus Lyman alpha detector Spatial resolution: Swath width: Accuracy: |
| SOLSTICE SOLar STellar Irradiance Comparison Experiment NASA | SORCE, UARS | Operational | Earth radiation budget radiometer | Provides data on UV and charged particle energy inputs, and on time variation of full-disk solar UV spectrum. Measures solar UV radiation (115 to 430nm) with resolution of 0.12nm. Compares solar UV output with UV radiation of stable bright blue stars | Waveband: UV: 115-180nm & 170-320nm Spatial resolution: Swath width: Accuracy: 1% |
| Sounder NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Operational | Atmospheric temperature and humidity sounders | Provides atmospheric soundings and data on atmospheric stability and thermal gradient winds | Waveband: GOES 8-12; N,O,P: VIS-TIR: 19 channels Spatial resolution: 10km Swath width: Horizon to horizon Accuracy: |
| Sounder (INSAT) ISRO | INSAT-3D | TBD | Atmospheric temperature and humidity sounders | Atmospheric soundings, atmospheric stability, thermal gradient winds | Waveband: SWIR: 3.74-4.74µm, MWIR: 6.51-11.03µm, TIR: 12.02-14.71µm, VIS: 0.55-0.75µm Spatial resolution: 10x10 km Swath width: Full (Full Earth disc sounding), Program (Options provided for for Sector Scans) Accuracy: |
| SOVAP SOlar Variability Picard radiometer CNES | PICARD | Being developed | Earth radiation budget radiometer | Total solar irradiance measurements | Waveband: Total irradiance Spatial resolution: Swath width: Accuracy: |
| SPECTRA Surface Processes and Ecosystem Changes Through Response Analysis ESA | ESA Future Missions | Prototype | Imaging multi-spectral radiometers (vis/IR) & Multiple direction/polarisation radiometers | Data for study of land surface processes | Waveband: VIS-SWIR: 450-2350 nm and TIR: 10.3-12.3 micron Spatial resolution: Spatial sampling interval approx 50m, along track pointing ±30 deg Swath width: 50km Accuracy: |
| SSB/X-2 Special Sensor Gamma Ray Particle Detector NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16 | Operational | Space Environment | Detects the location, intensity, and spectrum of X-rays emitted from the Earth's atmosphere | Array-based system |
| SSIES-2 Special Sensor Ionospheric Plasma Drift/Scintillation Meter NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16 | Operational | Space Environment | Measurement of the ambient electron density and temperatures, the ambient ion density, and ion temperature and molecular weight | Consists of an electron sensor (Langmuir probe) and an ion sensor mounted on a 2.5 meter boom. The ion sensor is a planar aperture, planar collector sensor oriented to face the spacecraft velocity vector at all times. In addition to the Langmuir probe and planar collector, has a plasma drift meter and a scintillation meter. |
| SSIES-3 Special Sensor Ionospheric Plasma Drift/Scintillation Meter NOAA (US DoD) | DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19, DMSP F-20 | TBD | Space Environment | Measurement of the ambient electron density and temperatures, the ambient ion density, and ion temperature and molecular weight | Consists of an electron sensor (Langmuir probe) and an ion sensor mounted on a 2.5 meter boom. The ion sensor is a planar aperture, planar collector sensor oriented to face the spacecraft velocity vector at all times. In addition to the Langmuir probe and planar collector, has a plasma drift meter and a scintillation meter. |
| SSJ/4 Special Sensor Precipitating Plasma Monitor NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16 | Operational | Magnetic field | Measurement of transfer energy, mass, and momentum of charged particles through the magnetosphere-ionosphere in the Earth's magnetic field | Consists of four electrostatic analyzers that record electrons and ions between 30 eV and 30 KeV as they flow past the spacecraft toward the Earth. The instruments "look" toward the satellite zenith. |
| SSJ/5 Special Sensor Precipitating Plasma Monitor NOAA (US DoD) | DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19, DMSP F-20 | TBD | Magnetic field | Measurement of transfer energy, mass, and momentum of charged particles through the magnetosphere-ionosphere in the Earth's magnetic field | Consists of four electrostatic analyzers that record electrons and ions between 30 eV and 30 KeV as they flow past the spacecraft toward the Earth. The instruments "look" toward the satellite zenith. |
| SSM Special Sensor Magnetometer NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19, DMSP F-20 | Operational | Magnetic field | Measures geomagnetic fluctuations associated withMeasures geomagnetic fluctuations associated with solar geophysical phenomena. With SSIES and SSJ provides heating and electron density profiles in the ionosphere | A triaxial fluxgate magnetometer |
| SSM/I Special Sensor Microwave Imager NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16 | Operational | Imaging multi-spectral radiometers (passive microwave) | Measures atmospheric, ocean and terrain microwave brightness temperatures to provide: sea surface winds, rain rates, cloud water, precipitation, soil moisture, ice edge, ice age. | Waveband: Microwave: 19.35, 22.235, 37, 85 GHz Spatial resolution: 15.7km x 13.9km to 68.9 x 44.3km (depends on frequency) Swath width: 1400km Accuracy: |
| SSM/T-1 Special Sensor Microwave Temperature Sounder NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16, DMSP F-18, DMSP F-19, DMSP F-20 | Operational | Atmospheric temperature and humidity sounders | Measures Earth's surface and atmospheric emission in the 50-60GHz oxygen band | Waveband: Microwave: 7 channels in the 50-60GHz range Spatial resolution: 174km diameter beam Swath width: 1500km Accuracy: |
| SSM/T-2 Special Sensor Microwave Water Vapor Sounder NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16 | Operational | Atmospheric temperature and humidity sounders | Water Vapour profiler | Waveband: Microwave: 91.6, 150, 183.31 (3 channels) (Total 5 channels) Spatial resolution: approx 48km Swath width: 1500km Accuracy: |
| SSMIS Special Sensor Microwave Imager Sounder NOAA (US DoD) | DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19, DMSP F-20 | Operational | Atmospheric temperature and humidity sounders | Measures thermal microwave radiation. Global measurements of air temp profile, humidity profile, ocean surface winds, rain overland/ocean, ice concentration/age, ice/snow edge, water vapour/clouds over ocean, snow water content, land surface temperature. | Waveband: Microwave: 19 - 183GHz (24 frequencies) Spatial resolution: Varies with frequency: 25x17km to 70X42km Swath width: 1700km Accuracy: |
| SSU Stratospheric Sounding Unit NOAA | NOAA-12, NOAA-14 | Operational | Atmospheric temperature and humidity sounders | Provides temperature profiles in stratosphere, top-of-atmosphere radiation from 25km to 50km altitude | Waveband: 669.99, 669.63 and 669.36/cm (carbon dioxide) Spatial resolution: 147.3km at nadir Swath width: ±40 deg scan Accuracy: |
| SSULI Special Sensor Ultraviolet Limb Imager NOAA | DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19, DMSP F-20 | TBD | Space Environment | Measures vertical profiles of the natural airglow radiation from atoms, molecules and ions in the upper atmosphere and ionosphere | SSULI makes measurements from the extreme ultraviolet (EUV) to the far ultraviolet (FUV) (80nm-170nm with 1.5 nm resolution). Uses a spectrograph fed by a mirror capable of scanning below the satellite horizon from 10-27 deg, every 90 seconds (which gives a vertical slice of Earth's atmosphere from 750-50km in altitude). |
| SSUSI Special Sensor Ultraviolet Spectrographic Imager NOAA | DMSP F-16, DMSP F-17, DMSP F-18, DMSP F-19, DMSP F-20 | TBD | Space Environment | Monitors the composition and structure of the upper atmosphere and ionosphere, as well as auroral energetic particle inputs, with spectrographic imaging and photometry. | A scanning imaging spectrograph whose field-of-view is scanned from horizon to horizon and a nadir-looking photometer system. The SIS produces simultaneous multispectral images over the spectral range 115-180nm. |
| SSZ NOAA (US DoD) | DMSP F-13, DMSP F-15, DMSP F-16 | Operational | Space Environment | Laser threat detector | The SSZ is a static Earth viewing sensor, monitoring electro magnetic radiation |
| STR Star Tracker ESA | Swarm | Operational | Precision orbit | Precise satellite orbit and attitude determination | Waveband: N/A Spatial resolution: <1arcsec Swath width: N/A Accuracy: <0.7arcsec |
| SUSIM (UARS) Solar Ultraviolet Irradiance Monitor NASA | UARS | Operational | Earth radiation budget radiometer | Provides data on UV and charged particle energy inputs, and on time variation of full-disk solar UV spectrum | Waveband: UV: 0.12-0.4µm Spatial resolution: Not applicable Spectral resolution: 0.15nm Accuracy: 1% Swath width: Looks at sun |
| SXI Solar X-ray Imager NOAA (USAF) | GOES-12, GOES-N, GOES-P, GOES-R | Prototype | Space Environment | Obtains data on structure of solar corona. Full disk imagery also provides warnings of geomagnetic storms, solar flares, and information on active regions of sun and filaments | Waveband: GOES 12,N,P: X-Ray 0.6-6.0nm bandpass Spatial resolution: Swath width: FWHM of ~10 arcsec Accuracy: |
| SXS Solar X-Ray Sensor NOAA | GOES-R | Approved | Space Environment | Studies of natural radiation hazard to humans at high altitudes and in space, as well as risk assessment and warning of episodes of surface charging, deep dielectric charging, and single event upset of satellite systems. | The GOES-R Project is in the formulation phase. The satellite will comprise improved spacecraft and instrument technologies, which will result in more timely and accurate weather forecasts, and improve support for the detection and observations of meteorological phenomena that directly affect public safety, protection of property, and ultimately, economic health and development. |
| TerraSAR-X X-Band Synthetic Aperture Radar DLR | TerraSAR-X | Approved | Imaging microwave radars | High resolution images for monitoring of land surface and coastal processes and for agricultural, geological and hydrological applications | Waveband: 9.65GHz, 300MHz bandwidth, all 4 polarisation modes Spatial resolution: Spotlight: 1,2m x 1-4m Stripmap: 3m x 3-6m ScanSAR: 16m x 16m Swath width: Spotlight: 5-10km x 10 km, Stripmap: 30 km, ScanSAR: 100 km Accuracy: |
| TES Tropospheric Emission Spectrometer NASA | Aura | Operational | Atmospheric chemistry | 3-D profiles on a global scale of all infra-red active species from surface to lower stratosphere. Measures greenhouse gas concentrations, tropospheric ozone, acid rain precursors, gas exchange leading to stratospheric ozone depletion | Waveband: SWIR-TIR: 3.2-15.4µm Spatial resolution: In limb mode: 2.3km vertical resolution. In down-looking mode: 50km x 5km (global), 5km x 0.5km (local) Swath width: Limb mode: global: 50km x 180km, local: 5km x 18km Accuracy: Ozone: 20ppb, Trace gases: 3-500ppb |
| TIM Total Irradiance Monitor NASA | Glory, SORCE | Operational | Earth radiation budget radiometer | Measurement of total solar irradiance directly traceable to SI units with an absolute accuracy of 0.03% abd relative accuracy of 0.001% per year | Waveband: Spatial resolution: Swath width: Looks at the sun every orbit, providing 15 measurements per day Accuracy: |
| TIS (CONAE) Thermal IR Scanner CONAE | SAC-F | Approved | Imaging multi-spectral radiometers (vis/IR) |  | Data not available |
| TM Thematic Mapper USGS | Landsat-5 | Operational | Imaging multi-spectral radiometers (vis/IR) | Measures surface radiance and emittance, lands cover state and change (eg vegetation type). Used as multipurpose imagery for land applications | Waveband: 0.45-12.50µm Spatial resolution: VIS-SWIR, 30m; TIR: 120m Swath width: 185km Accuracy: |
| TMR TOPEX Microwave Radiometer NASA | Topex-Poseidon | Operational | Imaging multi-spectral radiometers (passive microwave) | Provides altimeter data to correct for errors caused by water vapour and cloud-cover. Also measures total water vapour and brightness temperature | Waveband: Microwave: 18GHz, 21GHz, 37GHz Spatial resolution: 44.7km at 18GHz, 37.4km at 21GHz, 23.6km at 37GHz Swath width: 120 deg cone centred on nadir Accuracy: Total water vapour: 0.2g/sq cm, Brightness temperature: 0.3 K |
| TOM Total Ozone Mapper NRSCC (CAST) | FY-3A, FY-3B, FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Being developed | Atmospheric chemistry | Ozone chemistry measurements | Waveband: UV Spatial resolution: 50km Swath width: Accuracy: |
| TOPEX TOPEX NASA Radar Altimeter NASA | Topex-Poseidon | Operational | Radar altimeters | Measurement of global ocean surface topography | Waveband: Microwave: 126 GHz and 5.3 GHz Spatial resolution: Swath width: 6km Accuracy: 2.4cm |
| TOPSAT telescope BNSC | TopSat | Prototype | High resolution optical imagers | Experimental medium-resolution imaging satellite supporting a range of possible land applications. | Waveband: Panchromatic VIS: 0.5-0.75µm. 3-band multi-spectral. Spatial resolution: 2.5m pan. 5m multi-spectral. Swath width: 10km-MS, 15km-Pan Accuracy: |
| TRSR Turbo-Rogue Space Receiver NASA | Jason, Jason-2 (also known as OSTM) | TBD | Precision orbit & Atmospheric temperature and humidity sounders | Provides precise continuous tracking data of satellite to decimeter accuracy | Waveband: L-band:1228 and 1575MHz Spatial resolution: Not applicable Swath width: Not applicable Accuracy: |
| TSIS Total Solar Irradiance Sensor NOAA | NPOESS-3, NPOESS-6 | Being developed | Earth radiation budget radiometer | 0.2- 2 micron solar spectral irradiance monitor | Waveband: UV-SWIR: 0.2-2µm Spatial resolution: Swath width: Accuracy: 1.5w/m2 |
| Variant ROSKOSMOS | SICH-1M |  | Magnetic field | Studies of the ionosphere | Payload package which includes: an electric probe, a wave probe, a Rogovsky coil, a Faraday cup, a fluxgate magnetometer, and a data acquisition unit. |
| VEGETATION CNES (EEC) | SPOT-4, SPOT-5 | Operational | Imaging multi-spectral radiometers (vis/IR) | Data of use for crop forecast and monitoring, vegetation monitoring, and biosphere/ geosphere interaction studies | Waveband: Operational mode: VIS: 0.61-0.68µm, NIR: 0.78-0.89µm, SWIR: 1.58-1.75µm, Experimental mode: VIS: 0.43-0.47µm Spatial resolution: 1.15km at nadir - minimal variation for off-nadir viewing Swath width: 2200km Accuracy: |
| VFM Vector Magnetometer ESA | Swarm | Operational | Magnetic field | The VFM is the prime instrument of the Swarm mission. It will provide ultra linear and low-noise measurements of the Earth's magnetic field vector components. | Waveband: N/A Spatial resolution: <0.1nT Swath width: N/A Accuracy: <0.5nT/15days |
| VHRR Very High Resolution Radiometer ISRO | INSAT-2E, INSAT-3A, KALAPANA | Operational | Imaging multi-spectral radiometers (vis/IR) | Cloud cover, rainfall, wind velocity, sea surface temperature, outgoing longwave radiation, reflected solar radiation in spectral band 0.55-0.75µm, emitted radiation in 10.5-12.5µm range | Waveband: VIS: 0.55-0.75µm, NIR: 5.7-7.1µm, TIR: 10.5-12.5µm Spatial resolution: 2km in visible, 8km in IR Swath width: Full Earth disk every 30 minutes Accuracy: |
| VIIRS Visible/Infrared Imager Radiometer Suite NOAA (NASA) | NPOESS-1, NPOESS-2, NPOESS-3, NPOESS-4, NPOESS-5, NPOESS-6, NPP | Approved | Imaging multi-spectral radiometers (vis/IR) | Global observations of land, ocean, and atmosphere parameters: cloud/weather imagery, sea-surface temperature, ocean colour, land surface vegetation indices | Waveband: VIS - TIR: 0.4-12.5µm (22 channels) Spatial resolution: 400m-1.6km Swath width: 3000km Accuracy: SST 0.35K |
| VIRR Multispectral Visible and Infra-red Scan Radiometer (10 channels) NRSCC (CAST) | FY-3A, FY-3B, FY-3C, FY-3D, FY-3E, FY-3F, FY-3G | Being developed | Imaging multi-spectral radiometers (vis/IR) | Multispectral Visible and Infra-red Scan Radiometer | Waveband: Spatial resolution: 1.1km Swath width: 3200km Accuracy: |
| VISSR (GMS-5) Visible and Infra-red Spin Scan Radiometer (GMS-5) JAXA (JMA) | GMS-5 | Operational | Imaging multi-spectral radiometers (vis/IR) | Data used for cloud type and motion detection wind. Also measures sea surface temperature and atmospheric water vapour | Waveband: VIS: 0.55-0.9µm, TIR: 6.5-7, 10.5-11.5, 11.5-12.5µm Spatial resolution: Visible: 1.25km, TIR: 5km Swath width: Full Earth disk in all channels, every 1 hour Accuracy: |
| WAOSS-B Wide-Angle Optoelectronic Stereo Scanner DLR | BIRD | Operational | Imaging multi-spectral radiometers (vis/IR) | Vegetation and Cloud coverage | Waveband: VIS: 600-670nm, NIR: 840-900nm Spatial resolution: 185m Swath width: 533km Accuracy: |
| WEFAX Weather Facsimile NOAA | GOES-9, GOES-10, GOES-11, GOES-12, GOES-N, GOES-O, GOES-P, GOES-R | Operational | Communications | Weather Facsimile | Data communications |
| WFC Wide Field Camera NASA | CALIPSO | Approved | Imaging multi-spectral radiometers (vis/IR) | Acquires high spatial resolution imagery for meteorological context | Waveband: VIS: 620 to 670 nm Spatial resolution: 125m Swath width: 60km Accuracy: |
| WFI Wide Field Imager CAST (INPE) | CBERS-2, CBERS-2B | Operational | Imaging multi-spectral radiometers (vis/IR) | Earth resources, environmental monitoring, land use | Waveband: VIS: 0.63-0.69µm, NIR: 0.77-0.89µm Spatial resolution: 258m Swath width: 890km Accuracy: 0.3pixels |
| WFI-2 Wide Field Imager 2 CAST (INPE) | CBERS-3, CBERS-4 | Operational | Imaging multi-spectral radiometers (vis/IR) | Earth resources, environmental monitoring, land use | Waveband: VIS: 0.45-0.52, 0.52-0.59, 0.63-0.69, 0.77-0.89µm Spatial resolution: 73m Swath width: Accuracy: |
| WiFS Wide Field Sensor ISRO | IRS-P4 | Operational | Imaging multi-spectral radiometers (vis/IR) | Vegetation monitoring, environmental monitoring, drought monitoring, snow melt run-off forecasting, global green cover assessment, agro-climatic regional planning. | Waveband: VIS: 0.62-0.68µm NIR: 0.77-0.86µm SWIR: 1.55-1.7µm (IRS P3 only) Spatial resolution: 188m Swath width: 810km Accuracy: |
| WINDII CNES (NASA) | UARS | Not operational | Atmospheric chemistry | Day and night wind measurements between 80km and 300km altitude. Measures atmospheric temperature and concentration of emitting species. WINDII is no longer operational on UARS. | Waveband: Visible-NIR:0.55-0.78µm Spatial resolution: Vertical: 2km Horizontal: 25km Swath width: 70-310km Accuracy: Wind speed: 10m/s |
| WTE Whale Tracker Experiment CONAE | SAC-C | TBD | Data collection | Environmental data collection system | Data communication |
| XPS XUV Photometer System NASA | SORCE | Operational | Other | Objective is to measure the extreme UV solar irradiance from 1-35nm | Waveband: UV: 1-35nm Spatial resolution: Swath width: Accuracy: |